## Slide 1: JCTVC-K0138 Non-CE1: Deblocking of Large Block Artifacts
Geert Van der Auwera, Rajan Joshi, Marta Karczewicz

## Slide 2: CE1
Intra prediction modification:
  Restriction on max transform block size for boundary filtering of DC, horizontal and vertical intra modes
Following modifications to the deblocking filter are considered in CE1:
  Strong/weak filter decision
    Removal of slope restriction condition
    Addition of second activity condition
    Increase of edge discontinuity threshold from 2.5tC to 16tC
  Strong filter coefficients for p1, q1, p2, q2 samples
  Strong filter clipping for p0, q0, p1, q1, p2, q2
  Beta threshold curve for QP > 41
  Boundary strength increase: alternatives studied
    32x32 block edges
    Max TB/TU edges
    tC default offset increase from 2 to 3 for Bs = 2
At DIS stage, minimal changes to deblocking filter are preferred

## Slide 3: Proposal Summary
Problem: edge discontinuities not smoothed due to narrow clipping of normal filter
Proposal: If edge is maximum transform edge, then boundary strength (Bs) value is set to 3 and wider normal filter clipping interval is chosen (see changes in blue below)
HM8 “normal” filter:
   = ( 9(q0-p0) - 3(q1-p1) + 8 )/16
  If (  < 10tc )
    δ = Clip3( -c1, c1, )
    p0’ = Clip( p0 + δ )
    q0’ = Clip( q0 - δ )
    If modify p1:
      p = Clip3( -c2, c2, ( (p2 + p0 + 1)/2 - p1 + δ)/2 )
      p1’ = Clip( p1 + p )
    If modify q1:
      q = Clip3( -c2, c2, ( (q2 + q0 + 1)/2 - q1 - δ)/2 )
      q1’ = Clip( q1 + q )
    Filter clipping thresholds
      c1 = tC and c2 = tC / 2
      If ( Bs = 3 ), then c1 = 4tC and c2 = 2tC
Proposal:
Sharp edge discontinuity is smoothed
HM8:
Sharp edge discontinuity remains after filtering

## Slide 4: Subjective quality Examples Max transform = 32x32

## Slide 5
HM8.0: “Riverbed” (LD-B, QP32, max TB=32x32, frame #2)

## Slide 6
Proposal: “Riverbed” (LD-B, QP32, max TB=32x32, frame #2)

## Slide 7
HM8.0: “Riverbed” (LD-B, QP37, max TB=32x32, frame #2)

## Slide 8
Proposal: “Riverbed” (LD-B, QP37, max TB=32x32, frame #2)

## Slide 9
HM8.0: “Red Kayak” (LD-B, QP37, max TB=32x32, frame #7)

## Slide 10
Proposal: “Red Kayak” (LD-B, QP37, max TB=32x32, frame #7)

## Slide 11
HM8.0: “Ducks Take Off” (LD-B, QP32, max TB=32x32, frame #7)

## Slide 12
Proposal: “Ducks Take Off” (LD-B, QP32, max TB=32x32, frame #7)

## Slide 13
HM8.0: “Ducks Take Off” (LD-B, QP37, max TB=32x32, frame #7)

## Slide 14
Proposal: “Ducks Take Off” (LD-B, QP37, max TB=32x32, frame #7)

## Slide 15
HM8.0: “West Wind Easy” (LD-B, QP32, max TB=32x32, frame #6)

## Slide 16
Proposal: “West Wind Easy” (LD-B, QP32, max TB=32x32, frame #6)

## Slide 17
HM8.0: “Kimono” (LD-B, QP32, max TB=32x32, frame #240)

## Slide 18
Proposal: “Kimono” (LD-B, QP32, max TB=32x32, frame #240)
Improved texture detail in roof region

## Slide 19
HM8.0: “Kimono” (LD-B, QP32, max TB=32x32, frame #137)

## Slide 20
Proposal: “Kimono” (LD-B, QP32, max TB=32x32, frame #137)
Improved texture detail in face region

## Slide 21: Subjective quality Examples Max transform = 16x16

## Slide 22
HM8.0: “Riverbed” (LD-B, QP32, max TB=16x16, frame #2)

## Slide 23
Proposal: “Riverbed” (LD-B, QP32, max TB=16x16, frame #2)

## Slide 24
HM8.0: “Ducks Take Off” (LD-B, QP37, max TB=16x16, frame #199)

## Slide 25
Proposal: “Ducks Take Off” (LD-B, QP37, max TB=16x16, frame #199)

## Slide 26: Objective Results
CTC

## Slide 27: Conclusion
Minor modification of HEVC DIS deblocking filter:
  Adjusted normal filter clipping for max transform edges
Inclusion of intra prediction modification from CE1:
  Restrict boundary filtering to 4x4, 8x8, and 16x16
Advantages:
  Preserves HM8 deblocking filter decision conditions and filters
  No signalling of deblocking adjustment parameters required
  Significant reduction of large block artifacts without oversmoothing
  Improved subjective quality by additional texture sharpness is observed