## Slide 1: JCTVC-K0140 AHG9: Simple HEVC stream editing
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
11th JCT-VC meeting, Shanghai CN, 10-19 Oct. 2012

## Slide 2: Summary
Purpose
  Simple HEVC bitstream editing
Proposals
  Modifier of cpb_removal_delay and dpb_output_delay for removal of leading picture
  Relaxation of constrain imposed when fixed_pic_rate_flag is equal to 1
  SEI for indicating editing point in a bitstream

## Slide 3: Proposal 1 Modifier of cpb_removal_delay and dpb_output_delay

## Slide 4: Motivation
Generally a non-decodable leading picture is removed from a bitstream in the editing process.
CRD (cpb_removal_delay) and DOP (dpb_output_delay) of all pictures following a BLA picture need adjusted.
  Edited bitstream has to conform to the specification in Annex C.
Complexity reduction is needed for editing applications.

## Slide 5: Proposal in JCTVC-J0137
Two parameters were proposed in BP (Buffering period) SEI.
  alt_cpb_removal_delay_offset and alt_dpb_output_delay
  Similar concept to initial_alt_cpb_removal_delay(_offset)
It is not applicable when TFD (Tagged for discard) pictures and DLP (Decodable leading picture) pictures are interleaved.

## Slide 6: Proposal (Variation 1)
pic_timing( payloadSize ) { | Descriptor
if( CpbDpbDelaysPresentFlag ) { | 
num_removed_tfds | u(8)
cpb_removal_delay | u(v)
…. | 
CRD’ = CRD – (NRTBLA – NRT)
DOD’ = DOD – NRT
NRT: num_removed_tfds

## Slide 7: Proposal (Variation 2)
buffering_period( payloadSize ) { | Descriptor
….. | 
if ( NalHrdBpPresentFlag ¦¦ VclHrdBpPresentFlag ) | 
{ | 
ptsei_overwrite_flag | u(1)
if ( ptsei_overwrite_flag ) | 
num_entries_minus1 | ue(v)
for ( i = 0; i <= num_entries_minus1+1; i ++ ) { | 
alt_cpb_removal_delay_offset[ i ] | ue(v)
alt_dpb_output_delay_offset[ i ] | 
} | 
} | 
} | 
} | 

## Slide 8: Proposal 2 Relaxation of constraint related to fixed_pic_rate_flag

## Slide 9: Motivation
Constraint related to fixed_pic_rate_flag equal to 1 to,dpb( n ) = to,dpb( nn ) − to,dpb( n ) = tc * ( pic_duration_in_tcs_minus1[ i ] + 1 )
This constraint is not fulfilled when two bitstreams with different value of sps_max_num_reorder_pics are connected.

## Slide 10: Proposal
Constraint of to,dpb( n ) is not applied at a sequence boundary.
Semantics of fixed_pic_rate_flag is changed as follows;
fixed_pic_rate_flag[ i ] equal to 1 indicates that, ….
When HighestTid is equal to i and, fixed_pic_rate_flag[ i ] is equal to 1 for a coded video sequence containing picture n and picture n in a coded video sequence is not the last picture of the coded video sequence in output order, the value computed for to,dpb( n ) as specified in Equation C‑17 shall be equal to tc * ( pic_duration_in_tcs_minus1[ i ] + 1 ), wherein tc is as specified in Equation C‑1 (using the value of tc for the coded video sequence containing picture n) when one or more of the following conditions are true for the following picture nn that is specified for use in Equation C‑17:
…

## Slide 11: Proposal 3 SEI message for indicating editing point

## Slide 12: Motivation
Concatenation of bitstream BSA and BSB
When BSA is cut at a wrong position, constraint of to,dpb( n ) is not satisfied.
It is a burden to the editing process to know where is the right position.

## Slide 13: Example

## Slide 14: Proposal
SEI message which indicates the right position.
editing_point( payloadSize ) { | Descriptor
if( NalHrBpPresentFlag ¦¦ VclHrdBpPresentFlag ) | 
cpb_status_present_flag | u(1)
if( cpb_status_present_flag ) { | 
if( NalHrdBpPresentFlag ) { | 
for( SchedSelIdx = 0; SchedSelIdx <= cpb_cnt_minus1; SchedSelIdx++ ) { | 
cpb_offset[ SchedSelIdx ] | u(v)
} | 
} | 
if( VclHrdBpPresentFlag ) { | 
for( SchedSelIdx = 0; SchedSelIdx <= cpb_cnt_minus1; SchedSelIdx++ ) { | 
cpb_offset[ SchedSelIdx ] | u(v)
} | 
} | 
} | 
} | 

## Slide 15: Proposal (cont.)
Constraint on editing point SEI message
  When an access unit is associated with an editing point SEI message, the output timing of the access unit shall not be earlier than any access units preceding the access unit.
cpb_offset
  Additional parameter whose occurrence is controlled by cpb_status_present_flag
  CPB position of the last access unit
  Used in determining cpb_removal_delay of BLA picture in order to conform to the specification in Annex C.