## Slide 1: JCTVC-K0141 AHG9: Low delay display hint SEI
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
11th JCT-VC meeting, Shanghai CN, 10-19 Oct. 2012

## Slide 2: Summary
Purpose
  Ultra-low delay end-to-end transmission
Proposal
  SEI message which assists a decoder in determining the possible earliest V-sync timing for outputting decoded pictures
  Follow-up proposal of JCTVC-J0136

## Slide 3: Motivation
Minimizing display delay, as well as decoding delay
When the timings of line decoding and line outputting are aligned, display delay becomes minimum.
Decoder timing model
V-sync(A) defines when each line is ready for outputting

## Slide 4: Alignment of V-sync timing

## Slide 5: Problem
It is not easy to determine the proper value of Δt since it is highly dependent to the DU structure.

## Slide 6: Proposal: low delay display hint SEI
low_delay_display_hint( payloadSize ) { | Descriptor
display_delay_hint | u(v)
decoding_delay_hint_present_flag | u(1)
if (decoding_delay_hint_present_flag ) | 
decoding_delay_hint | u(v)
} | 
display_delay_hint for signalling Δt
  In units of 90KHz
  Assumption of raster-scan display, constant DU decoding interval
Optional decoding_delay_hint
  In units of 90KHz
  Indicates the possible earliest time when a decoder can start the decoding process of access units in the bitstream without causing an underflow or an overflow of the CPB, assuming that the decoder decodes one access unit in one picture period.