## Slide 1: JCTVC-K0143 On handling of minimum POC range at decoder
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
11th JCT-VC meeting, Shanghai CN, 10-19 Oct. 2012

## Slide 2: Overview
Background
  The range of POC (picture order count)
  9th JCT-VC meeting: extended from 32-bit to 64-bit
    Maximum interval of IDR is 4.9*109 years.
  10th JCT-VC meeting: reverted to 32-bit with the following note
    If adequate text is provided to describe how a decoder can handle POC without having such a range limit, we can review the description of that scheme and consider including it in the standard and removing (or increasing) the 32 bit range limit. That aspect is for further study.
Proposals
  Text
  64-bit POC range

## Slide 3: Proposed text
NOTE 4 – The range limitation on the difference of two POC values referred in the decoding process of any access unit enables a decoder to handle PicOrderCntVal with the range limit smaller than [-263, 263 - 1], since only the relative value of POC is used in the decoding process.
The minimum range limit of the difference of two stored POC values needed for yielding the same result as in [-263, 263 - 1] range limit is [-224, 216 - 1] (i.e. 25-bit range).
In order to implement such smaller range limit, a signed x-bit (x = [25, 64]) register, in which a negative value is represented in 2's complement, is typically used to store LSB x-bit of each variable relating to a POC value (such as PicOrderCntVal and PicOrderCntMsb).
Addition, subtraction and comparison of two POC-related variables stored in signed x-bit registers are also performed in x-bit range, without using a carry bit or a borrow bit.
As the result, PicOrderCntVal is seen as the variable whose range limit is [-2x-1, 2x-1 - 1] and whose value is cyclic.