## Slide 1
JCTVC-K0144
Reduced worst-case memory bandwidth for SCU size larger than 8x8
11th JCT-VC meeting, Oct 2012.

## Slide 2: Problem
A check in the binarisation of part_mode treats SCU=8x8 case differently to SCU>8x8:
  Reaches PART_NxN mode in inter-prediction, which has implications for memory bandwidth.

## Slide 3: Solution
Remove PART_NxN from inter-prediction:
  Removes a check and hence the rightmost column from the part_mode binarisation table.
  Simplifies the WD text.
  Also, removes the only inter partition mode with 4 partitions (all others have 1 or 2).

## Slide 4: Consequences
No coding efficiency impact under common test conditions
Implications for worst case memory bandwidth reduction:
  If memory bandwidth at higher levels is not an issue, setting SCU=8x8 gives maximum flexibility in CU/PU structures.
  If memory bandwidth at higher levels is an issue, a normative restriction that SCU>8x8 may be applied to reduce worst-case memory bandwidth.

## Slide 5: Additional step
Presently 4x8 and 8x4 PUs are restricted to uni-pred.
Generalise this restriction to PART_Nx2N and PART_2NxN when CU size == SCU size.
  Limits MV line buffer to 2 MVs per SCU.
  If an SCU>8x8 constraint were placed on higher levels, would reduce memory buffering requirement.

## Slide 6: Results
SCU=16x16, PART_NxN removed from inter-prediction
  (Nebuta, SteamLocomotive show 0.0% to 0.4% luma degradation)

## Slide 7: Additional results
SCU=16x16, added PART_Nx2N and PART_2NxN restriction to uni-pred when CU size is equal to SCU size.

## Slide 8: Information
SCU=16x16 compared with SCU=8x8.