## Slide 1
Cheung Auyeung
Sony Electronics Inc
October 10, 2012
GOP Structures for Interlaced Video
Notes: 1

## Slide 2: Coding of Field Structure Pictures by HEVC
This contribution proposes more robust group of picture (GOP) structures for field structure coding than the HM8 CTC GOP structure.
  When frame structure coding is better,
    reduce the difference in coding efficiency gap between field structure coding and frame structure coding.
  When field structure coding is better,
    maintain the improvements of field structure coding over frame structure coding.
Extended HM8 memory allocation to support longer GOP structures.
  No other changes to HM8.
No changes to WD8.

## Slide 3: HM8 GOP Structure for Field Picture Coding
In HM8 CTC random access configurations, all pictures can only predict from pictures with even picture order count (POC).
In HM8 CTC low delay configurations, all odd POC pictures can only predict from pictures with even POC.
Since the HM8 CTC configurations does not use odd POC reference picture as much as even POC reference pictures, picture quality is suffered for slow motion and high texture interlace videos such as the MPEG2 “mobile and calendar” test sequence.

## Slide 4: CTC RA GOP Structure & Schedule
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
0 |  | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  | 4 |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 6 |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  | 5 |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  | 7 |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16
10 |  |  |  |  |  |  |  |  |  |  |  |  |  | 12 |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  |  | 10 |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  | 9 |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  |  |  |  |  | 11 |  |  |  |  | 
14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 14 |  | 
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 13 |  |  | 
16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 15 | 
Encoding Order
POC
Second GOP
Third GOP
is general
First GOP has only one picture
In random access (RA) CTC,
GOP size is 8
Example:
  At encoding order 2, POC 4 is encoded. It has POC 0 and POC 8 as reference picture.
  At encoding order 3, POC 2 is encoded. It has POC 0 and POC 4 as reference picture.
Pictures with odd POC are not reference pictures.
Ref Picture
Current Picture
Each vertical yellow bar shows the lifetime of a reference picture in the reference list.
It must be one continuous bar.

## Slide 5: Proposed RA Field GOP Structure
In the proposed RA GOP structure for field picture coding,
GOP size is 16
The nearest two pictures before the current picture, if available, consist of an even POC picture and an odd POC picture.
The nearest two pictures after the current picture, if available, consist of an even POC picture and an odd POC picture.
Encoding Order
POC
2nd GOP
3rd GOP
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
0 |  | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  |  |  | 9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  | 6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  | 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  |  |  |  |  | 11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  |  |  |  | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
17 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 17 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32
19 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 25 |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 24 |  |  |  |  |  |  |  | 
21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 21 |  |  |  |  |  |  |  |  |  |  | 
22 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 20 |  |  |  |  |  |  |  |  |  |  |  | 
23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 19 |  |  |  |  |  |  |  |  |  |  |  |  | 
24 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 18 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 23 |  |  |  |  |  |  |  |  | 
26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 22 |  |  |  |  |  |  |  |  |  | 
27 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 29 |  |  | 
28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 28 |  |  |  | 
29 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 27 |  |  |  |  | 
30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 26 |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 31 | 
32 |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 30 |  | 

## Slide 6: CTC LD GOP Structure & Schedule
Encoding Order
POC
First GOP has only one picture
In low delay (LD) CTC,
GOP size is 4
Example:
  At encoding order 2, POC 2 is encoded. It has POC 0 and POC 1 as reference picture.
  At encoding order 3, POC 3 is encoded. It has POC 0 and POC 2 as reference picture.
Pictures with odd POC are not reference pictures of odd POC pictures.
Ref Picture
Current Picture
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
0 |  | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  | 4 |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 5 |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 6 |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  |  | 7 |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  | 9 |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  |  | 10 |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  |  |  | 11 |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  | 12 |  |  |  | 
13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 13 |  |  | 
14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 14 |  | 
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 15 | 
16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16
2nd GOP
3rd GOP
4th GOP
5th GOP
5th GOP is general. It is used to define the low delay configuration files.

## Slide 7: Proposed Low Delay GOP Structure
Encoding Order
POC
2nd GOP
3rd GOP
4th GOP
5th GOP
5th GOP is general. It is used to define the low delay configuration files.
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
0 |  | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  |  | 7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  | 9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  |  | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  |  |  | 11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  | 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
17 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 17 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 18 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
19 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 19 |  |  |  |  |  |  |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 20 |  |  |  |  |  |  |  |  |  |  |  | 
21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 21 |  |  |  |  |  |  |  |  |  |  | 
22 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 22 |  |  |  |  |  |  |  |  |  | 
23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 23 |  |  |  |  |  |  |  |  | 
24 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 24 |  |  |  |  |  |  |  | 
25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 25 |  |  |  |  |  |  | 
26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 26 |  |  |  |  |  | 
27 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 27 |  |  |  |  | 
28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 28 |  |  |  | 
29 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 29 |  |  | 
30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 30 |  | 
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 31 | 
32 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 32

## Slide 8: Tested RA GOP Structures
Test sequences
  Nine MPEG2 480i 30fps test sequences
  Each sequence is 150 frames except car, which is 140 frames.
Anchor (Frame-GOP-CTC)
  CTC RA configuration with frame structured pictures.
  GOP size is 8.
Field-GOP-CTC
  CTC RA configuration with field structured pictures.
  GOP size is 8.
Field-GOP-New
  Proposed RA configuration with field structured pictures.
  GOP size is 16.
RA results are cross-checked by
  Motorola, JCTVC-K0317
  Thank you very much.

## Slide 9: Results of RA GOP Structures
 | RA-Main |  |  |  |  |  |  | RA-HE10 |  |  |  |  | 
 | Field-GOP-CTC |  |  | Field-GOP-New |  |  |  | Field-GOP-CTC |  |  | Field-GOP-New |  | 
 | BD-rate (piecewise cubic) |  |  | BD-rate (piecewise cubic) |  |  |  | BD-rate (piecewise cubic) |  |  | BD-rate (piecewise cubic) |  | 
 | Y | U | V | Y | U | V |  | Y | U | V | Y | U | V
ballet | -44.9% | -21.5% | -29.6% | -44.6% | -30.8% | -34.2% |  | -45.1% | -22.2% | -29.3% | -45.0% | -32.1% | -34.6%
bicycle | -24.8% | -30.0% | -19.2% | -23.6% | -27.2% | -20.8% |  | -24.9% | -29.6% | -18.4% | -23.6% | -27.3% | -20.7%
bus | -24.1% | -23.5% | -11.2% | -29.5% | -35.4% | -26.5% |  | -24.3% | -23.7% | -9.7% | -29.6% | -36.0% | -26.7%
car | -31.9% | -14.0% | -16.3% | -33.2% | -20.9% | -19.3% |  | -31.9% | -11.9% | -13.2% | -33.3% | -19.6% | -18.6%
cheer | -13.4% | 0.1% | -6.1% | -11.2% | -6.6% | -8.9% |  | -13.5% | 0.4% | -6.1% | -11.2% | -6.6% | -9.0%
flower | 13.4% | 70.3% | 53.2% | -11.0% | 7.2% | 3.0% |  | 13.2% | 68.0% | 51.7% | -11.1% | 6.9% | 2.4%
football | -47.5% | -57.7% | -56.7% | -46.7% | -56.8% | -53.4% |  | -47.7% | -57.5% | -56.5% | -46.8% | -56.4% | -53.8%
mobile | 117.1% | 237.2% | 217.4% | 9.1% | 29.4% | 28.6% |  | 117.0% | 233.4% | 216.0% | 8.9% | 29.2% | 27.9%
tennis | 75.9% | 144.7% | 106.7% | 1.9% | 20.4% | 13.5% |  | 75.8% | 143.8% | 106.9% | 1.9% | 20.1% | 13.0%
average | 2.2% | 34.0% | 26.5% | -21.0% | -13.4% | -13.1% |  | 2.1% | 33.4% | 26.8% | -21.1% | -13.5% | -13.3%
The proposed GOP structure reduced the BDR gap between frame sequence and field sequence.
There are still about 30% BDR gap for chroma for mobile and calendar.

## Slide 10: Tested LD GOP Structures
Test sequences
  Nine MPEG2 480i 30fps test sequences
  Each sequence is 150 frames except car, which is 140 frames.
Anchor (Frame-GOP-CTC)
  CTC LD configuration with frame structured pictures.
  GOP size is 4.
Field-GOP-CTC
  CTC LD configuration with field structured pictures.
  GOP size is 4.
Field-GOP-New
  Proposed LD configuration with field structured pictures.
  GOP size is 8.
LD results are cross-checked by
  Motorola, JCTVC-K0317
  Panasonic, JCTVC-K0326
  Thank you very much.

## Slide 11: Results of LD GOP Structures
 | LB-Main |  |  |  |  |  |  | LB-HE10 |  |  |  |  | 
 | Field-GOP-CTC |  |  | Field-GOP-New |  |  |  | Field-GOP-CTC |  |  | Field-GOP-New |  | 
 | BD-rate (piecewise cubic) |  |  | BD-rate (piecewise cubic) |  |  |  | BD-rate (piecewise cubic) |  |  | BD-rate (piecewise cubic) |  | 
 | Y | U | V | Y | U | V |  | Y | U | V | Y | U | V
ballet | -35.0% | -24.2% | -27.1% | -39.2% | -30.0% | -33.7% |  | -35.6% | -23.5% | -27.4% | -40.1% | -30.9% | -34.7%
bicycle | -17.8% | -20.9% | -15.7% | -18.8% | -19.3% | -15.3% |  | -17.8% | -20.9% | -15.4% | -18.8% | -19.3% | -15.1%
bus | -22.9% | -22.0% | -16.3% | -28.7% | -29.8% | -25.5% |  | -23.1% | -22.8% | -16.4% | -28.8% | -30.2% | -26.6%
car | -22.2% | -12.2% | -10.1% | -25.7% | -15.7% | -13.4% |  | -22.3% | -10.4% | -5.9% | -25.7% | -15.2% | -12.2%
cheer | -1.4% | -1.2% | -1.4% | -5.9% | -5.6% | -5.5% |  | -1.1% | -0.8% | -1.0% | -5.7% | -6.0% | -5.6%
flower | 12.6% | 33.2% | 39.0% | -11.3% | 0.1% | -1.2% |  | 12.6% | 33.2% | 39.6% | -11.4% | -0.4% | -1.5%
football | -42.0% | -50.6% | -48.6% | -42.3% | -49.6% | -46.1% |  | -42.0% | -50.0% | -48.3% | -42.3% | -48.9% | -45.3%
mobile | 113.6% | 187.4% | 176.4% | 5.0% | 28.0% | 23.8% |  | 113.4% | 189.0% | 177.6% | 4.9% | 27.1% | 23.5%
tennis | 75.3% | 113.8% | 99.0% | -2.7% | 18.5% | 8.3% |  | 75.3% | 114.1% | 97.9% | -2.1% | 17.8% | 7.2%
average | 6.7% | 22.6% | 21.7% | -18.8% | -11.5% | -12.1% |  | 6.6% | 23.1% | 22.3% | -18.9% | -11.8% | -12.3%
 | LP-Main |  |  |  |  |  |  | LP-HE10 |  |  |  |  | 
 | Field-GOP-CTC |  |  | Field-GOP-New |  |  |  | Field-GOP-CTC |  |  | Field-GOP-New |  | 
 | BD-rate (piecewise cubic) |  |  | BD-rate (piecewise cubic) |  |  |  | BD-rate (piecewise cubic) |  |  | BD-rate (piecewise cubic) |  | 
 | Y | U | V | Y | U | V |  | Y | U | V | Y | U | V
ballet | -37.3% | -27.7% | -31.1% | -41.4% | -34.1% | -36.1% |  | -37.7% | -26.6% | -31.0% | -42.0% | -33.5% | -36.7%
bicycle | -19.8% | -22.1% | -17.2% | -20.7% | -19.7% | -15.7% |  | -19.7% | -22.2% | -16.5% | -20.7% | -20.0% | -15.9%
bus | -30.6% | -29.1% | -22.8% | -34.5% | -33.5% | -28.5% |  | -31.0% | -31.5% | -22.6% | -34.9% | -35.8% | -30.2%
car | -25.7% | -13.7% | -10.1% | -28.2% | -14.1% | -9.6% |  | -25.8% | -12.0% | -8.0% | -28.2% | -13.8% | -9.3%
cheer | -2.2% | -1.9% | -2.3% | -6.2% | -6.1% | -6.0% |  | -1.9% | -1.0% | -1.1% | -6.1% | -5.7% | -5.0%
flower | 6.3% | 30.1% | 33.2% | -10.7% | 5.2% | 4.2% |  | 6.2% | 30.0% | 34.1% | -10.8% | 4.6% | 3.6%
football | -42.9% | -51.4% | -49.1% | -43.1% | -50.1% | -45.9% |  | -42.6% | -50.8% | -48.6% | -42.7% | -49.5% | -45.6%
mobile | 103.0% | 180.2% | 169.8% | 8.2% | 37.1% | 32.3% |  | 103.2% | 180.0% | 169.3% | 7.9% | 35.0% | 30.7%
tennis | 68.3% | 111.1% | 91.6% | 2.0% | 28.9% | 15.5% |  | 67.9% | 108.0% | 92.2% | 1.6% | 23.4% | 14.8%
average | 2.1% | 19.5% | 18.0% | -19.4% | -9.6% | -10.0% |  | 2.1% | 19.3% | 18.6% | -19.5% | -10.6% | -10.4%

## Slide 12: Conclusions
The propose GOP structures for field sequence are more robust than the CTC GOP structures for field sequence.
  There are still significant BDR gap for chroma for some tested sequences.
  Effect of 3-2 pull down was not tested
Propose to adopt to HM9 software
  the software memory extension to HM9 to support longer GOP structure.
  the new GOP structures for field sequences to be a part of HM9 configuration files.