## Slide 1: JCTVC-K0164 AHG 9: On non-ref TSA & STSA
The 11th JCT-VC Meeting
LG Electronics

## Slide 2: Outline
TSA & STSA can be considered like markers
  Telling that from this point, decoder can start decoding higher temporal layer
  Telling bitstream extractor to stop removing NAL units from that point
Currently we have TSA_R, TSA_N, STSA_R, and STSA_N
If TSA_N and STSA_N are removed, the bitstream losses its markers
  E.g., by extractor that simply removed non-referenced NAL units
  Several cases are presented
Proposal:
  Add constraint such that TSA & STSA NAL units shall not be discarded during bitstream removal, or,
  Remove TSA_N and STSA_N
  Add constraint for STSA such that there should be no temporal gap between two consecutive STSA NAL units.

## Slide 3: TSA & STSA as marker for bitstream removal

## Slide 4: Case 1
TSA_N is used to indicate temporal sub-layer access
During congestion, all non-referenced NAL units are removed
Results: no more marker to indicate temporal sub-layer access

## Slide 5: Case 2 (1)
Coded structure
NAL unit removal plan

## Slide 6: Case 2 (2)
Bitstream has to pass to MANE
  MANE 1: simply remove non-referenced NAL units if needed
  MANE 2: remove NAL units by taking care of TSA & STSA

## Slide 7: Proposal #1
Specify that TSA & STSA are not to be removed intentionally by system
Or, remove TSA_N and STSA_N

## Slide 8: Proposal #2 (1)
Add a constraint such that for STSA NALUs, there should be no temporal layer gap between two consecutive STSA NALUs.
  The first STSA NALU after a RAP NALU can appear at any temporal layer except the base temporal layer
  The next STSA NALU shall have at one higher temporal layer that the previous one.

## Slide 9: Proposal #2 (2)
With the constraint, the use of STSA can be more robust

## Slide 10: Summary
TSA_N and STSA_N may have issues
  Can be removed by simple bitstream extractor
We propose:
  To specify that TSA & STSA should not be removed intentionally by system, or alternatively:
    Remove TSA_N and STSA_N
    Simplify TSA NALUS and STSA NALUs to be only: TSA_NUT and STSA_NUT
  To add a constraint such that there should be no temporal layer gap between two consecutive STSA NALUs