## Slide 1: JCTVC-K0165: Proposal to add pic_struct information to HEVC
Osnat Bar-Nir, Chad Fogg

## Slide 2: Introduction
This contribution proposes to add AVC-like pic_struct information to pic_timing SEI.

## Slide 3: Introduction
In the case of 3:2 pulldown, without appropriate metadata, in order to maintain fixed frame rate constraint, the progressive 24 frames content should be coded as 60 fields (with 3:2 field duplication).
Display related metadata is required in order to maintain the original frame coding

## Slide 4: Introduction
At the previous meeting it was claimed that the straightforward solution would be to encode 60 fields, since the overhead of the duplicated fields is negligible.
Simulation results show that despite the negligible size of the duplicated fields (all skip), the coding efficiency significantly decreases due to field coding.

## Slide 5: Simulation Results
 | BD-rate (60 field vs. 24 frame) |  |  | BD-rate (48 fields vs. 24 frames) |  | 
Video Sequences | Y | U | V | Y | U | V
Kimono1 | 20.8% | 66.0% | 72.2% | 15.7% | 56.6% | 64.9%
Tennis | 1.9% | 46.0% | 40.8% | -2.4% | 38.4% | 34.0%
ParkScene | 85.7% | 144.2% | 140.1% | 70.8% | 120.8% | 115.8%
Animation | 11.4% | 60.7% | 51.2% | 11.0% | 57.7% | 53.8%
River & Boat | 13.2% | 75.0% | 74.0% | 11.4% | 69.2% | 70.0%
Dance (slow motion + static background) | 3.8% | 11.6% | 15.9% | 2.4% | 10.8% | 15.3%
Walking crowd | 18.4% | 44.6% | 49.8% | 13.9% | 38.9% | 43.4%
Overall | 22.17% | 64.01% | 63.43% | 17.54% | 56.06% | 56.74%

## Slide 6: Proposal
Add AVC-like pic_struct information to pic_timing SEI message, to explicitly define the intended display order and picture output time (NumClockTS*tc)
Remove redundant elements from field_indication SEI
Add pic_struct_present_flag to VUI()

## Slide 7: Interpretation of pic_struct (based on AVC’s table D-1)
Value | Indicated display of picture | Restrictions | NumClockTS
0 | (progressive) frame | field_pic_flag shall be 0 | 1
1 | bottom field | field_pic_flag shall be 1 | 1
2 | top field | field_pic_flag shall be 1 | 1
3 | top field bottom field, in that order | field_pic_flag shall be 0 | 2
4 | bottom field, top field, in that order | field_pic_flag shall be 0 | 2
5 | top field, bottom field, top field repeated, in that order | field_pic_flag shall be 0 | 3
6 | bottom field, top field, bottom field repeated, in that order | field_pic_flag shall be 0 | 3
7 | frame doubling | field_pic_flag shall be 0 | 2
8 | frame tripling | field_pic_flag shall be 0 | 3
9..15 | reserved |  | 

## Slide 8: Semantics
pic_timing( payloadSize ) { | Descriptor
if( CpbDpbDelaysPresentFlag ) { | 
cpb_removal_delay | u(v)
dpb_output_delay | u(v)
if( sub_pic_cpb_params_present_flag ) { | 
num_decoding_units_minus1 | ue(v)
for( i = 0; i <= num_decoding_units_minus1; i++ ) { | 
common_du_cpb_removal_delay_flag | u(1)
if( common_du_cpb_removal_delay_flag ) | 
common_du_cpb_removal_delay_minus1 | u(v)
num_nalus_in_du_minus1[ i ] | ue(v)
if( !common_du_cpb_removal_delay_flag ) | 
du_cpb_removal_delay[ i ] | u(v)
} | 
} | 
} | 
if (pic_struct_present_flag ){ | 
pic_struct | u(4)
} | 
} | 

## Slide 9: Changes to field_indication SEI
field_indication( payloadSize ) { | Descriptor
field_pic_flag | u(1)
progressive_source_flag | u(1)
duplicate_flag | u(1)
if( field_pic_flag ) | 
bottom_field_flag | u(1)
else if( !progressive_source_flag ) | 
top_field_first_flag | u(1)
else | 
reserved_zero_1bit /* equal to 0 */ | u(1)
reserved_zero_45bits /* equal to 0 */ | u(45)
} | 

## Slide 10: Conclusion
Metadata is required to address the case that the intended display format is different from the coding format, in systems that require fixed frame rate.
As in the case of 2:3 pulldown
It is propose to add AVC-like pic_struct information to pic_timing SEI message

## Slide 11: Thank you!