## Slide 1: JCTVC-K0166 AHG 9: On RAP NAL units
The 11th JCT-VC Meeting
LG Electronics

## Slide 2: Outline
There are 6 NALU types for RAP
  Some of them are actually very similar in behavior (i.e., IDR & BLA)
Proposal:
  Merge IDR & BLA: IDR_W_TFD, IDR_W_DLP, IDR_N_LP
  Consequently, need little modification in Slice Header
    Remove IdrPicFlag
    Always send POC_LSB including when the slice is part of IDR pic
    Always send RPS including when the slice is part of IDR pic
Temporal level of all RAP NALU is fixed to value 0
Proposal:
  Simplify 6 types of RAP NALU types as only 1: RAP_NUT
  Instead of signalling temporal level, use the 3 bits for detail RAP types

## Slide 3: Proposal #1 – Merge IDR & BLA NALU types (1)
BLA pictures
  Originally coded by encoder as CRA
  Changed by system to BLA when RA / splicing happen
Other than the above, IDR and BLA NALU types seems to be treated similarly
Merging the two RAP seems to be possible
  Either remove IDR or remove BLA
  If BLA is removed, then, we may have:
    IDR_W_TFD
    IDR_W_DLP
    IDR_N_LP

## Slide 4: Proposal #1 – Merge IDR & BLA NALU types (2)

## Slide 5: Proposal #1 – Merge IDR & BLA NALU types (3)
When BLA, slice header contains POC_LSB & RPS
Then if BLA & IDR are merged, the following modifications are needed
  Remove IdrPicFlag  no longer needed
  Signal POC_LSB in slice headers of IDR
  Signal RPS in slice headers of IDR

## Slide 6: Proposal #2 – Simplification to RAP NALU types
When NALU is RAP, signaling temporal level is redundant
  Constrained to be 0
Instead of using 3 bits for nuh_temporal_id_plus1, signal types of RAP
  Then simplify RAP NALU types from 6 types to only 1 type
  RAP_NUT
nal_unit_header( ) { | Descriptor
forbidden_zero_bit | f(1)
nal_unit_type | u(6)
nuh_reserved_zero_6bits | u(6)
if (nal_unit_type != RAP_NUT) | 
nuh_temporal_id_plus1 | u(3)
else | 
nuh_rap_type | u(3)
} | 

## Slide 7: Proposal #2 – Simplification to RAP NALU types
nuh_rap_type value | Descriptor
0 | Forbidden / unused
1 | BLA_W_TFD
2 | BLA_W_DLP
3 | BLA_N_LP
4 | IDR_W_LP
5 | IDR_N_LP
6 | CRA
7 | Reserved
nuh_rap_type value | Descriptor
0 | Forbidden / unused
1 | IDR_W_TFD
2 | IDR_W_DLP
3 | IDR_N_LP
4 | CRA
5 | Reserved
6 | Reserved
7 | Reserved
If proposal #1 is agreed