## Slide 1: JCTVC-K0167 AHG 9: On dependent slice
The 11th JCT-VC Meeting
LG Electronics

## Slide 2: Outline
For dependent slice, slice header contains minimum syntax elements
Non present syntax elements are copied from previous slice header
Such design may have some issues
  Error resilience
  Parallelism with used with WPP
Proposal:
  POC_LSB is signaled in header of dependent slice
  Signal address of previous slice

## Slide 3: Issue #1 – Error resilience at picture level
Picture with POC 101 has been successfully decoded
Since 1st slice of pic 102 is lost, the 2nd slice might be thought as part of pic 101
  No poc information in the 2nd slice of pic 102
Solution: Send POC_LSB in header of dependent slice

## Slide 4: Issue #2 – Dependent slice & WPP
Ref slice for dependent slice shall contains:
  ctbAddrTStoRS[ ctbAddrRStoTS[ slice_address ] − 1 ]
  When WPP is used, such slice might not be identified yet
Ex., when decoding of S4 is started, S3 might not be known yet!
S0
S1
S2
S3
S4
S5
Non-dependent slice
Dependent slice

## Slide 5: Issue #3 – Error resilience at slice level
Decoder might not aware that the 3rd slice is lost
The 4th slice is coded by referring to the 2nd slice
  Incorrect results
Such incorrect results might propagate to the 5th slice
Solution: when dependent slice, signal ref_slice_address

## Slide 6: Proposed changes
slice_header( ) { | Descriptor
… | 
if( dependent_slice_enabled_flag && !first_slice_in_pic_flag ) | 
dependent_slice_flag | u(1)
if( dependent_slice_flag ) { | 
ref_slice_address | u(v)
if( !IdrPicFlag ) { | 
pic_order_cnt_lsb | u(v)
if( !dependent_slice_flag ) { | 
… | 
} | 
… | 
} | 

## Slide 7: Summary
Several issues of dependent slice are observed
  Error resilience at picture level that may affect previous correctly decoded picture
  Parallelism issue when used together with WPP
    Incorrect slice header referencing
  Error resilience at slice level
Proposed solution
  Send POC_LSB in header of dependent slice
  Send address of reference slice in header of dependent slice