## Slide 1: JCTVC-K0169 AHG 9: On layer Id partition in VPS
The 11th JCT-VC Meeting
LG Electronics

## Slide 2: Outline
There are 2 approaches for layer ID partition in VPS extension
  Approach 1: Combination of dimension types is not fixed
  Approach 2: Combination of dimension types is fixed
Proposal: A partitioning design that is in between the 2 approaches
  List of dimension types are signalled outside the loop for signalling layer ID
  Bits to vps_layer_id [i] is not restricted to 6. It is coded as u(v)
    Sum of bits for dimension_len

## Slide 3: Approach 1
Seems to be too flexible as combination of dimension_type can change from layer to layer
Total bits spent for defining layer id can be long
  Sum of dimension_id [i] – for j start from 0 to num_dimensions_minus1
vps_extension( ) { | Descriptor
… | 
// layer specific information | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) { | 
// mapping of layer ID to scalability dimension IDs | 
num_dimensions_minus1[ i ] | u(4)
for( j = 0; j <= num_dimensions_minus1; j++ ) { | 
dimension_type[ i ][ j ] | u(4)
dimension_id[ i ][ j ] | u(8)
} | 
// layer dependency | 
… | 
} | 
} | 
dimension_ type[ i ][ j ] | dimension_id[ i ][ j ]
0 | view order idx
1 | depth flag
2 | dependency ID
3 | quality ID
4..15 | reserved

## Slide 4: Approach 2
To rigid
It is difficult to make good combinations of dimensions.
  Do not like future proof design
  Seems like predicting the future
vps_extension( ) { | Descriptor
… | 
// scalability type and layer_id partitioning method | 
scalability_type | u(4)
for( i = 0; i < MaxDim( scalability_type ); i++ ) { | 
layer_id_dim_len[ i ] | u(3)
// layer specific information | 
… | 
} | 
} | 

## Slide 5: Approach 2
scalability_type | MaxDim(scalability_type) | Scalability dimensions
0 | 1 | none (base HEVC)
1 | 2 | spatial and quality
2 | 3 | spatial, quality, reserved
3 | 4 | spatial, quality, reserved, reserved
4 | 2 | multiview and depth
5 | 3 | multiview, depth, reserved
6 | 4 | multiview, depth, reserved, reserved
7 | 4 | multiview, spatial, quality and depth
8 | 5 | multiview, spatial, quality, depth, reserved
9 | 6 | multiview, spatial, quality, depth, reserved, reserved
10...15 | reserved | reserved

## Slide 6: Proposed design
Having the loop for dimension type & length independently
  Improve approach 2 since it relaxes fixing the scalability type.
  Simplify approach 1 since combinations of dimension type is defined earlier.
vps_extension( ) { | Descriptor
… | 
// layer specific information | 
num_dimension_minus1 | ue(v)
for (i = 0; i <= num_dimension_minus1; i++) { | 
dimension_type [i] | u(4)
dimension_len [i] | u(3)
} | 
for (i = 1; i <= vps_max_layers_minus1; i++) { | 
vps_layer_id [i] | u(n)
// layer dependency | 
… | 
} | 
} | 
dimension_ type[ i ][ j ] | dimension_id[ i ][ j ]
0 | view order idx
1 | depth flag
2 | dependency ID
3 | quality ID
4..15 | reserved