## Slide 1: AHG7: Options present in Extended Chroma Format model
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-K0181

## Slide 2: Introduction
AHG7 ECF software model history:
During the 10th JCT-VC conference, two models (J0191 & J0357) were presented for extending the HEVC chroma formats.
J0191 was extended to include J0357 and patched to HM7.1
During the meeting cycle, J0191 was patched to HM8.0 and supplied by the AHG Chair to the AHG7 branch, along with a set of 10-bit 4:2:2 and 4:4:4 sequences.
The software has since been patched to HM8.1.
Benchmarks against JM18.4 were provided by BBC to AHG7 (also confirmed by ourselves).

## Slide 3: Extended Chroma Format Model
Examination of options available in 4:2:2/4:4:4 :
  The system was evaluated using the standard intra_he10 and lowdelay_he10 profiles at the standard set of QPs (22, 27, 32, 37).
  Previous simulations (distributed via the reflector) indicated there was correspondence between 8 and 10-bit profiles.
  AHG7 ECF model provides 44 different options:
  33 options were tested.
  11 options were not tested or reserved for future study.

## Slide 4: Table of Configurable Features
 | Tool / Feature | Options | Options Tested
Block structure | Slices/CU/PU structures. | 3 | 3
 | TU structures. |  | 
 | NSQT. |  | 
Prediction | Intra-prediction angular prediction. | 16 | 15
 | Intra reference sample filtering. |  | 
 | TU edge filtering for H, V and DC modes. |  | 
 | LM_Chroma. |  | 
 | Motion interpolation filters |  | 
Transform & Quantizer | MDDT. | 6 | 4
 | Modified QP for rectangular blocks (4:2:2) |  | 
 | Scaling lists. |  | 
 | Chroma QP clipping table. |  | 
Entropy Coding | Chroma CBF Context Variable (CV) derivation. | 19 | 11
 | Chroma CV sets and rules. |  | 
 | MDCS. |  | 
 | Significance map coding. |  | 
No functional changes implemented for deblocking filter, ALF, SAO. |  |  | 

## Slide 5: Summary / Conclusion
JCT-VC K0181 details results produced when the AHG7 software default configurations are adjusted.
It is proposed that the committee consider these results in order to decide whether a change in base configuration is required.
It is also proposed that the committee consider extending the operating points (lower QPs) and adjusting the test-set of sequences for these new chroma formats.