## Slide 1: AHG4: Dependent slices restriction
Semih Esenlik
Matthias Narroschke
Thomas Wedi
11th JCT-VC meeting, Shanghai 09-19 October 2012

## Slide 2: Summary
Meeting notes from HLS AhG meeting on JCTVC-K0314:
Conceptually, a "dependent slice" should be considered part of the same slice.
The HLS AHG agreed that these aspects should be clarified. Offline study with review of the identified issues was recommended.
Problem:
Existing restrictions on the joint usage of slices and WPP/tiles do not follow the above principle.
Proposal:
Clarify/extend the scope of previous restrictions to consider dependent slices.

## Slide 3: Problem 1: Single core decoding of tiles
(2) Slice
Tile 1
Tile 2
(3) Slice
(1) Slice
(2) Normal Slice
Tile 1
Tile 2
(4) Slice
(1) Slice
(3) Dependent Slice
Not allowed
(Restriction on slices & tiles)
Allowed
Problem: Single core decoding with regular z-scan order requires:
Ahead of time parsing of all slice headers.
(Alternatively) additional back and forth jumps in the bitstream to discover parent-dependent slice associations.
Additional storage space for slice headers.
Notes: Jul 31, 2026
<number>

## Slide 4: Problem 2: Non-causal bitstream
Wavefront 1
Wavefront 2
Wavefront 3
Slice
Slice
Wavefront 1
Wavefront 2
Wavefront 3
(1) Slice
(2) Normal Slice
(3) Dependent Slice
Not allowed
(Restriction on slices & WPP)
Allowed
Problem: Decoding of slice (3) cannot in parallel with slice (1).
Decoding latency is increased.
Minimum decoding latency is limited to 1 LCU row.
 Same problem exists also for tiles.
Notes: Jul 31, 2026
<number>

## Slide 5: Problem 3: Reduced loss resiliency
Slice(2) is assumed to be lost in the network.
Problem: Slice(3) is partially decodable if slice(2) is a dependent slice. However it is forced to be discarded since type (normal/dependent) of the lost slice is unknown.
 Same problem exists also for tiles.
Wavefront 1
Wavefront 2
Wavefront 3
(1) Slice
(2)Normal/Dependent slice
(3) Dependent Slice
Slice (2) is lost
Notes: Jul 31, 2026
<number>

## Slide 6: Solution for WPP, Alternative 1
If WPP is enabled and if a normal slice does not start at the beginning of a CTB row, then the next CTB row shall not start with a dependent slice.
(1) Normal slice
(2) Normal slice
Wavefront 1
Wavefront 2
Wavefront 3
(3) Dependent slice
Notes: Jul 31, 2026
<number>

## Slide 7: Solution for WPP, Alternative 2
If dependent slices and WPP are both enabled, normal slices start only at the beginning of a CTB row.
(1) Normal slice
(2) Normal slice
Wavefront 1
Wavefront 2
Wavefront 3
(3) Dependent slice

## Slide 8: Solution for tiles, Alternative 1
If the first CTB of a normal slice is not the first CTB of a tile, then the next tile shall not start with a depedent slice.
(2) Normal Slice
Tile 1
Tile 2
(4) Slice
(1) Slice
(3) Dependent Slice

## Slide 9: Solution for tiles, Alternative 2
If the dependent_slice_flag is equal to 1 and the first CTB of the slice is the first CTB of a tile, then the preceding and proceeding slices shall start at the beginning of a tile.
(2) Normal Slice
Tile 1
Tile 2
(4) Slice
(1) Slice
(3) Dependent Slice
Tile 1
Tile 2
(3) Slice
(1) Slice
(2) Dependent Slice
Notes: Jul 31, 2026
<number>

## Slide 10: BACKUP SLIDES

## Slide 11: Problem: Non-causal bitstream
Wavefront 1
Wavefront 2
Wavefront 1
Wavefront 2
(1) Normal slice
(2) Dependent slice
(3) Normal slice
(4) Dependent slice
How to initialize CABAC?
ENCODER
DECODER
If there is a normal slice at the upper CTB row after the first CTB  initialize CABAC with default initial values. Take the slice header data from the last normal slice in upper CTB row.
Otherwise  initialize CABAC with WPP tables.
(1) Normal slice
(2) Dependent slice
(3) Normal slice
Notes: Jul 31, 2026
<number>

## Slide 12: Problem: Non-causal bitstream
(1) Normal slice
(2) Depedent slice
Wavefront 1
Wavefront 2
Wavefront 3
(3) Dependent slice
Problem: The minimum decoding latency is limited to 1 LCU row (cannot be made smaller).
Encoder:
The encoding of slices (1) and (3) are completed long before the encoding of slice (2).
Decoder:
In order start decoding slice (3), both slices (1) and (2) are required to be available.
(4) Depedent slice
Notes: Jul 31, 2026
<number>