## Slide 1: AHG7: Adaptive colour-space transform of residual signals
K. Kawamura, T. Yoshino, S. Naito
KDDI Corp. (KDDI R&D Labs. Inc.)

## Slide 2: Overview
Additional coding tool for only 4:4:4 format
  Reduce colour space redundancy for each TU
  Target is residual signals of intra/inter pred.
  No additional syntax
  BD-rate 6.7%/7.2%/8.7% (AI/RA/LD) for YUV4:4:4
  BD-rate 24.3%/36.9%/37.5% for RGB4:4:4 (non-C.T.C.)
Recommend to adopt the proposal to CE/HM
  Related to FrExt or Prof. Prof.

## Slide 3: Motivation & Solution
Motivation
  Reduce inter-plane redundancy
Proposed solution: ACST
  Three planes are transformed into that in no correlated space.
  Prediction error signals are transformed.
  Transform matrix is based on singular-value-decomposition for each TU.

## Slide 4: Proposed architecture
Intra Prediction
Inter Prediction
Color space transform.
FDCT/FDST
Q
IQ
IDCT/IDST
Color space inverse transform.
In-loop filters
Frame buffer
Local decoded image
Original image
Matrix derivation

## Slide 5: Colour space transform
Forward transform
Inverse transform

## Slide 6: Matrix derivation –reference–
Intra block case
  Coded pixels
Inter block case
  Reference blocks of MC
Target block
Reference
pixels
Reference
frame
Target frame
Reference
block
Target
block

## Slide 7: Matrix derivation –algorithm–
Covariance matrix
  Average is subtracted for each plane
  For example, [3x32][32x3]t=[3x3]
Simplified singular-value-decomposition
  Algorithm: Jacobi method
  Arithmetic: Integer multiplication and shift operation only

## Slide 8: Experimental Results 1
Implemented on HM8.0-Ahg7-dev
Chroma QP clipping is turned On.

## Slide 9: Experimental Results 2
RGB 444 sequences of non C.T.C.
Chroma QP clipping is turned Off.

## Slide 10: Experimental Results 3
Proposed ACST v.s. LM (K0190)
  Gain is significant.

## Slide 11: Remarks
No additional syntax
Some coding structure is changed
  All planes use same structure (CU/PU/TU)
  All planes use same intra prediction mode
  RDO of intra picture considers all planes simultaneously
Related contribution is JCTVC-K0192.

## Slide 12: Conclusion
Additional coding tool for only 4:4:4 format
  BD-rate 6.7%/7.2%/8.7% (AI/RA/LD) for YUV4:4:4
  BD-rate 24.3%/36.9%/37.5% for RGB4:4:4 (non-C.T.C.)
  Additional decoding runtime is small.
Recommend to adopt the proposal to HM
  Related to FrExt or Prof. Prof.

## Slide 13: Supplemental slides