## Slide 1: JCTVC_K0216 HEVC interlaced coding assessment and Chroma issue consideration
  J.M. Thiesse, J. Viéron, P. Larbier, A. Depreux

## Slide 2
Broadcasters and service providers express strong needs for Interlaced material coding support. Legacy interlaced video content represent still a very large part of the current video traffic.
So far, Interlace support in HEVC has been achieved through the adoption of the field indication SEI message assuming field only encoding.
In previous Stockholm meeting, contribution JCTVC-J0466 reported an assessment of HEVC interlaced coding considering field-only coding: limited performance against AVC were highlighted.
This contribution proposes a new assessment of HEVC performance for interlace coding including efficient field GOP structure and two solutions for chroma misalignment issue.
Introduction
Notes: <number>

## Slide 3
Top/Bottom fields encoded in a « frame scan order ».
Each field has a Top and a Bottom field as reference in each list.
Config file modification available on JCTVC-K0216 for 8 and 16 fields
Proposed Field GOP structure
Fig. 1 Reference Gop structure
Fig. 2 Proposed Gop structure

## Slide 4
Interlaced 4:2:0 material
  Different vertical sampling position of chroma components,
  Displacement between top and bottom fields chroma samples
Inconsistency during chroma MV derivation when a Top field points to a Bottom field or inversely
Chroma vector misalignment :
  MV top to bottom: chroma MV points to 0.25 pixel below the correct position.
  MV bottom to top: chroma MV points to 0.25 pixel above the correct position.
“Encoder-only” solution:
  Spend more bits on Chroma residual
  Disabled Skip mode with top to bottom reference (and bottom to top)
=> Coding efficiency decrease
“AVC like” solution: shift during encoding (required field signalization)
Chroma misalignment issue

## Slide 5
Three steps:
Before encoding, align both top and bottom fields chroma samples : chroma shifting
Related chroma displacements are then signaled in the bitstream
At the decoding side, inverse shifting of the chroma samples in a proper way (e.g. original source)
Signalization:
  Previous proposition: add three new syntax elements in SEI: chroma_sample_loc_delta_flag, chroma_sample_loc_delta_x and chroma_sample_loc_delta_y
  As suggested by JCT-VC, VUI can be used for the proposed shift:
  chroma_loc_info_present_flag set to 1
  chroma_sample_loc_type_top_field set to 4
  chroma_sample_loc_type_bottom_field set to 2
  => « Hack » of the initial VUI purpose => loss of the original Chroma phase position
  => Clarification of VUI definition and usage?
Proposal

## Slide 6
Experiments were conducted using HM-8.0 software in RAHE configuration and ATEME own H.264/AVC encoder (PAFF + MBAFF)
Four HD (1920x1080@60i, 450 frames) sequences specified in ITU-R BT.1120-3 and two additional SD sequences have been used
Proposed GOP structure tested for 8 and 16 fields (2 references by B pictures)
Proposed algorithm with phase shifting using Lanczos-3 filter (6 taps)
Experiment settings
 | H.264/AVC | HEVC
FrameRate | {25, 30} | {50, 60}
SourceHeight | 1088 | 544
FrameToBeEncoded | 450 | 900
IntraPeriod | 48 | 96
GOPSize | 4 (frames) | 8 (fields)
 | H.264/AVC | HEVC
FrameRate | {25, 30} | {50, 60}
SourceHeight | 1088 | 544
FrameToBeEncoded | 450 | 900
IntraPeriod | 48 | 96
GOPSize | 8 (frames) | 16 (fields)
Configs for 8 fields
Configs for 16 fields

## Slide 7
Modified field GOP structure: average coding gain of 23.8%
  This GOP structure strentghen Chroma misalignment issue (more top to bottom and bottom to top references)
Chroma misalignment is visually corrected by the two proposed solution associated to an objective Chroma improvement (+5% against reference).
Results HEVC vs AVC (8 fields)
 | BD-rate (HM8.0 frame)* |  |  | BD-rate (HM8.0 field) |  |  | BD-rate (HM8.0 field + proposed GOP structure) |  |  | BD-rate (HM8.0 field + proposed GOP structure + chroma shift before coding) |  |  | BD-rate (HM8.0 field + proposed GOP structure + chroma shift inside HM) |  | 
Video Sequences | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Church_HD | -28.2 | -62.0 | -44.0 | -51.7 | -51.2 | -31.6 | -53.8 | -48.8 | -29.9 | -53.8 | -50.0 | -30.7 | -53.8 | -52.3 | -33.3
Whale_Show_HD | -6.4 | -47.5 | -35.7 | -18.9 | -44.4 | -11.2 | -19.8 | -35.2 | -26.8 | -20.8 | -37.1 | -29.4 | -20.8 | -39.2 | -31.9
Marching_in_HD | -21.9 | -81.5 | -78.7 | -16.8 | -57.7 | -50.8 | -13.2 | -43.0 | -32.2 | -13.3 | -45.9 | -35.9 | -13.3 | -49.5 | -40.8
Walk_HD | -34.8 | -66.3 | -57.6 | -31.9 | -42.2 | -31.7 | -32.1 | -37.8 | -26.9 | -32.1 | -39.4 | -29.1 | -32.2 | -44.7 | -35.8
Mobile_and_calendar_SD | -34.9 | -72.5 | -70.1 | 7.8 | -16.6 | 0.7 | 1.4 | -2.4 | 14.8 | 1.1 | -7.2 | 7.8 | 1.1 | -11.4 | 1.4
EBU_scene3_SD | 40.4 | 24.2 | 30.3 | -22.8 | -33.8 | -26.8 | -24.7 | -32.0 | -24.6 | -25.1 | -33.7 | -25.6 | -25.2 | -35.2 | -27.6
Overall | -14.3 | -50.7 | -42.6 | -22.4 | -41.0 | -25.2 | -23.8 | -33.2 | -20.9 | -24.0 | -35.6 | -23.8 | -24.0 | -38.7 | -28.0

## Slide 8
Using 16 fields with proposed GOP structure leads to stronger coding efficiency with 26% bitrate savings for Luma.
Same observations for Chroma
Adaptive Frame/Field will clearly help as proposed in JCTVC-K0250 => ≈ 30%
Results HEVC vs AVC (16 fields)
 | BD-rate (HM8.0 frame) |  |  | BD-rate (HM8.0 field)** |  |  | BD-rate (HM8.0 field + proposed GOP structure) |  |  | BD-rate (HM8.0 field + proposed GOP structure + chroma shift before coding) |  |  | BD-rate (HM8.0 field + proposed GOP structure + chroma shift inside HM) |  | 
Video Sequences | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Church_HD | -23.9 | -56.2 | -37.0 | -49.2 | -44.4 | -23.7 | -56.2 | -55.3 | -39.7 | NA | NA | NA | -56.3 | -58.4 | -43.0
Whale_Show_HD | -6.0 | -45.2 | -34.0 | -22.1 | -50.6 | -47.0 | -21.6 | -33.9 | -25.4 | NA | NA | NA | -21.6 | -36.8 | -29.2
Marching_in_HD | -20.9 | -80.3 | -77.8 | -15.7 | -52.3 | -45.6 | -17.3 | -48.1 | -39.4 | NA | NA | NA | NA | NA | NA
Walk_HD | -32.3 | -63.4 | -55.1 | -29.9 | -37.6 | -27.6 | -36.0 | -43.8 | -34.3 | -36.1 | -46.4 | -37.8 | -36.1 | -50.0 | -42.5
Mobile_and_calendar_SD | -32.1 | -70.2 | -67.5 | 12.5 | -6.5 | 12.5 | 0.1 | -8.2 | 6.2 | -0.2 | -14.7 | -2.1 | -0.2 | -18.3 | -8.0
EBU_scene3_SD | 39.2 | 23.4 | 28.1 | -23.4 | -34.2 | -27.9 | -24.7 | -31.7 | -23.7 | -25.1 | -33.3 | -24.1 | -25.2 | -34.8 | -26.4
Overall | -14.3 | -50.9 | -42.6 | -21.3 | -37.6 | -26.5 | -26.0 | -36.8 | -26.1 |  |  |  |  |  | 

## Slide 9
Proposed field GOP structure improves interlaced encoding performances
Chroma misalignment is a major issue which needs to be smartly resolved: corrected by tested solutions
Significant interlaced coding performances reported
Recommendations:
  Adopt proposed GOP structure for future interlaced assessments
  Integrate code modification for field management into HM
  Adopt Chroma shifting using SEI or VUI signalization (after clarification of VUI purpose)
Conclusion

## Slide 10
Chroma leaks