## Slide 1: K0221: On Sub-picture Based HRD Buffering
Sachin Deshpande
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Introduction
A CPB in HRD may operate at access unit level or sub-picture level.
For supporting correct HRD behavior and conformance at both access unit level and sub-picture level based on the leaky bucket model of HRD operation the {R,B,F} parameters need to be signaled for both access unit level and for sub-picture level.
Currently in HEVC draft 8 the initial buffering delay (parameter related to F) is already supported to be signaled separately for access unit level operation and for sub-picture level operation.
However currently in HEVC draft 8 only one CPB size parameter is signaled for each bitrate schedule. This is insufficient to support operation at both access unit level and sub-picture level.
<number>
Notes: <number>

## Slide 3: Proposal
This document proposes syntax elements and semantics to signal a CPB size and a CPB size scale parameter for sub-picture based CPB operation.
These parameters are calculated using leaky bucket model of operation for HRD at sub-picture level.
The main advantages of the proposed approach are:
  The signaling of CPB size and CPB size scale parameters for sub-picture based CPB operation allows correctly checking the bitstream conformance including checking that no buffer overflow or underflow occurs when operating at sub-picture level.
  It can result in requiring a smaller buffer size (for CPB) when HRD is operating at sub-picture level.
<number>
Notes: <number>

## Slide 4: Proposed Syntax & Semantics
<number>

## Slide 5: Conclusion
The document proposed syntax and semantics to signal CPB size related parameters for the operation of CPB at sub-picture level.
We propose to adopt the proposed approach in HEVC.
<number>