## Slide 1
JCTVC-K0231: VPS syntax re-ordering for easy access of extension parameters
Munsi Haque, Kazushi Sato
Sony Corporation
September 26, 2012

## Slide 2: Motivation
      Middle-boxes (network entities) to extract some of the VPS syntax parameters and VPS extension data
        Such data contains various HEVC Extension information in scalable video coding, multi-view coding and 3D video coding areas.
        needed for session negotiation and/or capability exchanges for better communication and system integration purposes.
      Re-ordering of some syntax parameters inside VPS
        enables the external network devices for easy access of some of the useful parameters in VPS and its extension
      The existing syntax parameter next_essential_info_byte_offset is re-defined as next_essential_info_byte_count
        Specifies the total number of bytes present in the optional fields of profile_tier_level(.) and vps_extension() including the bits of the syntax parameter vps_extension_byte_alignment_reserved_one_bit
        Note: byte-offset from the start of the VPS NAL Unit packet to this syntax parameter is already known as 4

## Slide 3: To locate VPS Extension in NALU Payload
Proposal Item:
  Place VPS Extension information near the beginning of the VPS NALU payload for easy access
Fixed addressing - next_essential_info_byte_count
  This byte count helps to locate and access essential information in VPS NAL unit without the need of entropy decoding
 | forbidden_zero_bit (1) | 
 | nal_unit_type (6) | 
NALUH |  | 
 | reserved/ layer_id (6) | 2 bytes
 | temporal_id_plus1 (3) | 
 | VPS Fixed Header (16) | 2 bytes
 | Profile_Level_data & VPS Extension | 
VPS (Payload) |  | 
 | Other VPS Data | 
Fixed length bits assignment
next_essential_info_byte_count
nal_unit_type (VPS) = 25

## Slide 4: VPS Parameters Access
JCTVC-K0231 changes positions of some syntaxes from those in JCTVC-J1007
next_essential_info_byte_count (Recap)
  specifies total number of bytes present in the optional fields of profile_tier_level(.) and vps_extension() including the bits of the syntax parameter vps_extension_byte_alignment_reserved_one_bit.
  Byte count independent from statistical codes bits-allocation [ue(v)]
  The byte-offset from the start of the VPS NAL Unit packet to next_essential_info_byte_count is already known as 4
video_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
vps_temporal_id_nesting_flag | u(1)
vps_reserved_zero_2bits | u(2)
max_num_layers_minus1 // vps_reserved_zero_6bits in DIS | u(6)
vps_max_sub_layers_minus1 | u(3)
profile_level( 1, vps_max_sub_layers_minus1 ) | 
next_essential_info_byte_offset //vps_reserved_zero_12bits in DIS | u(12)
for( i = 0; i <= vps_max_sub_layers_minus1; i++ ) { | 
vps_max_dec_pic_buffering[ i ] | ue(v)
vps_max_num_reorder_pics[ i ] | ue(v)
vps_max_latency_increase[ i ] | ue(v)
} | 
num_hrd_parameters | ue(v)
for( i = 0; i < num_hrd_parameters; i++ ) { | 
if( i > 0 ) | 
op_point( i ) | 
hrd_parameters( i = = 0, vps_max_sub_layers_minus1 ) | 
} | 
bit_equal_to_one | u(1)
vps_extension( ) | 
vps_extension_flag | u(1)
if( vps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
vps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
JCTVC-J1007 (Solutions for VPS Extension)
video_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
vps_temporal_id_nesting_flag | u(1)
vps_reserved_zero_2bits | u(2)
max_num_layers_minus1 // reserved_zero_6bits in DIS | u(6)
vps_max_sub_layers_minus1 | u(3)
next_essential_info_byte_count //reserved_zero_12bits in DIS | u(12)
profile_tier_level( 1, vps_max_sub_layers_minus1 ) | 
bit_equal_to_one | u(1)
vps_extension( ) | 
while( !byte_aligned( ) ) | 
vps_extension_byte_alignment_reserved_one_bit | u(1)
for( i = 0; i <= vps_max_sub_layers_minus1; i++ ) { | 
vps_max_dec_pic_buffering[ i ] | ue(v)
vps_max_num_reorder_pics[ i ] | ue(v)
vps_max_latency_increase[ i ] | ue(v)
} | 
num_hrd_parameters | ue(v)
for( i = 0; i < num_hrd_parameters; i++ ) { | 
if( i > 0 ) | 
op_point( i ) | 
hrd_parameters( i = = 0, vps_max_sub_layers_minus1 ) | 
} | 
vps_extension_flag | u(1)
if( vps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
vps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
JCTVC-K0231 (Modified VPS & Extension)