## Slide 1
JCTVC-K0232: On support of mixed video sequences in High Level Syntaxes
Munsi Haque, Kazushi Sato, Ali Tabatabai
Sony Corporation
September 26, 2012

## Slide 2: Motivation
      HEVC extensions deal with scalable video coding, multi-view coding, 3D video coding, Interlace video coding, etc.
      It is anticipated that many combinations of coded video sequences may exist in either scalable video layers or among 3D views
        Various content types from video sources of 2D (Progressive, Interlace), 3D (stereo, multi-view, Frame-Compatible), etc.
        Various coding type from hybrid codecs of HEVC, AVC, etc.
          Either in Base Layer/View and/or in Enhancement layers/views where inter-layer or inter-view predictions can be turned on/off based upon codec similarities
This proposal addresses High level syntax structures of VPS and SPS to enable such new HEVC extensions requirement
  syntax parameters are either re-defined or newly introduced to allow such HEVC extensions
  2 Options for VPS/SPS Syntax structures (Option 1 and Option 2)

## Slide 3: On High Level Parameter Sets in DIS
Parameter Set | Undefined Syntaxes in Version-1 | Descriptions with new suggestions | 
Case-1: Existing syntax parameters |  |  | 
video_parameter_set_rbsp( ) / VPS | vps_reserved_zero_2bits, u(2) |  | JCTVC-K0232: vps_sequence_type
 | vps_reserved_zero_6bits, u(6) |  | JCTVC-J1007: vps_max_num_layers_minus1
 | vps_reserved_zero_12bits, u(12) |  | JCTVC-J1007: next_essential_info_byte_offset
vps_extension() | scalability_type, u(4) sub_scalability_type, u(4) |  | JCTVC-K0233: coding_type, interlace parameter (top_field_first), etc.
sequence_parameter_set_rbsp() / SPS | sps_reserved_zero_bit, u(1) |  | JCTVC-K0232: sps_sequence_type
 | pic_height_in_luma_samples, ue(v) |  | Height for field = ½ Height for frame
picture_parameter_set_rbsp() / PPS | - |  | -
Case-2: Future extensions to define |  |  | 
VPS, SPS and PPS | Any other syntax for Interlace Support ? | JCTVC-K0232: To define | 
 | *_extension_flag, u(1) | Undefined | 
 | *_extension_data_flag, u(1) | Undefined | 

## Slide 4: Mixed Sequences Support – Option 1
vps_sequence_type | Sequence type in VPS
00 | Frame pictures only
01 | Mixed Progressive and Interlace pictures
10 | Mixed 2D and 3D Frame pictures
11 | Mixed 2D and 3D Frame-Compatible pictures
video_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
vps_temporal_id_nesting_flag | u(1)
vps_sequence_type // vps_reserved_zero_2bits in DIS | u(2)
vps_reserved_zero_6bits // used in JCTVC-J1007 | u(6)
vps_max_sub_layers_minus1 | u(3)
profile_level( 1, vps_max_sub_layers_minus1 ) | 
vps_reserved_zero_12bits // used in JCTVC-J1007 | u(12)
for( i = 0; i <= vps_max_sub_layers_minus1; i++ ) { | 
vps_max_dec_pic_buffering[ i ] | ue(v)
vps_max_num_reorder_pics[ i ] | ue(v)
vps_max_latency_increase[ i ] | ue(v)
} | 
num_hrd_parameters | ue(v)
for( i = 0; i < num_hrd_parameters; i++ ) { | 
if( i > 0 ) | 
op_point( i ) | 
hrd_parameters( i = = 0, vps_max_sub_layers_minus1 ) | 
} | 
bit_equal_to_one | u(1)
vps_extension( ) | 
vps_extension_flag | u(1)
if( vps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
vps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
sps_sequence_type_flag | Sequence_type
0 | Frame (2-D)
1 | Frame / Field / 3-D Frame / 3-D Frame-Compatible
seq_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
sps_max_sub_layers_minus1 | u(3)
sps_sequence_type_flag // sps_reserved_zero_bit in DIS | u(1)
…………….. DELETED ………………………….. | 
pic_width_in_luma_samples | ue(v)
pic_height_in_luma_samples | ue(v)
…………….. DELETED ………………………….. | 
vui_parameters_present_flag | u(1)
if( vui_parameters_present_flag ) | 
vui_parameters( ) | 
sps_extension_flag | u(1)
if( sps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
sps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
VPS
SPS

## Slide 5: Mixed Sequences Support – Option 2
video_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
vps_temporal_id_nesting_flag | u(1)
vps_reserved_zero_2bits | u(2)
vps_reserved_zero_6bits | u(6)
vps_max_sub_layers_minus1 | u(3)
profile_and_level( 1, vps_max_sub_layers_minus1 ) | 
vps_reserved_zero_12bits | u(12)
……………….. DELETED …………………………….. | 
vps_sequence_type_flag // for mixed sequence type in VPS | u(1)
if(vps_sequence_type_flag) { | 
vps_sequence_type | u(2)
vps_coding_type | u(2)
} | 
vps_extension_flag | u(1)
if( vps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
vps_extension_data_flag | u(1)
} | 
rbsp_trailing_bits( ) | 
} | 
seq_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
sps_max_sub_layers_minus1 | u(3)
sps_reserved_zero_bit | u(1)
…………….. DELETED ………………………….. | 
pic_width_in_luma_samples | ue(v)
pic_height_in_luma_samples | ue(v)
…………….. DELETED ………………………….. | 
vui_parameters_present_flag | u(1)
if( vui_parameters_present_flag ) | 
vui_parameters( ) | 
sps_sequence_type_flag // for mixed sequences | u(1)
sps_extension_flag | u(1)
if( sps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
sps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
vps_coding_type | Coding Type
00 | HEVC
01 | AVC
10 | reserved
11 | reserved
Combined effect of vps_sequence_type and sps_sequence_type_flag
VPS syntax |  | SPS syntax | 
vps_sequence_type | Sequence type in VPS | sps_sequence_type_flag | Sequence type
00 | Frame pictures only | 0 | Frame
 |  | 1 | Frame
01 | Mixed Progressive and Interlace pictures | 0 | Frame
 |  | 1 | Field
10 | Mixed 2D and 3D Frame pictures | 0 | 2D Frame
 |  | 1 | 3D Frame (stereo, multi-view)
11 | Mixed 2D and 3D Frame-Compatible pictures | 0 | 2D Frame
 |  | 1 | 3D Frame-Compatible (stereo-view)
VPS
SPS
Note (Option 2): vps_sequence_type, vps_coding_type, sps_sequence_type_flags can be assigned more bits for HEVC extensions