## Slide 1
JCTVC-K0233: VPS Extension updates in Strawman Design Approach 1 using a modified version of Scalability Mapping Table
Munsi Haque, Kazushi Sato, Ali Tabatabai
Sony Corporation
September 26, 2012

## Slide 2: Motivation
A 2-step VPS extension design method
  First, enhancement of scalability_type mapping table in approach 2 “strawman” design of VPS Extension
  Second, selection of approach 1 design over approach 2 design, and modify it with the enhanced mapping table for the final version
Added optimization and flexibility to approach 1 design
  compact definition of dimension_ids for HEVC extensions
  inclusion of mixed video sequences for HEVC Extensions
  a new sub_scalability_type mapping table creation

## Slide 3: Limitation in Approach 2 design
Selection of approach 1 design over approach 2 design for the final version
approach 2 has some limitation in its basic design
  it restricts the bit-allocations for various dimension_ids when it defines the syntax parameter, layer_id_dim_len[i] as follows:
    "layer_id_dim_len[ i ] specifies the length, in bits, of the i-th scalability dimension ID. The sum of the values layer_id_dim_len[ i ] for all i values in the range of 0 to 7 shall be less than or equal to 6.“
  It forces the design to assign a particular scalability layer with a very limited set of values for its dimension_ids
    Such limitation is not a desirable design choice

## Slide 4: VPS Extension Design with Approach 1
vps_extension( ) { // approach 1 design | Descriptor
while( !byte_aligned( ) ) | 
vps_extension_byte_alignment_reserved_one_bit | u(1)
// layer specific information | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) { | 
// mapping of layer ID to scalability dimension IDs | 
num_dimensions_minus1[ i ] | u(4)
for( j = 0; j <= num_dimensions_minus1; j++ ) { | 
dimension_type[ i ][ j ] | u(4)
dimension_id[ i ][ j ] | u(8)
} | 
// layer dependency | 
num_direct_ref_layers[ i ] | u(6)
for( j = 0; j < num_direct_ref_layers[ i ]; j++ ) | 
ref_layer_id[ i ][ j ] | u(6)
} | 
} | 
dimension_type[ i ][ j ] | dimension_id[ i ][ j ]
0 | view order idx
1 | depth flag
2 | dependency ID
3 | quality ID
4..15 | reserved
Approach 1 design is more elaborate than Approach 2
New design Goal: Use enhanced scalability_type mapping tables of Approach 2 for better re-design of Approach 1
  redundancy removal of dimension_type syntax parameter
  compact bit allocations for dimension_ids from 8 bits to a fixed number of bits via a LUT (pre-defined) approach
  Enables coding of mixed video sequences for HEVC extensions by using a new dimesnion_id parameter, sub_scalability_type

## Slide 5: VPS Extension: Modified Mapping Tables of Approach 2
JCTVC-K0233 (Option 1)
JCTVC-J1007 (Approach 2)
scalability_type | MaxDim(scalability_type) | Scalability dimensions
0 | 1 | none (base HEVC)
1 | 2 | spatial and quality
2 | 3 | spatial, quality, reserved
3 | 4 | spatial, quality, reserved, reserved
4 | 2 | multiview and depth
5 | 3 | multiview, depth, reserved
6 | 4 | multiview, depth, reserved, reserved
7 | 4 | multiview, spatial, quality and depth
8 | 5 | multiview, spatial, quality, depth, reserved
9 | 6 | multiview, spatial, quality, depth, reserved, reserved
10...15 | reserved | reserved
scalability_type | MaxDim (scalability_type) | Scalability dimensions | dimension_id | dimension_id_len
0 | 0 | none (base HEVC) | - | -
1 | 4 | coding_type, sub_scalability_type, spatial, quality | coding_type, sub_scalability_type, dependencyID, qualityID | 2, 4, 4, 4
2 | 5 | coding_type, sub_scalability_type, spatial, quality, reserved | coding_type, sub_scalability_type, dependencyID, qualityID, reserved | 2, 4, 4, 4, 4
3 | 6 | coding_type, sub_scalability_type, spatial, quality, reserved, reserved | coding_type, sub_scalability_type, dependencyID, qualityID, reserved, reserved | 2, 4, 4, 4, 4, 4
4...15 | - | reserved |  | 
coding_type, sub_scalability_type –> 2 new dimension_ids added
coding_type | Video coding type
0 | HEVC (default)
1 | AVC
2 | reserved
3 | reserved
sub_scalability_type | sub_scalability dimension_type | MaxDimSub (sub_scalability_type) | diemension_id | dimensionSub_id_len
0 | mono-view (2D) | 0 | - | -
1 | interlace (2D) | 1 | top_field_first | 1
2 | frame-compatible (3D) | 3 | depth_flag, left_view_first, fc_format | 1, 1, 4
3 | stereo-view (3D) | 3 | depth_flag, view1_id, view2_id | 1, 4, 4
4 | multi-view (3D) | 1 | depth_flag | 1
5 ... 15 | reserved |  |  | 

## Slide 6: Mixed sequences for VPS in Mapping tables
“coding_type” parameter to allow mixed coding contents of HEVC or AVC among base layer/view or enhancement_layer/view with some restrictions for mixed sequences in VPS (see also JCTVC-K0232)
“interlace” parameter allows interlace contents to be present in VPS side by side with other content types for various sequences (see also JCTVC-K0232)
  top_field_first being 1 means that the reconstructed sequence starts with a top field as the first field output during the decoding process, else it is a bottom_field_first for interlace video coding.
Allow mixed sequences of 2-D frame, 3-D Frame-compatible (Stereo), or 3D view (Stereo or Multi-view) pictures (see also JCTVC-K0232)
  additional parameters on Frame-Compatible (3D)
    left_view_first and fc_format are dimesnion_ids for Frame-compatible 3D video.
    left_view_first being 1 means that the reconstructed sequence starts with the frame-compatible format having a left view as the first view output during the decoding process, else it is a right_view_first for frame-compatible video coding.
    fc_format is a 4-bit data element indicating the format for multiplexing of two views into a single frame or sequence of frames for frame-compatibe 3D setreo-views.
      Examples for fc_format values are Top_Bottom (0), Side_by_Side (1), Row Interleaved (2), Column Interleaved (3), Checkerboard (4), etc.

## Slide 7: VPS Extension Design with Approach 1
vps_extension( ) { // new design (JCTVC-K0233) | Descriptor
while( !byte_aligned( ) ) | 
vps_extension_byte_alignment_reserved_one_bit | u(1)
// layer specific information | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) { | 
// mapping of layer ID to scalability dimension IDs | 
scalability_type | u(4)
num_dimensions1 = MaxDim (scalability_type) | 
for( j = 0; j < num_dimensions1; j++ ) { | 
nb = dimension_id_len[j] | 
dimension_id[ i ][ j ] | u(nb)
} | 
if (num_dimesnions1 > 0) { | 
sub_scalability_type[ i ] = dimension_id[ i][1] | 
num_dimensions2 = MaxDimSub ( sub_scalability_type[i] ) | 
for( j = 0; j < num_dimensions2; j++ ) { | 
nb = dimensionSub_id_len[j] | 
dimension_id[ i ][ num_dimensions1 + j ] | u(nb)
} | 
if (sub_scalability_type[i] == 4) { // multi-view | 
num_views[ i ] // views number | u(4)
for(j=0; j< num_views[i]; j++) | 
view_id[ i ][ j ] // view_ids | u(4)
} | 
} | 
// layer dependency | 
num_direct_ref_layers[ i ] | u(6)
for( j = 0; j < num_direct_ref_layers[ i ]; j++ ) | 
ref_layer_id[ i ][ j ] | u(6)
} | 
} | 
vps_extension( ) { // approach 1 design (JCTVC-J1007) | Descriptor
while( !byte_aligned( ) ) | 
vps_extension_byte_alignment_reserved_one_bit | u(1)
// layer specific information | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) { | 
// mapping of layer ID to scalability dimension IDs | 
num_dimensions_minus1[ i ] | u(4)
for( j = 0; j <= num_dimensions_minus1; j++ ) { | 
dimension_type[ i ][ j ] | u(4)
dimension_id[ i ][ j ] | u(8)
} | 
// layer dependency | 
num_direct_ref_layers[ i ] | u(6)
for( j = 0; j < num_direct_ref_layers[ i ]; j++ ) | 
ref_layer_id[ i ][ j ] | u(6)
} | 
} | 
dimension_type[ i ][ j ] | dimension_id[ i ][ j ]
0 | view order idx
1 | depth flag
2 | dependency ID
3 | quality ID
4..15 | reserved