## Slide 1
JCTVC-K0234: HEVC VUI Parameters Extension beyond Version 1
Munsi Haque, Kazushi Sato
Sony Corporation
September 26, 2012

## Slide 2: Motivation
Extends the Version-1 VUI syntax structure
  To add new syntax parameters for HEVC extensions of scalable video coding, multi-view coding, 3D video coding, etc.
VUI Extension in High Level Syntaxes with 2 options
  Option 1
    New syntax parameters use the re-defined scalability_type mapping table of VPS Extension design of Approach 2, as described in contribution JCTVC-K0233.
  Option 2
    VUI Extension uses syntax parameters derived from VPS Extension design Approach 1 instead, as defined in JCTVC-J1007.

## Slide 3: VPS Extension: New Mapping Tables from Approach 2
JCTVC-K0233 (Option 1)
JCTVC-J1007 (Approach 2)
scalability_type | MaxDim(scalability_type) | Scalability dimensions
0 | 1 | none (base HEVC)
1 | 2 | spatial and quality
2 | 3 | spatial, quality, reserved
3 | 4 | spatial, quality, reserved, reserved
4 | 2 | multiview and depth
5 | 3 | multiview, depth, reserved
6 | 4 | multiview, depth, reserved, reserved
7 | 4 | multiview, spatial, quality and depth
8 | 5 | multiview, spatial, quality, depth, reserved
9 | 6 | multiview, spatial, quality, depth, reserved, reserved
10...15 | reserved | reserved
scalability_type | MaxDim (scalability_type) | Scalability dimensions | dimension_id | dimension_id_len
0 | 0 | none (base HEVC) | - | -
1 | 4 | coding_type, sub_scalability_type, spatial, quality | coding_type, sub_scalability_type, dependencyID, qualityID | 2, 4, 4, 4
2 | 5 | coding_type, sub_scalability_type, spatial, quality, reserved | coding_type, sub_scalability_type, dependencyID, qualityID, reserved | 2, 4, 4, 4, 4
3 | 6 | coding_type, sub_scalability_type, spatial, quality, reserved, reserved | coding_type, sub_scalability_type, dependencyID, qualityID, reserved, reserved | 2, 4, 4, 4, 4, 4
4...15 | - | reserved |  | 
coding_type, sub_scalability_type –> 2 new dimension_ids added
coding_type | Video coding type
0 | HEVC (default)
1 | AVC
2 | reserved
3 | reserved
sub_scalability_type | sub_scalability dimension_type | MaxDimSub (sub_scalability_type) | diemension_id | dimensionSub_id_len
0 | mono-view (2D) | 0 | - | -
1 | interlace (2D) | 1 | top_field_first | 1
2 | frame-compatible (3D) | 3 | depth_flag, left_view_first, fc_format | 1, 1, 4
3 | stereo-view (3D) | 3 | depth_flag, view1_id, view2_id | 1, 4, 4
4 | multi-view (3D) | 1 | depth_flag | 1
5 ... 15 | reserved |  |  | 

## Slide 4: Option 1: VUI Extensions beyond version-1
vui_parameters_ext_layer( MaxNumLayersMinus1) { | Descriptor
for( i = 0; i <= MaxNumLayersMinus1; i++ ) { | 
// vui scalability type and dimension IDs | 
vui_scalability_type | u(4)
num_dimensions1 = MaxDim (vui_scalability_type) | 
for( j = 0; j < num_dimensions1; j++ ) { | 
nb = dimension_id_len[j] | 
vui_dimension_id[ i ][ j ] | u(nb)
} | 
if(num_dimensions1 > 0) { | 
vui_sub_scalability_type[ i ] = vui_dimension_id[ i ][ 1 ] | 
num_dimensions2 = MaxDimSub (vui_sub_scalability_type[ i ] ) | 
for( j = 0; j < num_dimensions2; j++ ) { | 
nb = dimensionSub_id_len[j] | 
vui_dimension_id[ i ][ num_dimensions1 + j ] | u(nb)
} | 
if (vui_sub_scalability_type[ i ] == 4) { // multi-view | 
vui_num_views [ i ] // views number | u(4)
for(j=0; j< vui_num_views [ i ]; j++) | 
vui_view_id[ i ][ j ] // view_ids | u(4)
} | 
} | 
} | 
} | 

## Slide 5: Option 2: VUI Extensions beyond version-1
vui_parameters_ext_layer( MaxNumLayersMinus1) { | Descriptor
for( i = 0; i <= MaxNumLayersMinus1; i++ ) { | 
// vui dimension IDs | 
vui_num_dimensions_minus1[ i ] | u(4)
for( j = 0; j <= vui_num_dimensions_minus1; j++ ) { | 
vui_dimension_type[ i ][ j ] | u(4)
vui_dimension_id[ i ][ j ] | u(8)
} | 
} | 
} | 
vui_dimension_type[ i ][ j ] | vui_dimension_id[ i ][ j ]
0 | view order idx
1 | depth flag
2 | dependency ID
3 | quality ID
4..15 | reserved
dimension_type Table : Approach 1 VPS Extension design in JCTVC-J1007