## Slide 1: Decoder parallelism indication
K0236
Jonatan Samuelsson
Rickard Sjöberg
Magnus Westerlund
Bo Burman
Per Fröjdh

## Slide 2: Follow-up of J0249
Problem description
Proposed solution
Why not let system layer handle this?
  Example use cases
Why only restrict the number of luma samples per thread?
  Simple complexity model
Summary
Outline
One main difference: threads_idc in VUI instead of SPS

## Slide 3: Problem description
HEVC contains different tools that enable parallel decoding e.g. slices, tiles and wavefronts.
The decoder is not guaranteed that a bitstream is encoded using any of the tools that enables parallel decoding.
Mandating use of these tools would be a burden for the encoder and reduce compression efficiency.
It is difficult for a decoder to deduce whether or not parallel decoding is possible for an entire Coded Video Sequence.

## Slide 4: Proposed solution
We propose to add a variable; Threads, to indicate the minimal number of threads the bitstream is created for.
We propose to add the syntax element threads_idc in the VUI part of the SPS to represent the variable Threads.
The proposed variable Threads imposes restrictions on the bitstream that ensures that the bitstream is parallel decodable.
It also represents an approximation of the maximum “speed-up” that can be achieved with optimal scheduling.

## Slide 5: Details of the proposal
We propose to define upper limits on the number of luma samples that has to be handled per thread as a function of the picture size and threads_idc.
Thread 1
Thread 2
Thread 3
Thread 4
Thread 1
Thread 2
Thread 3
Thread 4
Th. 5
Slices
Tiles
Wavefront
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Thread 6

## Slide 6: Details of the proposal cont.
We propose to define three different exclusive options for fulfilling the requirement imposed by threads_idc:
tiles_enabled_flag is equal to 0 and entropy_coding_sync_enabled_flag is equal to 0, and there is no slice in the coded video sequence that contains more than Floor( PicSizeLuma / Threads ) number of luma samples.

## Slide 7: Details of the proposal cont.
We propose to define three different exclusive options for fulfilling the requirement imposed by threads_idc:
tiles_enabled_flag is equal to 0 and entropy_coding_sync_enabled_flag is equal to 0, and there is no slice in the coded video sequence that contains more than Floor( PicSizeLuma / Threads ) number of luma samples.
tiles_enabled_flag is equal to 1 and entropy_coding_sync_enabled_flag is equal to 0, and there is no tile in the coded video sequence that contains more than Floor( PicSizeLuma / Threads ) number of luma samples.

## Slide 8: Details of the proposal cont.
We propose to define three different exclusive options for fulfilling the requirement imposed by threads_idc:
tiles_enabled_flag is equal to 0 and entropy_coding_sync_enabled_flag is equal to 0, and there is no slice in the coded video sequence that contains more than Floor( PicSizeLuma / Threads ) number of luma samples.
tiles_enabled_flag is equal to 1 and entropy_coding_sync_enabled_flag is equal to 0, and there is no tile in the coded video sequence that contains more than Floor( PicSizeLuma / Threads ) number of luma samples.
tiles_enabled_flag is equal to 0 and entropy_coding_sync_enabled_flag is equal to 1, and the syntax elements pic_width_in_luma_samples, pic_height_in_luma_samples and the variable CtbSize are restricted such that:
  ( 2 * pic_height_in_luma_samples + pic_width_in_luma_samples ) * CtbSize ≤ floor( PicSizeLuma / Threads )

## Slide 9: Details of the proposal cont.
Thread 1
Thread 2
Thread 3
Thread 4
Th. 5

## Slide 10: Details of the proposal cont.
We propose that threads_idc is signaled with 8 bits and that Threads is calculated as:
Threads = ( threads_idc / 4 ) + 1
which makes it possible to represent any level of parallelism from 1 to 64.75 in steps of 0.25.

## Slide 11: Why not let system layer handle this?
Decoder parallelism will be utilized in many different systems and many different applications.
Having a common definition for indicating the parallelism of a bitstream improves compatibility between different systems.
Bitstream restrictions are more easily defined and easier to understand in the video layer specification in the right context.

## Slide 12: Example use case
Consider a software decoder that performs self-evaluation to adapt its capability declaration to the available resources of the platform on which it is run.
When installed on a slow computer it might be able to decode level 3.0.
When installed on a fast computer it might be able to decode level 4.1.

## Slide 13: Example use case cont.
When using the described decoder in a conversational application the decoder can negotiate on level, resolution, bitrate etc. based on the current performance. In such a scenario it would be very useful to take parallelism into account.

## Slide 14: Example use case cont.
Using the same described decoder in an adaptive streaming application the decoder can select which representation to decode based on the level, resolution, bitrate taking into account the current performance. In such a scenario it would be very useful to take parallelism into account.

## Slide 15: Why only restrict the number of luma samples per thread?
Consider a very simple model for approximating decoding complexity.
“CABAC decoding” is proportional to the number of bits
“Pixel decoding” is proportional to the number of luma samples with non-zero coefficients and quarter-pel mv
Sequential decoding:
Cabac decoding
Pixel decoding
Cabac decoding
Pixel dec.
tr,n( m )
tr,n( m + 1 )

## Slide 16: Why only restrict the number of luma samples per thread?
Cabac
Pixel
tr,n( m )
tr,n( m + 1 )
Cabac
Pixel
Cabac
Pixel
Cabac
Pixel
Parallel decoding:
Core 1:
Core 2:

## Slide 17: Why only restrict the number of luma samples per thread?
Cabac
Pixel
tr,n( m )
tr,n( m + 1 )
Cabac
Pixel
Cabac
Pixel
Cabac
Pixel
Parallel decoding:
Pixel
tr,n( m )
C
Pixel
Cabac
Pixel
Pixel
Parallel decoding:
C
Cabac
tr,n( m + 1 )
Core 1:
Core 2:
Core 1:
C 2:

## Slide 18: Why only restrict the number of luma samples per thread?
tr,n( m + 1 )
Pixel
tr,n( m )
C
Pixel
Cabac
Pixel
Pixel
Parallel decoding:
C
Cabac
X
Core 1:
C 2:

## Slide 19: Why only restrict the number of luma samples per thread?
tr,n( m + 1 )
Pixel
tr,n( m )
C
Pixel
Cabac
Pixel
Pixel
Parallel decoding:
C
Cabac
X
Pixel
Pixel
tr,n( m )
C
Pixel
Cabac
Pixel
Parallel decoding:
C
tr,n( m + 1 )
Core 1:
C 2:
Core 1:
C 2:
Cabac

## Slide 20: Summary
We propose to add threads_idc as a bitstream restriction VUI parameter in order to provide encoders and decoders with a parameter to express decoder parallelism.
When threads_idc is greater than 0, constraints are applied to the bitstream regarding parallel processing tools.
We believe threads_idc to be very useful for software decoders