## Slide 1: JCT-VC K0241: Color Gamut Scalable Video Coding
Louis Kerofsky, Seung-Hwan Kim, Kiran Misra, Andrew Segall, And Jie Zhao
Presenter: Andrew Segall

## Slide 2: Outline
Introduction
Color spaces BT.709 vs. BT.2020 (UHDTV)
Color Space Prediction
Color Space Scalability
Results
Conclusions

## Slide 3: ITU BT.2020 (UHDTV) recommendation
Full HD content used BT.709 which defines
  Resolution
  Primary chromaticities and white point D65 (hence color gamut)
  Nonlinearity i.e. Gamma
  Luma and chroma definitions
  Quantization Bit-depth 8, 10
Recent recommendation BT.2020 for Ultra High Definition TV (UHDTV)
  Resolutions 3840x2160 or 7680x4320 (4K and 8K)
  Primaries differ from BT-709 much wider gamut white point still D65
  Gamma same as BT-709
  Luma and chroma definitions some what differ but similar
  Quantization Bit-depth 10, 12 (no 8-bit)
For consumer application, the necessity to support transmission, distribution, and storage of 10-bit video may be costly.

## Slide 4: BT.709 vs. UHDTV Chromaticity
Gamut of UHDTV significantly larger in both green and red primaries.
Identical white point used for each D65.

## Slide 5: Generation of UHDTV test data
Existing test sequences were converted to UHDTV format assuming BT.709 input using the following steps
Each pixel was processed according to the following steps
YCbCr to R’G’B’ conversion using the matrix of BT.709
R’G’B’ to RGB using the nonlinearity of BT.709, (gamma)
RGB to XYZ using primary chromaticity values from BT.709
XYZ to RGB using primary chromaticity values from BT.2020 (UHDTV)
RGB to R’G’B’ using the nonlinearity of BT.2020 (UHDTV)
R’G’B’ to YCbCr conversion using matrix of BT.2020 (UHDTV)
YCbCr
R’G’B’
[BT.709]
RGB
[BT.709]
XYZ
RGB
R’G’B’
YCbCr
[BT.2020]
[BT.2020]
[BT.709]
[BT.2020]
Matrix
Nonlinearity
Chromaticity

## Slide 6: BT.709 and UHDTV image example
The data is shown in the same representation.
The image looks different since the data is designed for different color space.
Observe the color change particularly the desaturation of the red seen in the presentation of UHDTV data. The UHDTV data is designed for presentation with more highly saturated red primary as shown on the chromaticity diagram.
BT.709 data presented as BT.709
UHDTV data presented as BT.709

## Slide 7: Color Space Prediction
The BT.709 and UHDTV data appear quite correlated.
We illustrate the correlation through scatter plots and introduce some prediction models

## Slide 8: Color Space prediction
Relation between BT.709 and UHDTV depends on image content some sample predictors are shown below
Bit Difference predictor
  No parameters
Gain Offset predictor Channel Independent)
  Encoder selects 6 = 3+3 parameters then signals to decoder (default parameters possible)
Cross Color General affine predictor
  3x3 matrix M and length 3 offset vector
  Encoder selects 12=9+3 parameters then signals to decoder
Prediction parameters can be signaled at different granularity:
  Per sequence
  Per frame
  Per slice

## Slide 9: Predictor Parameter Design
Prediction parameters can be designed by minimizing an MSE criteria between the prediction from BT.709 and the UHDTV original.
For example the minimization problem may be of the form:
A solution using standard methods can be found in the form:
Where the matrix M is constructed from the BT.709 samples by:

## Slide 10: Predictor Performance (Basketball Drive)
Note the sizable MSE reduction compared to the bit difference prediction
Note the MSE reduction in the Y channel of using cross color prediction

## Slide 11: Need for scalability
Full HD content based on BT.709
  Full HD resolution 1920x1080
  BT-709 color space
  8-bit Y,U,V component sampling
Consumer 4K, 8K content based on UHDTV
  Resolutions 3840x2160 or 7680x4320 (4K and 8K)
  UHDTV wide color gamut primaries
  10-bit Y,U,V component sampling
Scalability needed to simultaneously support
  Spatial resolution increase i.e. full HD to 4K
  Color space conversion i.e. BT.709 to UHDTV
  Bit-depth scalability i.e. 8-bit to 10-bit

## Slide 12: Scalable coder
Input
BT.709
Input
UHDTV
Base Layer
Encoding Loop
Enhancement Layer
Encoding Loop
Base Layer
Reference
Bitstream
Multiplex
Enhancement Layer
Reference
Compressed
Output

## Slide 13: Scalable Coder Including Color Space Prediction
Input
BT.709
Input
UHDTV
Base Layer
Encoding Loop
Enhancement Layer
Encoding Loop
Base Layer
Reference
Bitstream
Multiplex
Enhancement Layer
Reference
Color Space
Predictor
Compressed
Output

## Slide 14: Color Space scalable tests
Color Space scalability was tested in the following manner
Original source sequences in UHDTV color space were prepared
Resolution was unchanged to avoid conflating resolution scalable results
Sequences were coded in the following ways using main profile random access extended to support 10-bit data as needed.
  Base Layer HM6.1 JCT-VC sequences (BT.709)
  Single Layer HM6.1 UHDTV 10-bit encoding
  Scalable coding base on HM6.1 with bit difference prediction
  Scalable coding base on HM6.1 with cross color channel prediction

## Slide 15: Simulcast Comparison Example (RaceHorses)
The single layer is compared to the Base Layer + Cross Color Enhancement Layer in terms of BD rate. The luma channel shows an increase of 6.8% while the chroma channels each show a BD rate savings -9.7% and -38.0% respectively.

## Slide 16: Enhancement Layer Comparison Example (RaceHorses)
The two Enhancement Layers are compared, the Bit-Difference and the Cross Color prediction methods in terms of BD rate. The BD rates show reductions in all channels.

## Slide 17: Average Test Results
A summary of BD rate comparisons over a range of test sequences is shown below.
Comparing Single Layer and Base Layer + Enhancement Layer (Cross Color) indicates a BD rate of [Y,U,V] = [8.5%, -13.8%,-38.5%] averaged across test content.
Comparing the Enhancement Layers based on Bit-Depth or Cross Color prediction shows a BD rate of [Y,U,V] = [-34.1%, -36.7%,-53.2%] averaged across test content.

## Slide 18: Conclusions
Scalable video coding is beneficial to support both full HD and UHDTV content.
In addition to resolution, UHDTV also includes a color gamut and bit-depth transition.
The proposed method of color prediction gives improvement in the ability to predict UHDTV data from BT.709 data represented in different color spaces.
Cross Color prediction give a significant reduction in BD rate compared to bit-shift prediction ranging across test content.
We propose adopting the Cross Color prediction tool into future scalable HEVC design.

## Slide 19: Additional Prediction Examples
The following slides illustrate the relation between BT.709 and UHDTV data for sample original source images
During use in a scalable codec, the BT.709 source will actually be a reconstructed image potentially resulting in higher MSE values than reported here.

## Slide 20: BasketballDrive (Duplicate of Previous)

## Slide 21: Cactus

## Slide 22: Kimono

## Slide 23: ParkScene

## Slide 24: RaceHorses

## Slide 25: Traffic