## Slide 1: Region of interest (ROI) SEI message (JCTVC-K0247)
Gosel Dedeoglu and Madhukar Budagavi
Texas Instruments Inc.
Joint Collaborative Team on Video Coding (JCT-VC)
of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
11th Meeting: Shanghai, CN, 10–19 Oct. 2012

## Slide 2: Introduction
Region of interest (ROI) based video coding is used in practice to improve video quality in pre-determined regions of videos such as human faces, text, and graphical elements such as logos
ROI and ROI priority determination done by a content analysis block
QP modulated depending on ROI priority

## Slide 3: Cloud computing/video infrastructure - 1
Common to chain multiple encode-decode blocks to prepare video content for delivery to end-users in cloud computing/video infrastructure applications
Examples include, multipoint video conferencing, overlaying text or logos on top of existing video content, server based video stabilization and quality enhancement, trans-rating between bit-rate/quality options, and transcoding from one video standard to another
Issues: Intermediate encoders do not have readily available ROI information and cannot take advantage of it
(V-CA – content analysis block, V-Enc – Video enc, V-Dec – video dec)

## Slide 4: Cloud computing/video infrastructure - 2
Brute force solution:
Disadvantages:
  Need to include content analysis block in every intermediate node
  Also ROI estimation might degrade in coding chain since every round of re-encoding could introduce quality loss
(V-CA – content analysis block, V-Enc – Video enc, V-Dec – video dec)

## Slide 5: Proposed solution
Signal ROI information in SEI
Advantages
  ROI information is propagated to intermediate encoders
  Additional content analysis blocks not required in intermediate nodes

## Slide 6: ROI SEI message
roi_window_start_xpos: Specifies the starting x-position of the ROI in pixels.
roi_window_start_ypos: Specifies the starting y-position of the ROI in pixels.
roi_window_width: Specifies the width of the ROI in pixels.
roi_window_height: Specifies the height of the ROI in pixels
roi_priority: Specifies the priority for the ROI.
roi_type: Specifies type of ROI (0: Face, 1:Text, ..)
roi_label: Specifies the label for the ROI. roi_label can be used to track ROIs from one frame to another: for instance, if they are used to track a person’s face in the video sequence, the person’s face will be assigned the same label through the whole video sequence.