## Slide 1: JCTVC-K0249: AhG6 SAO offset coding for higher bit-depth video
<number>
Woo-Shik Kim, Madhukar Budagavi, Vivienne Sze
Texas Instruments Inc., USA
Notes: <number>

## Slide 2: SAO Offset Coding in HM-8.0
<number>
Offset range depends on internal bit-depth
Truncated unary binarization with bypass coding
offset value: binarized bins
0: 0
1: 10
2: 110
3: 1110
…
30: 1111111111111111111111111111110
31: 1111111111111111111111111111111
< 10 bit video >
offset value: binarized bins
0: 0
1: 10
2: 110
3: 1110
…
6: 1111110
7: 1111111
< 8 bit video>
Max 31 bins per offset, bypass coded
 | 8 bit video | 9 bit video | 10 bit and above
Offset range | [0, 7] | [0, 15] | [0, 31]
Number of max bins | 7 | 15 | 31
Notes: <number>

## Slide 3: SAO Offset Coding in HM-8.0
<number>
Maximum bin rate for SAO offset coding
  4K@60fps (3840x2176) assuming 16x16 LCU size
  4 offsets for each color component, 12 for each LCU
  729 Mbins/sec for SAO offset coding only
Reducing worst case bypass bin desirable, since bypass bins throughput could be around only 2 times that of context coded bins at typically used processor frequencies
Reducing number of SAO offset bins can help real-time implementation
Notes: <number>

## Slide 4: Proposed Method – First Approach
<number>
No change in Main profile (8 bit video)
For internal bit-depth larger than 8
  Prefix: truncated unary binarization as in HM-8.0 (cMax = 7)
  Suffix: fixed length binarization when offset is larger than 6
  All bypass coded
Max 12 bins for 10 bit and above
0: 0
1: 10
2: 110
3: 1110
…
6: 1111110
7: 111111100111
8: 111111101000
9: 111111101001
…
30: 111111111110
31: 111111111111
<Proposed, 10 bit>
0: 0
1: 10
2: 110
3: 1110
…
6: 1111110
7: 11111110
8: 111111110
9: 1111111110
…
30: 1111111111111111111111111111110
31: 1111111111111111111111111111111
<HM8, 10 bit>
Notes: <number>

## Slide 5: Proposed Method – Second Approach
<number>
No change in Main profile (8 bit video)
For internal bit-depth larger than 8
  Prefix: truncated unary (TU) binarization as in HM-8.0 (cMax = 7)
  Suffix: 0th exp-Golomb (EG0) binarization when offset is larger than 6
  All bypass coded
Max 16 bins for 10 bit and above
Use of existing binarization scheme
0: 0
1: 10
2: 110
3: 1110
…
6: 1111110
7: 11111110
8: 1111111100
9: 1111111101
…
30: 1111111111101000
31: 1111111111101001
0: 0
1: 10
2: 110
3: 1110
…
6: 1111110
7: 11111110
8: 111111110
9: 1111111110
…
30: 1111111111111111111111111111110
31: 1111111111111111111111111111111
<HM8, 10 bit>
<Proposed, 10 bit>
Notes: <number>

## Slide 6: Experimental Results
<number>
No change for Main
No coding loss in HE10
TU+FL | Class A-E |  |  | Class F |  | 
 | Y | Cb | Cr | Y | Cb | Cr
AI-HE10 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RA-HE10 | 0.0% | 0.1% | 0.0% | -0.1% | 0.0% | -0.1%
LB-HE10 | 0.0% | 0.1% | 0.0% | -0.2% | 0.0% | -1.2%
LP-HE10 | 0.0% | -0.1% | -0.1% | -0.2% | -0.3% | 0.1%
TU+EG0 | Class A-E |  |  | Class F |  | 
 | Y | Cb | Cr | Y | Cb | Cr
AI-HE10 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RA-HE10 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
LB-HE10 | 0.0% | -0.1% | 0.0% | -0.2% | -0.5% | -1.6%
LP-HE10 | 0.0% | -0.1% | 0.0% | -0.2% | -0.3% | -0.3%
Notes: <number>

## Slide 7: Conclusions
<number>
Desirable to reduce worst case number of SAO offsets bins
Proposed SAO offset coding for internal bit-depth larger than 8
  TU+FL : max number of bin is 12
  TU+EG0 : uses existing binarization scheme with max number of bin 16
No change for Main profile
Maximum number of bin is reduced from 31 to 12 (TU+FL) or 16 (TU+EG0)
No coding loss in HE10
Notes: <number>