## Slide 1: Coding Interlaced Video Coding with HEVC

## Slide 2: Interlaced Coding using HEVC
HM 8.0 based coding
  HEVC frame
  HEVC field
  HEVC adaptive – Sequence Adaptive Field Frame (SAFF)
AVC JM18.4 based coding, for reference
  MBAFF

## Slide 3: Test Materials
Provided by NBC Universal, under NDA
  1920x1080i @ 30 frames/sec
  4:2:0 (converted from 4:2:2 using TM5 chroma-filter)
List of materials used
  Cheer1, 300 frames, camera motion + dancing
  Cheer2, 299 frames, camera motion + dancing
  Cheer3, 300 frames, camera motion + dancing
  Cheer4, 300 frames, mixed motion/still
  Mad1, 300 frames, 3:2 pulldown, mixed motion/still
  Music1, 208 frames, little camera motion, dancing

## Slide 4: Experiment Setup
HM 8.0
  Based on RA-Main test condition
  GOP (closed) size 32 for frame coding
  GOP (closed) size 64 for field coding
  Field/frame adaptive: per GOP decision of frame or field coding
AVC JM18.4 based coding, for reference
  MBAFF
  GOP size 32 frames, open

## Slide 5
Simulation results

## Slide 6: Sequence Adaptive Field-Frame
In HEVC, for each GOP, BD-rate was computed comparing frame coding with field coding. The best mode (in BD-rate sense) is tabulated below for each GOP.
GOP | Cheer1 | Cheer2 | Cheer3 | Cheer4 | Mad1 | Music1
0 | field | field | field | field | field | frame
1 | field | field | field | field | field | frame
2 | field | field | field | field | field | frame
3 | field | field | field | frame | field | frame
4 | field | field | field | frame | field | frame
5 | field | field | field | field | field | frame
6 | field | field | field | field | field | field
7 | field | field | field | field | frame | 
8 | field | field | field | field | frame | 
9 | field | field | field | field | frame | 

## Slide 7: HEVC Frame vs HEVC Field
 | BD-rate (piecewise cubic) |  | 
Clip | Y | U | V
Cheer1 | 76.8% | 62.7% | 74.6%
Cheer2 | 98.7% | 115.9% | 117.3%
Cheer3 | 88.5% | 98.2% | 94.4%
Cheer4 | 14.2% | -5.1% | -5.9%
Mad1 | 48.9% | 33.9% | 15.6%
Music1 | -12.7% | -49.1% | -51.0%
Average | 52.4% | 42.8% | 40.8%

## Slide 8: HEVC Field vs HEVC Adaptive
 | BD-rate (piecewise cubic) |  | 
Clip | Y | U | V
Cheer1 | 0.0% | 0.0% | 0.0%
Cheer2 | 0.0% | 0.0% | 0.0%
Cheer3 | 0.0% | 0.0% | 0.0%
Cheer4 | 0.1% | 5.7% | 6.0%
Mad1 | 4.6% | 8.0% | 20.6%
Music1 | 15.7% | 92.2% | 99.8%
Average | 3.4% | 17.6% | 21.0%

## Slide 9: HEVC Frame vs HEVC Adaptive
 | BD-rate (piecewise cubic) |  | 
Clip | Y | U | V
Cheer1 | 76.8% | 62.7% | 74.6%
Cheer2 | 98.7% | 115.9% | 117.3%
Cheer3 | 88.5% | 98.2% | 94.4%
Cheer4 | 14.2% | 0.2% | -0.5%
Mad1 | 54.6% | 43.2% | 37.6%
Music1 | 1.0% | -2.4% | -2.4%
Average | 55.6% | 53.0% | 53.5%

## Slide 10: HEVC Field vs JM 18.4 MBAFF
 | BD-rate (piecewise cubic) |  | 
Clip | Y | U | V
Cheer1 | -40.3% | -45.8% | -43.2%
Cheer2 | -41.6% | -47.4% | -43.2%
Cheer3 | -42.5% | -41.8% | -41.8%
Cheer4 | -25.3% | -17.5% | -20.2%
Mad1 | -20.6% | -31.4% | -25.5%
Music1 | -5.2% | -2.1% | 9.4%
Average | -29.3% | -31.0% | -27.4%

## Slide 11: HEVC Frame vs JM 18.4 MBAFF
 | BD-rate (piecewise cubic) |  | 
Clip | Y | U | V
Cheers1 | 5.5% | -11.0% | -0.3%
Cheers2 | 15.9% | 14.2% | 24.0%
Cheers3 | 8.9% | 16.5% | 14.3%
Cheers4 | -14.1% | -20.6% | -23.7%
Mad1 | 20.5% | -3.0% | -7.7%
Music1 | -15.5% | -47.9% | -43.4%
Average | 3.5% | -8.6% | -6.1%

## Slide 12: HEVC Adaptive vs JM 18.4 MBAFF
 | BD-rate (piecewise cubic) |  | 
Clip | Y | U | V
Cheers1 | -40.3% | -45.8% | -43.2%
Cheers2 | -41.6% | -47.4% | -43.2%
Cheers3 | -42.5% | -41.8% | -41.8%
Cheers4 | -25.3% | -21.6% | -24.3%
Mad1 | -23.2% | -34.7% | -35.4%
Music1 | -16.4% | -46.9% | -42.3%
Average | -31.5% | -39.7% | -38.4%

## Slide 13
Closed-GOP vs Open-GOP HEVC
Additional tests show that Closed-GOP use 4.2% more bits than Open-GOP for field coding and 5.2% more for frame coding.

## Slide 14: Conclusions
Coding efficiency gain of HEVC-SAFF over AVC-MBAFF is content-dependent.
  content with high camera motion shows higher gain for HEVC SAFF
  content with low camera motion and moderate scene motion shows lower gain for HEVC SAFF
Luma BD-rate gain varies from 16.4% to 42.5%.
Hints that there is room for improving performance of HEVC on interlaced content with interlaced-specific tools.
Recommend further study of HEVC with interlaced video.