## Slide 1: AHG7: The performance of extended chroma mode for non 4:2:0 format
J. Park
J. Kim
JCTVC-K0253

## Slide 2: Introduction
Intra chroma prediction : IntraFromLuma
  For HEVC, IntraFromLuma(LM chroma) mode was adopted as one of intra chroma prediction modes
  Principle of LM chroma for 4:2:0 sampling:
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 3: Proposed Method (I)
Extended intra chroma prediction mode for non 4:2:0 sampling
  We propose to use IntraFromLuma(LM chroma) mode for non 4:2:0 sampling
  Adaptation for 4:4:4 sampling
    All of luma samples are used
  Adaptation for 4:2:2 sampling
    Luma samples involved in the process are downsampled horizontally

## Slide 4: Proposed Method (I)
  4:4:4 sampling
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 5: Proposed Method (I)
  4:2:2 sampling
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 6: Proposed Method (II)
We propose that the parameters are derived every CU and used for every TU in the entire CU
chroma reconstruction
for T0
Parameter
Calculation for CU
TU0
TU1
TU2
TU3
chroma reconstruction
for T1
chroma reconstruction
for T2
chroma reconstruction
for T3
chroma reconstruction
for T0
Parameter
Calculation for T0
chroma reconstruction
for T1
Parameter
Calculation for T1
chroma reconstruction
for T2
Parameter
Calculation for T2
chroma reconstruction
for T3
Parameter
Calculation for T3
<Previous design in HEVC>
<Proposed design>

## Slide 7: Proposed Method (II)
Proposed method reduces number of parameter derivation in a CU
Proposed method may reduce total number of computation in a CU
 |  | Anchor (TU based derivation) | Proposed (CU based derivation)
Number of parameter derivation |  | 4 | 1
L & C | Addition | 4*(32*2) + 4*(32*2) | 64*2 + 64*2
LL & LC | Addition | 4*(32*2) + 4*(32*2) | 64*2 + 64*2
 | multiplication | 4*(32*2) + 4*(32*2) | 64*2 + 64*2
Constant computation | Addition | 4*14 | 14
 | multiplication | 4*5 | 5
 |  | Addition 1080 multiplication 532 | Addition 526 multiplication 261
Computation required for parameter derivation in each CU when 64x64CU with four 32x32 TUs in the case of 4:4:4 sampling
- Note : shift operation is not counted
 |  | Anchor (TU based derivation) | Proposed (CU based derivation)
Number of parameter derivation |  | 256 | 1
L & C | Addition | 256*(4*2) + 256*(4*2) | 64*2 + 64*2
LL & LC | Addition | 256*(4*2) + 256*(4*2) | 64*2 + 64*2
 | multiplication | 256*(4*2) + 256*(4*2) | 64*2 + 64*2
Constant computation | Addition | 256*14 | 14
 | multiplication | 256*5 | 5
 |  | Addition 11776 multiplication 5376 | Addition 526 multiplication 261
Computation required for parameter derivation in each CU when 64x64CU with 256 4x4 TUs in the case of 4:4:4 sampling
- Note : shift operation is not counted

## Slide 8
Experimental Results
We appreciate KDDI for cross checking.
Also we appreciate BBC for sharing the test sequences!
Performance of proposed methods
  Implemented on top of HM8.0_dev_ahg7
  For proposed (I), anchor is HM8.0_dev_ahg7
  For proposed (II), anchor is HM8.0_dev_ahg7+LMchroma on
 |  |  | AIMAIN | AIHE10 | RAMAIN | RAHE10 | LDMAIN | LDHE10
Proposed (I) :HM8._dev_ahg7 + LMon | 4:2:2 | Y | -2.5% | -2.8% | -1.2% | -1.3% | -0.3% | -0.3%
 |  | U | -5.3% | -5.8% | -6.9% | -7.7% | -2.5% | -3.0%
 |  | V | -4.4% | -5.0% | -4.1% | -4.6% | -1.7% | -2.2%
 | 4:4:4 | Y | -2.8% | -3.1% | -1.4% | -1.5% | -0.4% | -0.4%
 |  | U | -4.1% | -4.4% | -4.4% | -4.9% | -1.5% | -1.8%
 |  | V | -4.5% | -5.1% | -4.0% | -4.5% | -1.7% | -1.9%
Proposed (II) :HM8._dev_ahg7 + LMon + CU-based parameter derivation | 4:2:2 | Y | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
 |  | U | -0.3% | -0.3% | -0.3% | -0.3% | -0.1% | -0.2%
 |  | V | -0.3% | -0.3% | -0.2% | -0.2% | -0.2% | -0.1%
 | 4:4:4 | Y | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
 |  | U | 0.0% | 0.0% | 0.1% | -0.1% | 0.0% | 0.0%
 |  | V | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.3%

## Slide 9: Conclusion
We proposed including of extended intra chroma prediction (LM chroma ) mode for non 4:2:0 sampling
We proposed CU-based parameter calculation to reduce total number of calculation and total number of memory access in average.
  It may reduce total number of parameter calculation and memory access in a CU.
  It also showed small gains since it used bigger test set for calculating parameters.