## Slide 1: JCTVC-K0262 AHG9: NAL Unit Priority SEI Message
Eun-Seok Ryu, Yan Ye, Yuwen He, Yong He
InterDigital Communications, LLC
11th JCT-VC meeting, October 10-19, 2012

## Slide 2: Problem statement
  NAL unit priority information is essential for QoS handling for video applications such as streaming
  Unequal Error Protection
  Packet dropping for bandwidth adaptation
  Differentiated service by smart router, etc
Currently in WD8, NAL header NAL header has some priority indication: 3-bit temporal_id
Observation:
  video streaming server and media-aware router need high-level syntax to indicate NALU priority of encoded bitstream
  pictures in the same temporal level can still have different priorities
  Need for further priority differentiation
nal_unit_header( ) { | Descriptor
forbidden_zero_bit | f(1)
nal_unit_type | u(6)
nuh_reserved_zero_6bits | u(6)
nuh_temporal_id_plus1 | u(3)
} | 

## Slide 3: Hierarchical B prediction
In one intra period of 32 pictures, Position A pictures are referenced 12 times, while Position B pictures are referenced 16 times
Packet loss at Position A and at Position B has different implication on error propagation

## Slide 4: Simulation Results
Test settings
RA in common test condition
Drop 1 picture per intra period
HM6.1
Observation
Clear difference in performance between packet loss at Position A and at Position B
upper: with same TID, lower: with different TID
As much as 3dB

## Slide 5: Proposed SEI Message Syntax for NAL Unit Priority
SEI payload syntax
Definition of a priority_info for SEI
Indicates the priority of following NAL units until the next NALU priority SEI message is present
sei_payload( payloadType, payloadSize ) { | Descriptor
if( payloadType = = 0 ) | 
buffering_period( payloadSize ) | 
……….. | 
else if( payloadType = = 133) | 
priority_info( payloadSize ) | 
……….. | 
priority_info (payloadSize ) { | Descriptor
priority_id | u(4)
Reserved | u(4)
} | 

## Slide 6: Conclusions
Observation:
  Video streaming server and media-aware router need high-level syntax to indicate NALU priority without parsing video bitstream
  There is need to differentiate packet priorities within the same temporal layer
Proposed SEI message syntax for NAL unit priority
Recommend to adopt