## Slide 1: INTER-LAYER SPS PREDICTION FOR HEVC EXTENSIONS
JCTVC-K0277
Thomas Rusert (Ericsson)

## Slide 2: Summary
Following up on JCT3V-A0021
Observation: SPS-related redundancy in HEVC extensions
  Separate SPS per layer necessary if some SPS parameters are different
  Many SPS parameters are identical across layers
  Duplicating parameters in several SPSs implies redundancy
Proposed solution: Inter-layer SPS prediction
  Option for SPSs not associated with the base layer
  Predicted SPS parameters are inherited from active SPS in reference layer
Benefit of proposed solution: Bit savings
  SPS size under common coding conditions: ~300 bits
  SPS size can be several 1000 bits in some cases

## Slide 3: Proposed SPS Prediction
Additional syntax in SPS with layer_id > 0
  Indication whether SPS prediction is used
  Reference layer for SPS prediction
  Indication which groups of parameters are predicted
Parameter inheritance at SPS activation time
  Syntax elements not present in the SPS are inherited from the active SPS in the reference layer

## Slide 4: Proposed Syntax
seq_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
sps_max_sub_layers_minus1 | u(3)
sps_reserved_zero_bit | u(1)
profile_and_level( 1, sps_max_sub_layers_minus1 ) | 
seq_parameter_set_id | ue(v)
if( layer_id > 0 ) { */ not base layer */ | 
ref_layer_present_flag | u(1)
if( ref_layer_present_flag = = 1 ) { | 
delta_ref_layer_id_minus1 | ue(v)
rep_format_inheritance_flag | u(1)
coding_param_inheritance_flag | u(1)
ref_pic_sets_inheritance_flag | u(1)
} | 
} | 
if( rep_format_inheritance_flag = = 0 ) { | 
… | 

## Slide 5: Proposed Semantics
ref_layer_present_flag equal to 1 indicates that sequence parameter set prediction is used. If ref_layer_present_flag is not present, it is inferred to be equal to 0.
delta_ref_layer_id_minus1 + 1 specifies the difference of the value of layer_id and the value of layer_id for the reference layer used for sequence parameter set prediction. The value of delta_view_ref_layer_id_minus1 shall be in the range of 0 to layer_id - 1, inclusive.
rep_format_inheritance_flag equal to 1 indicates that representation format related parameters are inherited from the sequence parameter set active for the layer that has layer_id equal to layer_id - delta_ref_layer_id_minus1 - 1. If rep_format_inheritance_flag is not present, it is inferred to be equal to 0.
coding_param_inheritance_flag equal to 1 indicates that coding algorithm related parameters are inherited from the sequence parameter set active for the layer that has layer_id equal to layer_id - delta_ref_layer_id_minus1 - 1. If coding_param_inheritance_flag is not present, it is inferred to be equal to 0.
ref_pic_sets_inheritance_flag equal to 1 indicates that reference parameter sets are inherited from the sequence parameter set active for the layer identified by layer_id equal to layer_id - delta_ref_layer_id_minus1 - 1. If ref_pic_sets_inheritance_flag is not present, it is inferred to be equal to 0.

## Slide 6: Additional Text For SPS Activation
When a sequence parameter set RBSP is activated for a layer having layer_id equal to LId and delta_ref_layer_id_minus1 is present in the sequence parameter set RBSP, the values of all sequence parameter set syntax elements for the layer having layer_id equal to LId - delta_view_ref_layer_id_minus1 - 1 not present in the sequence parameter set RBSP that is activated for the layer having layer_id equal to LId are inferred to be active for the layer having layer_id equal to LId.
When a sequence parameter set RBSP is active for the layer having layer_id equal to LId and delta_ref_layer_id_minus1 is present in the sequence parameter set RBSP and the sequence parameter set active for the layer with layer_id equal to LId – delta_view_ref_layer_id_minus1 – 1 is deactivated, then the sequence parameter set RBSP active for the layer having layer_id_plus1 equal to LId shall be deactivated by the activation of another sequence parameter set RBSP for that layer.

## Slide 7: Example 1: 2 Layers
Decoder stores
  SPS RBSPs
  One set of active SPS parameters for each decoded layer
sps_id=0
sps_id=1
sps_id=2
sps_id=3

## Slide 8: Example 2: 3 Layers
sps_id=0
sps_id=0
sps_id=1
sps_id=1
sps_id=2
sps_id=3

## Slide 9: Example 3: 3 Layers
sps_id=0
sps_id=1
sps_id=2
sps_id=3
sps_id=4
sps_id=5

## Slide 10: Bitstream Constraint
When a “short SPS” is active and the corresponding source for SPS prediction is deactivated, then the short SPS shall be deactivated
sps_id=0
sps_id=1
sps_id=2
sps_id=2