## Slide 1: Comparison of Compression Performance of HEVC Draft 8 with AVC High Profile and Performance of HM8.0 with Different Delay Characteristics
Bin Li, Gary J. Sullivan, Jizheng Xu
University of Science and Technology of China
Microsoft Corp.

## Slide 2: Performance Comparison
HEVC Draft 8 (HM-8.0)
  HM-8.0 Main
AVC High Profile (JM-18.4)
  Almost unchanged when compared with JM-18.3
PNSR based objective measurement
Further study of JCTVC-G399, JCTVC-H0360, JCTVC-I409, JCTVC-J0236

## Slide 3: AVC High Profile vs. HEVC Draft 8 Main Profile
 | All Intra | Random Access | Low Delay
Class A | −23.3% | −36.9% | 
Class B | −22.6% | −39.5% | −41.2%
Class C | −20.0% | −30.7% | −32.7%
Class D | −16.7% | −28.7% | −30.2%
Class E | −28.6% |  | −43.2%
Class F | −28.2% | −31.0% | −34.6%
Average | −23.0% | −33.7% | −36.3%
Average without F | −21.9% | −34.3% | −36.7%

## Slide 4: HM-8.0 Main Profile with Different Delay Characteristics
 | LDP Vs. LDB | LDB Vs. RA | RA Vs. Hier-B | LDB Vs. Hier-B
Class A |  |  | −8.9% | 
Class B | −11.0% | −10.7% | −11.5% | −21.3%
Class C | −6.8% | −13.4% | −6.4% | −19.1%
Class D | −6.8% | −16.5% | −7.9% | −22.9%
Class E | −8.2% |  |  | 
Class F | −3.6% | 74.8% | −30.2% | −11.9%
Average | −7.4% | 7.4% | −12.9% | −18.9%
Average without F | −8.4% | −13.3% | −8.8% | −21.1%

## Slide 5: Performance of QP Refinement
 | HM RA | HM LDB | JM RA | JM LD
Class A | −2.2% |  | −2.6% | 
Class B | −2.2% | −1.3% | −2.3% | −2.3%
Class C | −2.6% | −1.4% | −4.1% | −2.7%
Class D | −2.3% | −1.4% | −3.2% | −2.7%
Class E |  | −2.6% |  | −5.5%
Class F | −2.3% | −1.5% | −3.7% | −3.1%
Average | −2.3% | −1.6% | −3.1% | −3.1%
Average without F | −2.3% | −1.6% | −3.0% | −2.3%

## Slide 6: JM Vs. HM with QP Refinement
 | Random Access | Low Delay
Class A | −36.4% | 
Class B | −39.1% | −40.7%
Class C | −29.3% | −31.8%
Class D | −27.9% | −29.3%
Class E |  | −41.4%
Class F | −29.9% | −33.5%
Average | −32.8% | −35.3%
Average without F | −33.5% | −35.8%