## Slide 1: JCTVC-K0302 AHG7: On processing 4:2:2 chroma format
R&D
© BBC MMXII
Andrea Gabriellini and Marta Mrak
BBC Research and Development

## Slide 2: On processing 4:2:2 chroma format
To support compression of 4:2:2 format, the AHG7 software uses non-square transforms and transform blocks
  Additional supporting tools required - as introduced in AHG7 software
  Different variants of the tools only compared with each other
  Additional experiment designed to evaluate efficiency of 4:2:2 support

## Slide 3: Experiment setup
4:2:2
U, V 2
[1, 3, 3, 1]
4:4:4
HM-8.0-dev-ahg7
Encoder
HM-8.0-dev-ahg7
Decoder
4:4:4
4:2:2
U, V 2
[1, 2, 1]
Upsampled 4:2:2 videos encoded with AHG7 branch operating on 4:4:4 samples
After decoding, downsampling to 4:2:2 is used
  PSNR computed at this point

## Slide 4: Results for 4:2:2 sequences - comparison with JM
 | All Intra HE10 |  | 
 | Y | U | V
Kimono | -28.0% | -30.9% | -37.5%
Parkscene | -11.7% | -24.9% | -26.1%
Birds-in-cage | -29.0% | -35.7% | -47.9%
Ducks-and-legs | -6.8% | -21.9% | -25.9%
Traffic | -19.6% | -27.9% | -32.4%
Crowd-run | -11.2% | -25.6% | -26.9%
Old-town | -10.8% | -28.3% | -34.0%
Seeking | -11.3% | -27.4% | -28.3%
Overall | -16.0% | -27.8% | -32.4%
Enc Time[%] | 68% |  | 
Dec Time[%] | 147% |  | 
 | Low delay B HE10 |  | 
 | Y | U | V
Kimono | -50.0% | -34.3% | -36.4%
Parkscene | -39.8% | -40.2% | -40.2%
Birds-in-cage | -73.9% | -74.5% | -75.4%
Ducks-and-legs | -41.8% | -38.4% | -46.8%
Traffic | -44.6% | -43.2% | -50.9%
Crowd-run | -22.5% | -30.8% | -30.9%
Old-town | -53.7% | -58.2% | -58.0%
Seeking | -31.7% | -35.8% | -36.3%
Overall | -44.8% | -44.4% | -46.8%
Enc Time[%] | 70% |  | 
Dec Time[%] | 116% |  | 
 | All Intra HE10 |  | 
 | Y | U | V
Kimono | -24.3% | -33.4% | -40.2%
Parkscene | -9.3% | -19.1% | -16.0%
Birds-in-cage | -27.0% | -32.8% | -51.6%
Ducks-and-legs | -6.7% | -7.5% | -16.4%
Traffic | -16.6% | -23.9% | -29.6%
Crowd-run | -9.9% | -10.3% | -14.0%
Old-town | -12.2% | -18.0% | -30.0%
Seeking | -10.7% | -16.7% | -21.0%
Overall | -14.6% | -20.2% | -27.3%
Enc Time[%] | 79% |  | 
Dec Time[%] | 187% |  | 
 | Low delay B HE10 |  | 
 | Y | U | V
Kimono | -45.3% | -50.6% | -47.5%
Parkscene | -33.9% | -47.1% | -40.9%
Birds-in-cage | -68.4% | -77.6% | -79.2%
Ducks-and-legs | -35.2% | -30.5% | -42.2%
Traffic | -37.9% | -48.8% | -56.8%
Crowd-run | -19.1% | -29.2% | -31.2%
Old-town | -51.6% | -67.6% | -69.2%
Seeking | -28.5% | -38.8% | -43.3%
Overall | -40.0% | -48.8% | -51.3%
Enc Time[%] | 77% |  | 
Dec Time[%] | 143% |  | 
HM-8.0-dev-ahg7 4:2:2 vs JM18.4
HM-8.0-dev-ahg7 4:2:2 to 4:4:4 vs JM18.4

## Slide 5: Results for 4:2:2 sequences - comparison with HM (AHG7)
BD-rates difficult to interpret because of the interpolation involved in its computation
Tested 4:2:2 to 4:4:4 format conversion has worse performance at high bit-rates; PSNR gains in chroma components occurs in some points, with some losses in luma
  Performance is not consistent, pointing to possible problems in the AHG4 software (either 4:2:2 or 4:4:4 support)