## Slide 1: JCTVC-K0315 On default scaling list values
R&D
© BBC MMXII
Matteo Naccari, Marta Mrak, Andrea Gabriellini
BBC Research and Development

## Slide 2: Default scaling lists: main principles
The HEVC standard allows using scaling lists (a.k.a. quantisation matrices)
Some default values are provided:
  Derived using a simple model of the Human Visual System (HVS) and proposed in JCTVC-G880
  They model the HVS property: i.e. low sensitivity to the distortion introduced in high spatial frequencies
4×4 scaling list obtained with theHVS model used in G880
16 | 16 | 17 | 21
16 | 17 | 20 | 25
17 | 20 | 30 | 41
21 | 25 | 41 | 70
12 | 12 | 13 | 16
12 | 13 | 15 | 19
13 | 15 | 22 | 31
16 | 19 | 31 | 53
4×4 default scaling list for the luma component in intra coded blocks

## Slide 3: Default scaling lists: do they improve the perceived quality?
HEVC default scaling lists should:
  Improve the perceived quality for a given target rate (or dually)
  Reduce the coded rate for a given perceptual quality level
At the last JCT-VC meeting in Stockholm some concerns were expressed about the default scaling lists. From the meeting notes;
  “…The question was also raised how suitable the current DCT default matrices are, as in practice most implementers would use own matrices with adaptation to the video material characteristics…”
An experiment has been designed to assess the performance brought by the default scaling lists both in objective and subjective terms
  JCT-VC videos coded with HM-8.0 and default scaling lists for Main configurations
  Additional QP values have been tested: 29, 30, 31, 33, 34, 35 and 36
  The coded videos are compared with the HM-8.0 anchors
In this proposal:

## Slide 4: Results: objective evaluation (BD-rates)
A bitrate distribution between luma and chroma is observed:
 | All Intra Main |  | 
 | Y | U | V
Class A | 0.3% | 0.1% | 0.8%
Class B | 1.4% | -1.3% | -1.5%
Class C | 0.9% | 0.1% | 0.0%
Class D | 0.9% | -0.1% | -0.1%
Class E | 0.4% | -0.9% | -1.0%
Overall | 0.8% | -0.4% | -0.4%
 | 0.8% | -0.4% | -0.4%
Class F | 0.5% | -0.1% | -0.1%
 | Random Access Main |  | 
 | Y | U | V
Class A | 0.2% | 1.1% | 2.4%
Class B | 0.5% | -1.3% | -1.5%
Class C | 0.8% | -0.2% | -0.2%
Class D | 0.9% | -0.6% | -0.7%
Class E |  |  | 
Overall | 0.6% | -0.3% | -0.1%
 | 0.6% | -0.3% | -0.1%
Class F | 0.5% | -0.1% | 0.0%
 | Low delay B Main |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.4% | -1.8% | -2.3%
Class C | 0.9% | -0.8% | -1.1%
Class D | 0.7% | -1.0% | -0.8%
Class E | 0.4% | -1.2% | -0.7%
Overall | 0.6% | -1.2% | -1.3%
 | 0.6% | -1.2% | -1.4%
Class F | 0.6% | 0.1% | -0.3%

## Slide 5: Results: subjective evaluation
An informal subjective viewing have been organised at the BBC R&D premises
  5 experts took part to the experiment
  Side-by-side comparison w.r.t. to the HM-8.0 anchors in a light controlled viewing room
  Further inspection is done by stopping the video player onto some frames
Coded contents selected according to their level of texture, motion and sharp details:
  Kimono, Cactus, Park-Scene, China-Speed, Basketball-Drive, Kristen-and-Sara and Slide-Editing
  Additional QP values also tested
Some slight quality differences were noticed only on a frame-by-frame comparison (not in play out)
Quality differences may be due to RDO search with use of default scaling lists

## Slide 6: Conclusions
An experiment has been designed to assess the performance and suitability of default scaling lists (motived also from observations provided at the previous meeting)
From the informal subjective viewing seems that default scaling lists bring a minimal contribution to the overall video quality
Some high bitrate reductions are observed for particular coding conditions (QP 22)
Some possible factors which contribute to the limited performance:
  The HVS model considers JPEG quantisation rather than predictive one
  Model parameters tuned onto different image resolutions than the ones considered for HEVC