## Slide 1: JCTVC_K0353 HEVC encoding of deinterlaced sequences: a preliminary study
  Z. Agyo, J.M. Thiesse, J. Viéron, P. Larbier

## Slide 2
Deinterlacing interlaced sequences before HEVC encoding have been suggested during previous meetings:
  What is its efficiency?
This contribution reports an assessments of encoding after deinterlacing vs field coding and vs AVC
Introduction

## Slide 3
HEVC encoding using HM8.0 with field GOP structure defined in JCTVC-K0216 compared to AVC encoding (MBAFF + PAFF)
Four HD interlaced sequences tested (100 frames)
Three deinterlacers tested: ATEME’s Deinterlacers and two well-known deinterlacers.
Experimental settings
 | H.264/AVC | HEVC Field | HEVC deinterlaced frame
FrameRate | 30 | 60 | 60
SourceHeight | 1088 | 544 | 1088
FrameToBeEncoded | 200 | 100 | 100
IntraPeriod | 48 | 96 | 96
GOPSize | 8 | 16 | 8
Experiments configuration

## Slide 4
Performances are highly content-dependent
Encoding of deinterlaced sequences is more efficient for static sequences
Results: HEVC deinterlaced vs HEVC field (1)
 | ATEME's Deinterlacer |  |  | Deinterlacer 1 |  |  | Deinterlacer 2 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Church | 31,0 | -42,2 | -39,0 | 76,1 | -37,5 | -36,9 | 0,2 | -42,8 | -41,5
Marching in | -18,5 | -69,9 | -73,8 | -14,2 | -61,9 | -65,5 | -20,5 | -55,5 | -58,0
Walk through the square | -4,6 | -53,5 | -54,8 | -14,4 | -41,8 | -42,3 | -27,6 | -31,5 | -33,0
Whale show | 6,9 | -60,0 | -59,7 | 2,2 | -58,6 | -59,2 | -0,6 | -53,2 | -52,3
Overall | 3,71 | -56,42 | -56,85 | 12,42 | -49,97 | -50,99 | -12,12 | -45,74 | -46,20
Encoding of deinterlaced sequences vs Field coding with re-interlacing

## Slide 5
“Without” taking deinterlacing degradation into account, deinterlaced encoding is better than field coding
ATEME’s deinterlacer allows better “intrinsic coding” efficiency
Results: HEVC deinterlaced vs HEVC field (2)
 | ATEME's Deinterlacer |  |  | Deinterlacer 1 |  |  | Deinterlacer 2 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Church | -57,4% | -48,5% | -51,7% | -21,9% | -49,1% | -51,2% | -40,9% | -60,7% | -64,6%
Marching in | -60,8% | -56,1% | -55,8% | -40,8% | -68,8% | -69,7% | -44,7% | -75,3% | -74,2%
Walk through the square | -42,9% | -32,2% | -33,3% | -27,3% | -46,4% | -47,6% | -34,1% | -42,4% | -42,6%
Whale show | -23,6% | -49,9% | -55,3% | -19,4% | -60,8% | -62,9% | -20,6% | -70,0% | -70,8%
Overall | -46,18% | -46,67% | -49,04% | -27,35% | -56,28% | -57,84% | -35,07% | -62,09% | -63,04%
Encoding of deinterlaced sequences vs Field coding without re-interlacing

## Slide 6
Results: HEVC deinterlaced vs AVC
 | ATEME's Deinterlacer |  |  | Deinterlacer 1 |  |  | Deinterlacer 2 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Church | -51,3 | -80,0 | -78,8 | -34,4 | -78,3 | -78,1 | -63,8 | -80,0 | -79,6
Marching in | -60,1 | -89,8 | -91,0 | -64,1 | -87,0 | -88,3 | -65,2 | -83,7 | -84,9
Walk through the square | -47,1 | -74,4 | -75,2 | -52,5 | -67,7 | -67,9 | -59,8 | -61,8 | -62,7
Whale show | -9,6 | -48,9 | -44,3 | -13,4 | -47,7 | -44,3 | -16,2 | -46,2 | -42,5
Overall | -42,01 | -73,25 | -72,29 | -41,08 | -70,16 | -69,67 | -51,24 | -67,93 | -67,42
HEVC encoding of deinterlaced sequences vs AVC encoding of interlaced sequences

## Slide 7
Deinterlacing and its encoding is a tricky topic
Better compression is achieved by encoding deinterlaced sequences (vs field coding) when deinterlacing degradation is not considered
Significant performances against AVC have been observed (40%)
Further study will be performed to assess coding efficiency of all the loop from captation to visualization
Conclusion