## Slide 1: JCTVC-K0363 Study of Software Model for Scalable HEVC Extension in JCTVC-K0345
PoLin Lai, Shan Liu, and Shawmin Lei (MediaTek)
Presented by PoLin Lai
JCT on 3D Video Coding Extension Development
Oct, 2012

## Slide 2: Highlights
The high-level framework, i.e. multiple layers, hooks for scalability, difference-domain coding, is from JCTVC-K0045 (macro: K0045)
Encoding process:
  For JCTVC-K0345, within each GOP
    First, encode ALL pictures in the Base Layer (BL)
    Then , encode pictures in the Enhancement Layer (EL)
  An alternative approach is to encode collocated BL/EL-pairs together in GOP
Features (the “meat”) for the following are implemented:
  Can be tracked by individual or combination of macros
  Inter-layer texture prediction: Intra-BL Mode
  Inter-layer syntax prediction: Merge / AMVP, Inter-BL Mode
  Difference-domain coding: Diff-INTRA, Diff-INTER
  Modified deblocking considering Diff.
Notes:     Problem and proposeVSP off, finding inter-view reference without warping

## Slide 3: Inter-layer Texture Prediction
Intra-BL mode (K0045_Intra_BL)
  Extend SVC Intra-BL mode to all BL blocks, i.e. multi-loop
  Upsampled reconstructed BL samples as predictor.
  Residual of the CU are coded as HEVC’s INTER residual
  Prediction mode set to INTRA DC (K0045_Intra_BL_PredModeDC)
Estimated performance
  In principle Intra-BL similar to JCTVC-K0038
  Results from JCTVC-K0038, EL-Only Target rate:
  AI, 2X 28.5%, 1.5X 48.4%
  RA, 2X 17.6%, 1.5X 37.8%
Notes: VSP_skip and others

## Slide 4: Inter-layer Syntax Prediction (1/2)
Modified AMVP (K0045_InterLayerMotionPred)
  Additional inter-layer motion vector predictor (IL)
  Place it at the beginning of the candidate list
Modified Merge (K0045_InterLayerMotionPred + K0042_MERGE)
  Co-located BL Merge flag = 0: Additional candidate from BL
  Co-located BL Merge flag = 1: Same candidate list as HEVC
  Reordering process may be invoked. [Refer to JCTVC-K0345 for details]
Performance
  Can be tested by disabling BOTH K0045_InterLayerMotionPred, K0042_MERGE
Notes: VSP_skip and others

## Slide 5: Inter-layer Syntax Prediction (2/2)
Inter-BL Mode (K0045_Inter_BL)
  Not a commonality among CfP proposals [BoG JCTVC-K0354]
  At CU level, all prediction parameters are inferred from co-located BL
  Details in JCTVC-K0345
  When no motion vectors available in BL for a sub-partition, switch to inter-layer INTRA-picture prediction for that sub-partition (K0042_Inter_BL_SwitchToIntra)
Performance
  Can be tested by disabling K0045_Inter_BL
Notes: VSP_skip and others

## Slide 6: Difference-domain Coding
Encode difference picture as a texture picture (K0045_DiffCoding)
  Difference signal = EL picture – upsampled reconstructed BL
  HEVC INTRA / INTER modes are supported, i.e. include MC in Diff-domain
Different interpolation filter for subpel for Diff-domain MC (K0045_DiffCoding_Interp)
  Not a commonality among CfP proposals
  Bi-linear interpolation filters to generate subpel for Diff-domain MC
Estimated performance
  Can be tested by disabling BOTH K0045_DiffCoding
  K0033 with Diff: AI 2X 37.0%, 1.5X 55.8%, RA 2X 33.8%, 1.5X 50.3%
  K0050 w/o Diff: AI 2X 36.7%, 1.5X 55.6%, RA 2X 31.6%, 1.5X 48.7%
Notes: VSP_skip and others

## Slide 7: Modified De-blocking
Not a commonality among CfP proposals [BoG JCTVC-K0354]
Additional criteria added to the de-blocking filter’s block strength calculation to consider difference coding mode vs. pixel coding mode
If only one of the blocks is Diff Coded, force Bs = 1
Notes: VSP_skip and others

## Slide 8: Conclusions and Suggestions
Features (the “meat”) for the following are implemented:
  Inter-layer texture prediction: Intra-BL Mode
  Inter-layer syntax prediction: Merge / AMVP, Inter-BL Mode
  Difference-domain coding: Diff-INTRA, Diff-INTER
  Modified deblocking considering Diff
  Can be disabled by individual or combination of macros
  Include features not commonality among CfP proposals
Also consider other s/w as starting point
IF using JCTVC-K0345 as s/w model, ONLY enable K0045_Intra_BL (“meat” only as example, no priority)
Notes:     Problem and proposeVSP off, finding inter-view reference without warping