## Slide 1: TE3: Summary report of tool experiment on Combined Prediction in SHVC
Xiang Li, Edouard François, Polin Lai, Do-Kyoung Kwon, Ankur Saxena

## Slide 2: TE3 subsets
TE3.1 Intra prediction based on reconstructed base layer
TE3.2 Intra prediction based on differential picture
TE3.3 Inter prediction based on reconstructed base layer
TE3.4 Inter prediction based on differential picture
TE3.5 SVC style residual prediction
TE3.6 Generalized residual prediction

## Slide 3: TE3.1 Intra prediction based on reconstructed BL
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.1.2 | JCTVC-L0036 (Nokia) dc_delta added to Intra Pred when size >= 8x8. dc_delta = (DC BL Pred block) - (DC EL Pred block). | AI-2x AI-1.5x | -0.2% | 0.0% | 0.0% | 105% | 100%
4.1.3 (Inter not mandatory) | JCTVC-L0099 (LG) Unavailable ref samples for Intra Prediction at EL are replaced by collocated BL samples. | AI-2x AI-1.5x inter | -0.1% 0.0% | -0.1% -0.1% | -0.1% -0.1% | 102% 100% | 101% 100%

## Slide 4: TE3.2 Intra pred. based on differential picture
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.2.1 | JCTVC-L0037 (Nokia) Intra horiz and vertic pred modes at EL replaced by new modes which combine EL and BL as Pred_el = Ref_el + Rec_bl - Ref_bl. No additional Signaling. | AI-2x AI-1.5x | -0.3% | -0.1% | -0.1% | 100% | 99%
4.2.1 + 4.1.2 |  | AI-2x AI-1.5x | -0.4% | -0.1% | -0.2% | 104% | 100%
4.2.2 | JCTVC-L0222 (Qualcomm) CU level Diff domain Intra Pred. MDIS disabled. Planar modified to set all pixels in bottom-right portion ((x + y) >= N-1) to 0. | AI-2x AI-1.5x | -0.9% | 0.0% | -0.2% | 156% | 108%
4.2.3 | JCTVC-L0135 (LG) CU Level Diff Domain Intra Prediction. Diff signal is clipped to [-128,127] | AI-2x AI-1.5x | -0.8% | -0.1% | -0.3% | 159% | 109%
4.2.4 | JCTVC-L0183 (Vidyo/Samsung) CU level Diff Intra Pred. Offset 128 added to diff signal to keep dynamic range in [0, 255] | AI-2x AI-1.5x | -0.8% | -0.2% | -0.4% | 171% | 142%
Differential Signal:
  ( EL Reconstructed Signal – Upsampled Reconstructed BL Signal ) in Current Picture

## Slide 5: TE3.3 Inter pred. based on reconstructed BL
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.3.1 | JCTVC-L0072 (MediaTek) Rec_el = Clip( (Pred_el + Rec_bl) / 2 + Residue_el ) CU level signaling. If CU in 2Nx2N with at least one non-zero residue. | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -1.2% | -3.3% | -3.8% | 104% | 100%
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.6.2.2 | JCTVC-L0206 (Qualcomm) Combined prediction of BL and EL. CU level signaling. Rec_el=Clip(Pred_el+Rec_bl+1)/2+Residue_el) | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -1.2% | -3.6% | -4.2% | 116% | 100%

## Slide 6: TE3.4 Inter pred. based on differential picture
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.4.1 | JCTVC-L0136 (LG) CU level diff-inter prediction. Diff signal clipped to [-128, 127] | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -2.0% | -3.5% | -3.7% | 153% | 103%
4.4.2 | JCTVC-L0184 (Vidyo/Samsung) CU level diff-inter prediction. Offset 128 added to keep dynamic range of [0, 255]. Bi-linear interpolation for sub-pel diff blocks. Deblocking BS=1 for the diff/non-diff boundary. | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -2.4% | -3.7% | -3.7% | 168% | 131%
Differential Signal:
  ( EL Reconstructed Signal – Upsampled Reconstructed BL Signal ) in Reference Picture

## Slide 7: TE3.5 SVC style residual prediction
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.5.1 | JCTVC-L0286 (Intel) SVC style residual prediction. signaling at CU level for intra, PU level for inter. Base residues are bi-linearly up-sampled. | AI-2x AI-1.5x | -0.1% | 0.0% | 0.0% | 167% | 109%
 |  | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -0.4% | -0.9% | -1.0% | 103% | 110%
2nd order Residual Prediction using Decoded BL residual

## Slide 8: TE3.6 Generalized residual prediction
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.6.1 | JCTVC-L0100 (Canon) CU level signaling. Pred_el=Ref_el+Rec_bl-Ref_bl. This method does not apply to skip mode. | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -1.6% | -2.8% | -2.9% | 143% | 83%
4.6.2.1 Test1 | JCTVC-L0078 (Qualcomm) CU level signaling. Pred_el=Ref_el + w*(Rec_bl-Ref_bl), w= 0.5, 1. Interpol. directly on Diff block for sub-pel positions. Fast GRP mode selection method (encoder only). Test 1: GRP (0.5) | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -2.4% | -3.0% | -2.8% | 118% | 107%
Test2 | Test 2: GRP (0.5, 1) + Fast GRP mode selection |  | -2.8% | -4.3% | -4.2% | 116% | 104%
Test3 | Test 3: GRP (0.5, 1) + Fast GRP mode selection + 4-tap up-sampling filter for GRP mode |  | -3.5% | -3.7% | -3.8% | 116% | 129%
4.6.3 | JCTVC-L0038 (Nokia) PU level signaling. Pred_el=Ref_el + w*(Rec_bl-Ref_bl), w=0.5, 1 | RA-2x, 1.5x, SNR LP-2x, 1.5x, SNR | -2.4% | -3.8% | -4.0% | 115% | 104%
2nd order Residual Prediction using BL Temporal Pred Residual

## Slide 9: TE3.6 Generalized residual prediction (late release)
Proposal | Description | Test case | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT
4.6.2.1 Test4 | JCTVC-L0078 (Qualcomm) CU level signaling. Pred_el=Ref_el + w*(Rec_bl-Ref_bl), w= 0.5, 1. Interpol. directly on Diff block for sub-pel positions. Fast GRP mode selection method (encoder only). Test 4 (recently released): Test 1 + additional ME |  | -3.1% | -3.7% | -3.4% | 159% | 109%
Test5 | Test 5 (recently released): Test 2 + additional ME |  | -3.4% | -4.8% | -4.7% | 148% | 105%

## Slide 10: List of related non-TE proposals
Proposals | Title
JCTVC-L0074 (MediaTek) | Non-TE3: Adaptive predictor compensation with generalized residual prediction
JCTVC-L0084 (Samsung) | Non TEB3: Bi-directional optical flow for inter-layer texture prediction
JCTVC-L0104 (Canon) | Non-TE3: Simplification of Generalized Residual Inter-Layer Prediction (GRILP) in SHVC
JCTVC-L0140 (LG) | Non-TE3: Modifications on inter-layer texture, DC, planar predictions
JCTVC-L0190 (Qualcomm) | Non-TE3: Extension of Test 4.6.2.1 on Generalized Residual Prediction
JCTVC-L0193 (Technicolor) | Base Layer residue upsampling and skip mode
JCTVC-L0211 (Qualcomm) | NonTE3/4: Combination of TE-B4 4.2.1 Adaptive Up-samp. Filter and TE3 4.6.2.1 GRP
JCTVC-L0215 (Sony) | Non-TE3: Cross-checking and simplif. of intra residual planar prediction in TE3-4.2.2
JCTVC-L0265 (Sony) | On interpolation filter for Generalized Residual Prediction
JCTVC-L0267 (Sharp) | Hybrid Intra and Inter-layer Prediction
JCTVC-L0294 (Qualcomm) | Non-TE3 : Simplification of Difference Intra Prediction In SHVC

## Slide 11: More Detailed Results
Subtests | Proposal | Test case | Results (BD-rate reduction of EL+BL) |  |  |  |  | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
4.1 Intra prediction based on reconstructed base layer | 4.1.2 | AI-2x | -0.2% | -0.1% | 0.0% | 105% | 99% | -0.2% | 0.0% | 0.0% | 105% | 100%
 |  | AI-1.5x | -0.1% | 0.0% | 0.0% | 105% | 101% |  |  |  |  | 
 | 4.1.3 (Inter results are not mandatory) | AI-2x | -0.2% | -0.1% | -0.1% | 102% | 101% | -0.1% | -0.1% | -0.1% | 102% | 101%
 |  | AI-1.5x | -0.1% | 0.0% | -0.1% | 102% | 101% |  |  |  |  | 
 |  | RA-2x | -0.1% | -0.1% | -0.1% | 100% | 100% | 0.0% | -0.1% | -0.1% | 100% | 100%
 |  | RA-1.5x | 0.0% | -0.1% | -0.1% | 100% | 100% |  |  |  |  | 
 |  | RA-SNR | 0.0% | 0.0% | 0.0% | 102% | 102% |  |  |  |  | 
 |  | LDP-2x | 0.0% | -0.1% | -0.1% | 100% | 99% |  |  |  |  | 
 |  | LDP-1.5x | 0.0% | -0.1% | -0.1% | 101% | 100% |  |  |  |  | 
 |  | LDP-SNR | 0.0% | -0.1% | -0.1% | 99% | 99% |  |  |  |  | 
4.2 Intra prediction based on differential picture | 4.2.1 | AI-2x | -0.3% | -0.1% | -0.2% | 101% | 99% | -0.3% | -0.1% | -0.1% | 100% | 99%
 |  | AI-1.5x | -0.2% | 0.0% | -0.1% | 99% | 100% |  |  |  |  | 
 | 4.2.1 + 4.1.2 | AI-2x | -0.4% | -0.2% | -0.2% | 105% | 99% | -0.4% | -0.1% | -0.2% | 104% | 100%
 |  | AI-1.5x | -0.3% | 0.0% | -0.1% | 104% | 101% |  |  |  |  | 
 | 4.2.2 | AI-2x | -1.1% | -0.3% | -0.5% | 160% | 109% | -0.9% | 0.0% | -0.2% | 156% | 108%
 |  | AI-1.5x | -0.8% | 0.2% | 0.0% | 151% | 107% |  |  |  |  | 
 | 4.2.3 | AI-2x | -0.9% | -0.4% | -0.6% | 163% | 110% | -0.8% | -0.1% | -0.3% | 159% | 109%
 |  | AI-1.5x | -0.6% | 0.1% | 0.0% | 154% | 109% |  |  |  |  | 
 | 4.2.4 | AI-2x | -0.9% | -0.5% | -0.7% | 177% | 141% | -0.8% | -0.2% | -0.4% | 171% | 142%
 |  | AI-1.5x | -0.6% | 0.0% | -0.2% | 166% | 143% |  |  |  |  | 

## Slide 12: More Detailed Results
Subtests | Proposal | Test case | Results (BD-rate reduction of EL+BL) |  |  |  |  | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
4.3 Inter prediction based on reconstructed base layer | 4.3.1 | RA-2x | -0.4% | -1.7% | -1.9% | 105% | 101% | -1.2% | -3.3% | -3.8% | 104% | 100%
 |  | RA-1.5x | -0.6% | -2.3% | -2.7% | 103% | 100% |  |  |  |  | 
 |  | RA-SNR | -0.8% | -3.3% | -3.9% | 103% | 100% |  |  |  |  | 
 |  | LDP-2x | -1.2% | -2.6% | -3.0% | 105% | 100% |  |  |  |  | 
 |  | LDP-1.5x | -1.5% | -4.1% | -4.7% | 103% | 99% |  |  |  |  | 
 |  | LDP-SNR | -2.4% | -6.0% | -7.0% | 104% | 100% |  |  |  |  | 
Subtests | Proposal | Test case | Results (BD-rate reduction of EL+BL) |  |  |  |  | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
4.6 Generalized residual prediction | 4.6.2.2 | RA-2x | -0.4% | -1.9% | -2.1% | 122% | 103% | -1.2% | -3.6% | -4.2% | 116% | 100%
 |  | RA-1.5x | -0.6% | -2.5% | -3.0% | 114% | 99% |  |  |  |  | 
 |  | RA-SNR | -0.8% | -3.5% | -4.1% | 113% | 102% |  |  |  |  | 
 |  | LDP-2x | -1.2% | -2.9% | -3.3% | 118% | 97% |  |  |  |  | 
 |  | LDP-1.5x | -1.5% | -4.6% | -5.3% | 113% | 98% |  |  |  |  | 
 |  | LDP-SNR | -2.5% | -6.4% | -7.5% | 115% | 101% |  |  |  |  | 

## Slide 13: More Detailed Results
Subtests | Proposal | Test case | Results (BD-rate reduction of EL+BL) |  |  |  |  | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
4.4 Inter prediction based on differential picture | 4.4.1 | RA-2x | -1.8% | -3.3% | -3.3% | 165% | 104% | -2.0% | -3.5% | -3.7% | 153% | 103%
 |  | RA-1.5x | -2.4% | -4.3% | -4.5% | 154% | 101% |  |  |  |  | 
 |  | RA-SNR | -1.5% | -3.5% | -3.7% | 145% | 105% |  |  |  |  | 
 |  | LDP-2x | -2.0% | -2.9% | -3.0% | 161% | 106% |  |  |  |  | 
 |  | LDP-1.5x | -2.8% | -4.2% | -4.3% | 149% | 101% |  |  |  |  | 
 |  | LDP-SNR | -1.5% | -3.0% | -3.1% | 143% | 105% |  |  |  |  | 
 | 4.4.2 | RA-2x | -1.7% | -2.6% | -2.6% | 182% | 137% | -2.4% | -3.7% | -3.7% | 168% | 131%
 |  | RA-1.5x | -2.1% | -3.8% | -3.9% | 170% | 138% |  |  |  |  | 
 |  | RA-SNR | -1.7% | -3.7% | -4.0% | 157% | 115% |  |  |  |  | 
 |  | LDP-2x | -2.7% | -2.9% | -2.5% | 179% | 139% |  |  |  |  | 
 |  | LDP-1.5x | -3.3% | -4.5% | -4.4% | 165% | 140% |  |  |  |  | 
 |  | LDP-SNR | -2.7% | -4.9% | -5.2% | 155% | 118% |  |  |  |  | 
4.5 SVC style residual prediction | 4.5.1 | AI-2x | -0.1% | -0.1% | -0.1% | 172% | 109% | -0.1% | 0.0% | 0.0% | 167% | 109%
 |  | AI-1.5x | 0.0% | 0.0% | 0.0% | 163% | 109% |  |  |  |  | 
 |  | RA-2x | -0.3% | -0.8% | -0.9% | 103% | 112% | -0.4% | -0.9% | -1.0% | 103% | 110%
 |  | RA-1.5x | -0.5% | -1.1% | -1.3% | 103% | 114% |  |  |  |  | 
 |  | RA-SNR | -0.3% | -0.8% | -0.9% | 103% | 100% |  |  |  |  | 
 |  | LDP-2x | -0.1% | -0.6% | -0.7% | 103% | 115% |  |  |  |  | 
 |  | LDP-1.5x | -0.6% | -1.3% | -1.4% | 103% | 117% |  |  |  |  | 
 |  | LDP-SNR | -0.3% | -0.7% | -0.7% | 103% | 102% |  |  |  |  | 

## Slide 14
Subtests | Proposal | Test case | Results (BD-rate reduction of EL+BL) |  |  |  |  | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
4.6 Generalized residual prediction | 4.6.1 | RA-2x | -1.5% | -2.5% | -2.5% | 155% | 85% | -1.6% | -2.8% | -2.9% | 143% | 83%
 |  | RA-1.5x | -1.8% | -3.2% | -3.3% | 143% | 80% |  |  |  |  | 
 |  | RA-SNR | -1.1% | -2.7% | -2.9% | 132% | 80% |  |  |  |  | 
 |  | LDP-2x | -1.8% | -2.5% | -2.5% | 154% | 81% |  |  |  |  | 
 |  | LDP-1.5x | -2.3% | -3.5% | -3.5% | 142% | 87% |  |  |  |  | 
 |  | LDP-SNR | -1.3% | -2.4% | -2.6% | 133% | 87% |  |  |  |  | 
 | 4.6.2.1 Test1 | RA-2x | -1.5% | -2.9% | -3.0% | 121% | 108% | -2.4% | -3.0% | -2.8% | 118% | 107%
 |  | RA-1.5x | -2.3% | -3.7% | -4.0% | 116% | 107% |  |  |  |  | 
 |  | RA-SNR | -1.7% | -3.6% | -3.9% | 114% | 110% |  |  |  |  | 
 |  | LDP-2x | -2.4% | -2.2% | -1.7% | 122% | 105% |  |  |  |  | 
 |  | LDP-1.5x | -3.4% | -2.6% | -1.5% | 117% | 105% |  |  |  |  | 
 |  | LDP-SNR | -3.2% | -3.1% | -2.6% | 116% | 106% |  |  |  |  | 
 | 4.6.2.1 Test2 | RA-2x | -1.9% | -4.0% | -4.2% | 119% | 105% | -2.8% | -4.3% | -4.2% | 116% | 104%
 |  | RA-1.5x | -2.8% | -5.2% | -5.6% | 111% | 103% |  |  |  |  | 
 |  | RA-SNR | -2.1% | -4.7% | -5.2% | 114% | 107% |  |  |  |  | 
 |  | LDP-2x | -2.7% | -3.4% | -3.0% | 124% | 102% |  |  |  |  | 
 |  | LDP-1.5x | -3.9% | -4.3% | -3.5% | 113% | 101% |  |  |  |  | 
 |  | LDP-SNR | -3.4% | -4.2% | -3.8% | 118% | 105% |  |  |  |  | 
 | 4.6.2.1 Test3 | RA-2x | -2.3% | -3.4% | -3.6% | 119% | 125% | -3.5% | -3.7% | -3.8% | 116% | 129%
 |  | RA-1.5x | -3.0% | -4.1% | -4.6% | 111% | 125% |  |  |  |  | 
 |  | RA-SNR | -2.8% | -4.3% | -4.8% | 113% | 141% |  |  |  |  | 
 |  | LDP-2x | -3.4% | -3.1% | -2.7% | 123% | 124% |  |  |  |  | 
 |  | LDP-1.5x | -4.5% | -3.6% | -3.0% | 113% | 123% |  |  |  |  | 
 |  | LDP-SNR | -4.8% | -4.0% | -3.8% | 117% | 141% |  |  |  |  | 
 | 4.6.3 | RA-2x | -1.7% | -3.6% | -3.8% | 122% | 103% | -2.4% | -3.8% | -4.0% | 115% | 104%
 |  | RA-1.5x | -2.5% | -4.5% | -4.9% | 113% | 110% |  |  |  |  | 
 |  | RA-SNR | -1.6% | -4.2% | -4.7% | 114% | 104% |  |  |  |  | 
 |  | LDP-2x | -2.3% | -2.9% | -2.8% | 117% | 103% |  |  |  |  | 
 |  | LDP-1.5x | -3.4% | -3.8% | -3.6% | 109% | 100% |  |  |  |  | 
 |  | LDP-SNR | -2.9% | -3.8% | -4.2% | 114% | 103% |  |  |  |  | 

## Slide 15: More Detailed Results
Subtests | Proposal | Test case | Results (BD-rate reduction of EL+BL) |  |  |  |  | Average of Coding Gain and Geometry Mean of Coding Time |  |  |  | 
 |  |  | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
4.6 Generalized residual prediction | 4.6.2.1 Test4 (recently released) | RA-2x | -2.0% | -3.6% | -3.6% | 171% | 110% | -3.1% | -3.7% | -3.4% | 159% | 109%
 |  | RA-1.5x | -2.7% | -4.1% | -4.4% | 160% | 109% |  |  |  |  | 
 |  | RA-SNR | -2.4% | -4.5% | -4.8% | 149% | 113% |  |  |  |  | 
 |  | LDP-2x | -3.0% | -2.9% | -2.3% | 168% | 107% |  |  |  |  | 
 |  | LDP-1.5x | -4.1% | -3.0% | -2.0% | 158% | 106% |  |  |  |  | 
 |  | LDP-SNR | -4.2% | -4.0% | -3.5% | 148% | 109% |  |  |  |  | 
 | 4.6.2.1 Test5 (recently released) | RA-2x | -2.4% | -4.5% | -4.5% | 156% | 105% | -3.4% | -4.8% | -4.7% | 148% | 105%
 |  | RA-1.5x | -3.2% | -5.5% | -5.8% | 140% | 105% |  |  |  |  | 
 |  | RA-SNR | -2.6% | -5.4% | -5.8% | 139% | 108% |  |  |  |  | 
 |  | LDP-2x | -3.4% | -4.0% | -3.5% | 162% | 103% |  |  |  |  | 
 |  | LDP-1.5x | -4.7% | -4.8% | -4.0% | 143% | 101% |  |  |  |  | 
 |  | LDP-SNR | -4.3% | -4.9% | -4.5% | 146% | 106% |  |  |  |  |