## Slide 1: TE 3-4.1.3 :filling unavailable reference samples in intra prediction at enhancement layer
C. Kim, B. Jeon (LG)
JCTVC-L0099
JCTVC-L0099

## Slide 2: Overall Summary
Filling unavailable reference samples in intra prediction at enhancement layer
  if there is any unavailable reference sample during intra prediction EL, the corresponding sample at BL will replace it.
Results for AI-2x and AI-1.5x
  Anchor SMuC 0.1.1 EL+BL
  BD rate savings : 0.2% and 0.1%
  Encoding times : 101.5% and 102.1%
  Decoding times : 101.2% and 101.4%
JCTVC-L0099

## Slide 3: Proposed method
In current SMuC 0.1.1,
  unavailable reference sample is replaced with padding or DC value.
In this contribution,
  the corresponding sample at BL will replace it.
  In below figure, left-bottom reference samples are unavailable and they are replaced with corresponding samples at BL.
JCTVC-L0099
EL
BL
Unavailable
reference
x
Replacement
with base layer reference

## Slide 4: Experimental Results(Intra)
Follow test conditions from TE3
JCTVC-L0099

## Slide 5: Experimental Results(Inter)
Follow test conditions from TE3
JCTVC-L0099

## Slide 6: Conclusion
We proposed filling unavailable reference samples in intra prediction at enhancement layer
Simulation results reportedly show 0.1-0.2% bit rate reduction compared with SMuC-0.1.1 anchor
Dec time increase : < 2.5%
Enc time increase : < 2%
JCTVC-L0099