## Slide 1: TE5: Results of test 5.2.6 on the Inter-Layer Motion Vector Prediction
G. Laroche, T. Poirier, P. Onno,
C. Gisquet, E. Francois
12th JCTVC Meeting, Geneva, January 2013

## Slide 2: Modification of the MERGE Mode
Maximum number of candidates is 6
TMVP derived only from the center C3 is the first candidate if the temporal collocated blocks are selected in the forward reference frame.
Pruning with TMVP candidate
Bottom left spatial candidate is added if count is less than 4
Add bottom right or center C3 BL MV after spatial candidates
Four offset candidates are added after BL MV candidate

## Slide 3: Experiments results
Reference: SMuC 0.1.1
Average BDR performance gain
  ALL: -1.6%(Y), -2.3%(U) and -2.5% (V)
  Mandatory: -1.4%(Y), -2.1%(U) and -2.3% (V)

## Slide 4: Additional results with MV compression for temporal motion vector
Reference: SMuC 0.1.1
Average BDR performance gain of the GRILP method is
  Mandatory: -1.4%(Y), -2.1%(U) and -2.2% (V)
=> No impact on results: same BDR gains

## Slide 5: Additional results in combination with Base Mode TE5 5.3.3
Reference: SMuC 0.1.1
Average BDR performance gain of the Merge modification is
  -3.6%(Y), -5.9%(U), -6.3%(V)

## Slide 6: Additional results in combination with Base Mode TE5 5.3.3
Reference: SMuC 0.1.1+BaseMode
Average BDR performance gain of the Merge modification is
  -3.6%(Y), -5.9%(U), -6.3%(V)

## Slide 7: Conclusion
Performance of Merge modification brings
  -1.6%(Y), -2.3%(U) and -2.5% (V)
Additional results show very good synergy with the Base Mode of TE5 5.3.3