## Slide 1: On Inter-Layer SAO for Base mode
G. Laroche, T. Poirier, C. Gisquet,
E. Francois, P. Onno
12th JCTVC Meeting, Geneva, January 2013

## Slide 2: Summary of the proposed Inter layer SAO
Use of the SAO syntax of the collocated LCU to reduce the SAO selection process for Enhancement layer
  Keep only if it is EO type
Use of a Default EO type when the collocated LCU is BO type or “No SAO” type
Offset always (1, 0, 0, -1) for Default type
Apply SAO filtering inside LCU to avoid base mode reconstruction of the pixels outside the LCU

## Slide 3: Inter layer SAO base layer derivation

## Slide 4: Experiments results
Reference: TE5.3.3
Average BDR performance gain
  -0.4%(Y), -1.0%(U) and -0.9% (V)
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.5% | -0.9% | -1.0% |  |  |  | -0.4% | -1.1% | -1.4%
Class B | -0.2% | -0.4% | -0.2% | -0.2% | -0.4% | -0.2% | -0.2% | -0.3% | -0.1%
Overall (EL+BL) | -0.3% | -0.5% | -0.4% | -0.2% | -0.4% | -0.2% | -0.3% | -0.5% | -0.4%
Overall (EL) | -0.6% | -1.2% | -1.0% | -0.4% | -1.3% | -0.7% | -0.5% | -1.4% | -1.1%
Enc Time[%] | 116.2% |  |  | 116.6% |  |  | 116.7% |  | 
Dec Time[%] | 127.8% |  |  | 117.8% |  |  | 131.8% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.6% | -1.8% | -1.7% |  |  |  | -0.5% | -1.8% | -1.8%
Class B | -0.4% | -1.2% | -1.1% | -0.4% | -1.4% | -1.5% | -0.5% | -1.5% | -1.3%
Overall (EL+BL) | -0.5% | -1.4% | -1.2% | -0.4% | -1.4% | -1.5% | -0.5% | -1.6% | -1.5%
Overall (EL) | -0.9% | -2.8% | -2.5% | -0.9% | -3.9% | -3.6% | -0.9% | -3.2% | -2.9%
Enc Time[%] | 114.4% |  |  | 114.0% |  |  | 114.0% |  | 
Dec Time[%] | 123.5% |  |  | 119.4% |  |  | 130.7% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 

## Slide 5: Experiments results
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -4.1% | -9.2% | -8.7% |  |  |  | -4.2% | -10.8% | -11.1%
Class B | -3.2% | -5.2% | -5.6% | -3.9% | -6.3% | -7.0% | -3.5% | -4.6% | -5.2%
Overall (EL+BL) | -3.4% | -6.4% | -6.5% | -3.9% | -6.3% | -7.0% | -3.7% | -6.4% | -6.9%
Overall (EL) | -6.7% | -12.1% | -12.3% | -10.3% | -17.0% | -18.4% | -7.8% | -13.4% | -14.2%
Enc Time[%] | 102.0% |  |  | 99.8% |  |  | 101.3% |  | 
Dec Time[%] | 139.6% |  |  | 168.6% |  |  | 140.1% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -3.4% | -7.3% | -6.7% |  |  |  | -4.2% | -8.4% | -8.2%
Class B | -2.9% | -4.0% | -3.9% | -3.4% | -5.2% | -5.3% | -3.7% | -4.6% | -4.8%
Overall (EL+BL) | -3.0% | -4.9% | -4.7% | -3.4% | -5.2% | -5.3% | -3.8% | -5.7% | -5.8%
Overall (EL) | -5.6% | -9.2% | -8.9% | -8.2% | -13.4% | -13.5% | -7.3% | -11.2% | -11.2%
Enc Time[%] | 102.9% |  |  | 100.3% |  |  | 102.5% |  | 
Dec Time[%] | 135.6% |  |  | 165.6% |  |  | 145.5% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
Reference: SMuC 0.1.1
Average BDR performance gain
  -3.4%(Y), -5.0%(U) and -5.3% (V)

## Slide 6: Conclusion
Proposal:
  Low complexity Inter layer SAO
    At encoder side by deriving the base layer syntax to avoid estimate all parameters
    At decoder side by filtering only pixel inside the CTB to avoid the reconstruction of neighboring CTB for base mode.
Performance of Inter layer SAO on Base mode only
  -0.4%(Y), -1.0%(U) and -0.9% (V) vs Base mode
  => Give better performances than the Inter layer SAO on Intra BL tested in TE4 with an equivalent complexity.