## Slide 1
TE2: Inter-layer Texture Prediction Signalling (test 3.1.9)
Elena Alshina
Samsung Electronics Co., Ltd
Jan. XX, 2013
Notes: <number>

## Slide 2: CU-based Intra_BL mode
Proposed CU-based Intra_BL mode
  Prediction: corresponding BL block of reconstructed pixels are scaled to the EL CU resolution
  Residual: same as non-scalable HEVC's inter residual sample coding process
  Special mode: Intra_BL skip mode in case of no significant coefficient
<number>
Start decoding a CU
Skip mode?
Intra_BL Skip mode?
Intra_BL mode?
Intra/Inter
Process Inter prediction
Process Inter prediction
Process Intra prediction
Process Inter-layer pixel prediction
Process Inter-layer pixel prediction
Residual decoding
Reconstruct CU
End
Yes
Inter
No
Intra
No
No
Yes
Yes

## Slide 3: CU-based Intra_BL mode
Simulation results (Test 3.1.9)
  According to the following results, test 3.1.9 provides not only BD-rate improvement but also decoder complexity reduction compared SmuC 0.1.1
  The following result is obtained by disabling Intra_BL skip mode and using Root Cbf coding for Intra_BL mode explicitly instead
<number>
 | Avg. AI (2X, 1.5X) |  |  | Avg. RA/LDP (2X, 1.5X) |  |  | AI 2 X | AI 1.5 X | RA 2X | RA 1.5X | RA SNR | LD 2X | LD 1.5X | LD SNR
 | Y | Enc. T | Dec. T | Y | Enc. T | Dec.T | Y | Y | Y | Y | Y | Y | Y | Y
Test 3.1.9 | -28.0% | 114.0% | 92.6% | -19.5% | 109.5% | 123.5% | -23.1% | -32.9% | -16.6% | -26.4% | -20.2% | -12.5% | -22.3% | -13.3%
SmuC 0.1.1 | -27.7% | 113.7% | 105.9% | -19.2% | 109.3% | 136.9% | -22.8% | -32.6% | -16.4% | -26.1% | -20.0% | -12.3% | -21.9% | -13.1%
Delta | -0.3% | 0.3% | -13.3% | -0.3% | 0.2% | -13.4% | -0.3% | -0.3% | -0.2% | -0.3% | -0.2% | -0.2% | -0.4% | -0.2%
 | Avg. AI (2X, 1.5X) |  |  | Avg. RA/LDP (2X, 1.5X) |  |  | AI 2 X | AI 1.5 X | RA 2X | RA 1.5X | RA SNR | LD 2X | LD 1.5X | LD SNR
 | Y | Enc. T | Dec. T | Y | Enc. T | Dec.T | Y | Y | Y | Y | Y | Y | Y | Y
Tested | -27.9% | 115.5% | 93.0% | -19.4% | 109.2% | 121.2% | -23.1% | -32.8% | -16.6% | -26.3% | -20.1% | -12.4% | -22.1% | -13.3%
SmuC 0.1.1 | -27.7% | 113.7% | 105.9% | -19.2% | 109.3% | 136.9% | -22.8% | -32.6% | -16.4% | -26.1% | -20.0% | -12.3% | -21.9% | -13.1%
Delta | -0.3% | 1.8% | -12.8% | -0.2% | -0.1% | -15.6% | -0.3% | -0.2% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.2%

## Slide 4
Thank you !
<number>