## Slide 1
JCTVC-L0112
AHG7: Reference sample filtering in intra prediction for chroma extended format
Junghye Min, Tammy Lee, Chanyul Kim

## Slide 2: Summary
Propose reference sample filtering methods in intra prediction for chroma extended formats
  Apply proposed sample filtering methods for chroma intra prediction
    Methods 1 : additional sample filtering for 4x4 and 8x8 transform units
    Methods 2: Methods1 + strong filtering for large transform units
  performance
    Method 1 : (-0.1%,-0,1%,-0.2%) in AI, (-0.1%, 0.0%, 0.0%) in RA
    Method 2: (-0.1%,-0.2%, -0.2%) in AI, (-0.1%, 0.0%, 0.0%) in RA

## Slide 3: Introduction -1
Reference sample filtering for intra prediction
  Depending on the transform unit size and intra prediction mode, whether filtered samples are used is determined
HM 9.0
  Reference sample filtering is applied only to luma samples
Common s/w for HM range extension
  Sample filtering is applied to chroma intra prediction for 4:4:4 format
  For 4:2:2 format, sample filtering is not used in chroma intra prediction
  Same sample filtering process from luma is applied to chroma component

## Slide 4: Introduction - 2
Motivations
  Chroma component is known to have noises with unnatural patterns
    Chroma component needs strong filtering for reference samples
  To provide optimized designs for chroma intra prediction to improve coding efficiency
Kimono 4:4:4 format

## Slide 5: Reference sample filtering process
Common S/W (same as HM9.0)
diff = min (abs( predMode - HOR_IDX), abs(predMode - VER_IDX));
sizeIndex=getSizeIndex(TuWidth)
filterFlag = diff > m_aucIntraFilter[sizeIndex]? 1:0;
m_aucIntraFilter [] =
{ 10, //4x4
7, //8x8
1, //16x16
0, //32x32
},
 | TU size |  |  |  | 
 |  | 4x4 | 8x8 | 16x16 | 32x32
 | 0 (planar) | 0 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | 2 | 0 | 1 | 1 | 1
 | 3 | 0 | 0 | 1 | 1
 | 4 | 0 | 0 | 1 | 1
 | 5 | 0 | 0 | 1 | 1
 | 6 | 0 | 0 | 1 | 1
 | 7 | 0 | 0 | 1 | 1
 | 8 | 0 | 0 | 1 | 1
 | 9 | 0 | 0 | 0 | 1
 | 10 (horizontal) | 0 | 0 | 0 | 0
intra | 11 | 0 | 0 | 0 | 1
pred | 12 | 0 | 0 | 1 | 1
mode | 13 | 0 | 0 | 1 | 1
 | 14 | 0 | 0 | 1 | 1
 | 15 | 0 | 0 | 1 | 1
 | 16 | 0 | 0 | 1 | 1
 | 17 | 0 | 0 | 1 | 1
 | 18 | 0 | 1 | 1 | 1
 | 19 | 0 | 0 | 1 | 1
 | 20 | 0 | 0 | 1 | 1
 | 21 | 0 | 0 | 1 | 1
 | 22 | 0 | 0 | 1 | 1
 | 23 | 0 | 0 | 1 | 1
 | 24 | 0 | 0 | 1 | 1
 | 25 | 0 | 0 | 0 | 1
 | 26 (vertical) | 0 | 0 | 0 | 0
 | 27 | 0 | 0 | 0 | 1
 | 28 | 0 | 0 | 1 | 1
 | 29 | 0 | 0 | 1 | 1
 | 30 | 0 | 0 | 1 | 1
 | 31 | 0 | 0 | 1 | 1
 | 32 | 0 | 0 | 1 | 1
 | 33 | 0 | 0 | 1 | 1
 | 34 | 0 | 1 | 1 | 1
Use Filtered samples

## Slide 6: Proposed method 1
Apply filtering for more cases in 4x4 and 8x8 transform units
m_aucIntraFilter [] =
{ 6, //4x4
1, //8x8
0, //16x16
0, //32x32
},
 | block size |  |  |  | 
 |  | 4x4 | 8x8 | 16x16 | 32x32
 | 0 (planar) | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | 2 | 1 | 1 | 1 | 1
 | 3 | 1 | 1 | 1 | 1
 | 4 | 0 | 1 | 1 | 1
 | 5 | 0 | 1 | 1 | 1
 | 6 | 0 | 1 | 1 | 1
 | 7 | 0 | 1 | 1 | 1
 | 8 | 0 | 1 | 1 | 1
 | 9 | 0 | 0 | 1 | 1
 | 10 (horizontal) | 0 | 0 | 0 | 0
intra | 11 | 0 | 0 | 1 | 1
pred | 12 | 0 | 1 | 1 | 1
mode | 13 | 0 | 1 | 1 | 1
 | 14 | 0 | 1 | 1 | 1
 | 15 | 0 | 1 | 1 | 1
 | 16 | 0 | 1 | 1 | 1
 | 17 | 1 | 1 | 1 | 1
 | 18 | 1 | 1 | 1 | 1
 | 19 | 1 | 1 | 1 | 1
 | 20 | 0 | 1 | 1 | 1
 | 21 | 0 | 1 | 1 | 1
 | 22 | 0 | 1 | 1 | 1
 | 23 | 0 | 1 | 1 | 1
 | 24 | 0 | 1 | 1 | 1
 | 25 | 0 | 0 | 1 | 1
 | 26 (vertical) | 0 | 0 | 0 | 0
 | 27 | 0 | 0 | 1 | 1
 | 28 | 0 | 1 | 1 | 1
 | 29 | 0 | 1 | 1 | 1
 | 30 | 0 | 1 | 1 | 1
 | 31 | 0 | 1 | 1 | 1
 | 32 | 0 | 1 | 1 | 1
 | 33 | 1 | 1 | 1 | 1
 | 34 | 1 | 1 | 1 | 1
Use Filtered samples

## Slide 7: Proposed method 2
Apply strong filter for large transform unit sizes
m_aucIntraFilter [] =
{ 6, //4x4
2, //8x8
1, //16x16
0, //32x32
},
 | block size |  |  |  | 
 |  | 4x4 | 8x8 | 16x16 | 32x32
 | 0 (planar) | 1 | 1 | 2 | 2
 | 1 | 0 | 0 | 0 | 0
 | 2 | 1 | 1 | 2 | 2
 | 3 | 1 | 1 | 2 | 2
 | 4 | 0 | 1 | 2 | 2
 | 5 | 0 | 1 | 2 | 2
 | 6 | 0 | 1 | 2 | 2
 | 7 | 0 | 1 | 2 | 2
 | 8 | 0 | 0 | 2 | 2
 | 9 | 0 | 0 | 0 | 2
 | 10 (horizontal) | 0 | 0 | 0 | 0
intra | 11 | 0 | 0 | 0 | 2
pred | 12 | 0 | 0 | 2 | 2
mode | 13 | 0 | 1 | 2 | 2
 | 14 | 0 | 1 | 2 | 2
 | 15 | 0 | 1 | 2 | 2
 | 16 | 0 | 1 | 2 | 2
 | 17 | 1 | 1 | 2 | 2
 | 18 | 1 | 1 | 2 | 2
 | 19 | 1 | 1 | 2 | 2
 | 20 | 0 | 1 | 2 | 2
 | 21 | 0 | 1 | 2 | 2
 | 22 | 0 | 1 | 2 | 2
 | 23 | 0 | 1 | 2 | 2
 | 24 | 0 | 0 | 2 | 2
 | 25 | 0 | 0 | 0 | 2
 | 26 (vertical) | 0 | 0 | 0 | 0
 | 27 | 0 | 0 | 0 | 2
 | 28 | 0 | 0 | 2 | 2
 | 29 | 0 | 1 | 2 | 2
 | 30 | 0 | 1 | 2 | 2
 | 31 | 0 | 1 | 2 | 2
 | 32 | 0 | 1 | 2 | 2
 | 33 | 1 | 1 | 2 | 2
 | 34 | 1 | 1 | 2 | 2
Use Filtered samples
Use samples from strong filter
c
c
c
c
c
c
c
c
c
c
c
c
3 tap filter
Original
samples
Filtered
samples
c
c
c
c
c
c
3 tap filter
Filtered
Samples
With strong
Filter

## Slide 8: Test results
Chroma formats | Common s/w | Test1 | Test2 | Test3
4:4:4 | Same as luma | Same as luma | Use method 1 | Use method 2
4:2:2 | Not applied | Same as luma | Use method 1 | Use method 2
test1 | All Intra HE Main-tier |  | 
 | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
test3 | All Intra HE Main-tier |  | 
 | Y | U | V
RGB 4:4:4 | -0.2% | -0.2% | -0.3%
YCbCr 4:4:4 | -0.1% | -0.2% | -0.2%
YCbCr 4:2:2 | -0.1% | -0.1% | -0.2%
Overall | -0.1% | -0.2% | -0.2%
 | -0.1% | -0.2% | -0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
test2 | All Intra HE Main-tier |  | 
 | Y | U | V
RGB 4:4:4 | -0.1% | -0.1% | -0.2%
YCbCr 4:4:4 | -0.1% | -0.1% | -0.1%
YCbCr 4:2:2 | -0.1% | -0.2% | -0.2%
Overall | -0.1% | -0.1% | -0.2%
 | -0.1% | -0.1% | -0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Sample filtering process for chroma

## Slide 9: Conclusions
Proposed methods provide additional gains in all color components without increase in encoding and decoding time
We recommend adopting the proposed sampling filtering method for the common s/w with range extension

## Slide 10
Thank you !

## Slide 11: Full results – test 1
test1 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 12: Full results – test 2
test2 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1%
YCbCr 4:4:4 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
YCbCr 4:2:2 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2%
Overall | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2%
 | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
Overall | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | -0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 13: Full results – test 3
test3 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.2% | -0.2% | -0.3% | -0.1% | -0.1% | -0.2%
YCbCr 4:4:4 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2%
YCbCr 4:2:2 | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2%
Overall | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2%
 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
 | -0.1% | 0.2% | 0.0% | -0.1% | -0.2% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  |