## Slide 1: JCTVC-L0119
Kemal Ugur, Hoda Roodaki-Lavasani, Miska M. Hannuksela Nokia
Adaptive resolution change with SHVC

## Slide 2: Summary
Adaptive Resolution Change (ARC): Dynamically changing the resolution within the video sequence without using IDR pictures.
ARC was earlier proposed for HEVC v1, but functionality was not included, mostly due to the need to include “resampling” process in v1.
SHVC inherently supports resolution change and inter-layer prediction, it can effectively support ARC use-cases with small changes.
Proposal:
We propose sequence level flags for SHVC to indicate the ARC operation for SHVC.

## Slide 3: Background
Benefits of ARC (JCTVC-F158)
Better network adaptation and error resilience: For better adaptation to changing network requirements for different content, it is desired to be able to change both the temporal / spatial resolution in addition to quality.
Fast start: The start-up time of the session could be increased by first sending a low resolution frame and then increasing the resolution.
  More important in HEVC due to intra frames taking relatively higher bitrate compared to earlier standards
Conference compose: When the person starts speaking, his/her corresponding resolution is increased. Doing this with an IDR frame causes a “blip” in the quality as IDR frames need to be coded at a relatively low quality so the delay is not increased.
BL0-BL1-BL2-BL3-EL3-EL4

## Slide 4: ARC
Illustration of how ARC reduces the bitrate compared to using IDR picture
Complete results in the contribution

## Slide 5: Proposal
Two flags are proposed for VPS:
inter_layer_pred_for_el_rap_only_flag : indicating that only RAP pictures in the enhancement layer may utilize inter-layer prediction and that non-RAP pictures in the enhancement layer never utilize inter-layer prediction.
single_layer_for_non_rap_flag :
  except for switching pictures, each AU in the sequence contains a single picture from a single layer (which may or may not be BL picture)
  Access units where switching happens include pictures from two layers and inter-layer scalability tools may be used.
Functionalities:
  Allows the decoder to know that scalability is not used except for achieving resolution change, so that the decoder resources can be allocated accordingly upon session start.
  Indicates that some access units do not necessarily contain BL pictures.
Reason for separating the functionality in two flags is that an encoder might originally send two layers for all AUs, but a middle-box could trim the bitstream differently for multiple recipients.

## Slide 6: Conclusion
Changing resolution without using IDR pictures is useful in video-conferencing.
SHVC inherently supports inter-layer prediction and resolution change  it can efficiently be used with ARC use-cases with small changes.
We propose high level flags for SHVC to indicate the ARC operation.

## Slide 7: Appendix
vps_extension( ) { | Descriptor
… | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) { | 
// layer dependency | 
num_direct_ref_layers[ i ] | u(6)
for( j = 0; j < num_direct_ref_layers[ i ]; j++ ) { | 
ref_layer_id[ i ][ j ] | u(6)
} | 
} | 
inter_layer_pred_for_el_rap_only_flag | u(1)
single_layer_for_non_rap_flag | u(1)
} | 
inter_layer_pred_for_el_rap_only_flag equal to 1 indicates that any non-RAP picture with layer_id greater than 0 does not use inter-layer prediction. inter_layer_pred_for_rap_only_flag equal to 0 indicates that any non-RAP picture with layer_id greater than 0 may or may not use inter-layer prediction.
NOTE – When inter_layer_pred_for_rap_only_flag is equal to 1, num_direct_ref_layers[ layerId ] and ref_layer_id[ layerId ][ j ] apply to RAP pictures with layer_id equal to layerId, while non-RAP pictures with layer_id equal to layerId do not actually use the layers indicated by ref_layer_id[ layerId ][ j ] for inter-layer prediction.
single_layer_for_non_rap_flag equal to 1 indicates either that all the VCL NAL units in an access unit have the same layer_id value or that two layer_id values are used by the VCL NAL units in an access unit and the picture with the greater layer_id value is a RAP picture. single_layer_for_non_rap_flag equal to 0 indicates that layer_id values may or may not be constrained beyond constraints specified in other parts of this Recommendation | International Standard.