## Slide 1: AHG7: Modification of intra angular prediction blending
S. Matsuo, S. Takamura, H. Fujii and A. Shimizu
NTT Corporation, Japan
JCTVC-L0128

## Slide 2: Summary
Intra angular prediction blending (K0155)
  Predicted samples are modified by blending the samples made by the opposite prediction direction
Its simplification is proposed (L0128)
  Weight coefficient matrices are removed to simplify the source code and the decoder description
Simulation results
  For AI:
    Overall average (Main-tier): 0.3% (Y), 0.2% (U), 0.2% (V)
    Max (EBURainFruits): 0.5% (R), 0.5% (G), 0.5% (B)
    Enc/DecTime: 103.8% / 102.8% (Main-tier)
  Works OK with inter, too
  Cross-checked by KDDI (JCTVC-L0374)

## Slide 3: Intra angular prediction blending
Modification of intra angular prediction (K0155)
  (Example) Predicted samples of mode 34 are blended with those of mode 2
  Weight coefficient matrices are defined for all block sizes and all prediction modes
Conventional
K0155

## Slide 4: Representation of weight coefficients
Weight function is newly defined
  Weights are analytically defined (no table needed)
  This function is used for all block sizes and all prediction modes
A
B
d=0
d=1
d=0
d=1
A
B
f(0.2)
f(0.4)
f(0.6)
f(0.8)
f(0.2)≒0.961
f(0.4)≒0.852
f(0.6)≒0.698
f(0.8)≒0.527

## Slide 5: Decoder description (1/2)
Predicted samples are modified by:
Weight function:
Weight coefficients w[x][y] are represented as:
  predSamples[x][y] = (w[x][y] * PS1[x][y] + (1024 - w[x][y]) * PS2[x][y] + 512) >> 10
  w[x][y] = exp
A
B
d=0
d=1
A(xA, yA)
B(xB, yB)

## Slide 6: Decoder description (2/2)
If predIntraMode >= 27,
If predIntraMode <= 9,
Otherwise, no modification is applied
  w[x][y] = exp
  xA = (y+1) * intraPredAngle + x * 32, yA = -32
  xB = -32, yB = (y+1) * intraPredAngleR + x * 32
  xA = -32, yA = (x+1) * intraPredAngle + y * 32
  xB = (x+1) * intraPredAngleR + y * 32, yB = -32
predModeIntra | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
intraPredAngleR | 32 | 39 | 49 | 60 | 79 | 114 | 205 | 512
predModeIntra | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34
intraPredAngleR | 512 | 205 | 114 | 79 | 60 | 49 | 39 | 32
Specification of intraPredAngleR

## Slide 7: Simulation results
Conditions
  Proposal was implemented in HM9.0RExt.
  Subject to the common test conditions for range extensions (K1006)
Results (AI)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.32% | -0.28% | -0.31% | -0.24% | -0.20% | -0.22%
YCbCr 4:4:4 | -0.38% | -0.27% | -0.25% | -0.32% | -0.20% | -0.18%
YCbCr 4:2:2 | -0.24% | -0.07% | -0.01% | -0.20% | -0.09% | -0.06%
Overall | -0.31% | -0.21% | -0.19% | -0.25% | -0.16% | -0.16%
 | -0.31% | -0.21% | -0.20% | -0.25% | -0.16% | -0.16%
Enc Time[%] | 103.8% |  |  | 103.2% |  | 
Dec Time[%] | 102.8% |  |  | 102.4% |  | 

## Slide 8: Simulation results (inter)
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.15% | -0.09% | -0.12% | -0.10% | -0.05% | -0.08%
YCbCr 4:4:4 | -0.17% | -0.14% | -0.11% | -0.13% | -0.05% | -0.06%
YCbCr 4:2:2 | -0.12% | -0.07% | 0.08% | -0.10% | -0.05% | 0.01%
Overall | -0.15% | -0.10% | -0.05% | -0.11% | -0.05% | -0.04%
 | -0.15% | -0.23% | -0.05% | -0.11% | 0.13% | -0.05%
Enc Time[%] | 99.9% |  |  | 100.0% |  | 
Dec Time[%] | 100.4% |  |  | 100.4% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.02% | -0.04% | -0.07% | -0.03% | -0.02% | -0.06%
YCbCr 4:4:4 | -0.12% | -0.08% | -0.11% | -0.10% | -0.06% | -0.01%
YCbCr 4:2:2 | -0.06% | -0.02% | 0.19% | -0.04% | 0.00% | 0.06%
Overall | -0.07% | -0.05% | 0.00% | -0.06% | -0.02% | -0.01%
 | -0.06% | 0.06% | -0.01% | -0.05% | -0.08% | 0.00%
Enc Time[%] | 100.0% |  |  | 100.1% |  | 
Dec Time[%] | 100.0% |  |  | 100.1% |  | 

## Slide 9: Conclusion
Modified intra angular prediction blending
  Weight function is newly introduced
Simulation results:
  For intra,
    Overall average (Main-tier): 0.2% ~ 0.3%
    Max (EBURainFruits): 0.5% (R), 0.5% (G), 0.5% (B)
    Enc/DecTime: 103.8% / 102.8% (Main-tier)
  Works OK with inter, too
  Cross-checked by KDDI (JCTVC-L0374)
Suggestion: Adopt this modification in HEVC range extensions

## Slide 10
Thank you, questions?