## Slide 1: AHG7: Modification filter for intra angular prediction
S. Matsuo, S. Takamura, H. Fujii and A. Shimizu
NTT Corporation, Japan
JCTVC-L0129

## Slide 2: Summary
Modification for some of intra angular predictions
  Predicted samples adjacent to the reference samples are modified in DC-prediction manner
Simulation results
  For AI:
    Overall average (Main): 0.23% (Y), 0.13% (U), 0.08% (V)
    Overall average (High): 0.17% (Y), 0.09% (U), 0.04% (V)
    Max (Traffic): 0.7% (R), 0.4% (G), 0.3% (B)
    EncTime: 100.0% (Main), 99.9% (High)
    Dectime: 101.1% (Main), 101.0% (High)
  Works OK with inter, too
  Cross-checked by KDDI (JCTVC-L0375)

## Slide 3: (FYI) Modification filter for DC mode
Intra DC mode of HEVC
  Average value (dcVal) is calculated and applied
  Predicted samples adjacent to reference samples are modified by the following equations
    predSamples[0][0]=(p[-1][0]+2*dcVal+p[0][-1]+2)>>2
    predSamples[x][0]=(p[x][-1]+3*dcVal+2)>>2, with x=1..nT-1
    predSamples[0][y]=(p[-1][y]+3*dcVal+2)>>2, with y=1..nT-1
    predSamples[x][y]=dcVal, with x,y=1..nT-1
  This modification method is applied to angular modes
dcVal

## Slide 4: (Proposal) Modification filter for angular mode
Intra angular prediction of HEVC
  In mode 2 to 9 and 27 to 34, some reference samples on the opposite side are available
  Proposal: Modification filter is applied to predicted samples adjacent to the reference samples on the opposite side
Conventional (mode 34)
Proposal (mode 34)

## Slide 5: Decoder description
In the process of angular mode,
  If predModeIntra >= 27,
  If predModeIntra <= 9,
  Otherwise, the modification filter is not applied
  predSamplesMod[0][y] = (p[-1][y+1] + 3 * predSamples[0][y] + 2) >> 2,
  with x=0 and y=0..nT-1
  predSamplesMod[x][0] = (p[x+1][-1] + 3 * predSamples[x][0] + 2) >> 2,
  with x=0 and y=0..nT-1

## Slide 6: Simulation results
Conditions
  Proposal was implemented in HM9.0RExt. and HM9.0.1
  Subject to the common test conditions for range extensions (K1006) and that for HEVC ver.1 (K1100)
Results (AI, HM9.0RExt-based)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.30% | -0.22% | -0.18% | -0.19% | -0.13% | -0.09%
YCbCr 4:4:4 | -0.17% | -0.10% | -0.01% | -0.13% | -0.06% | 0.01%
YCbCr 4:2:2 | -0.23% | -0.06% | -0.03% | -0.19% | -0.06% | -0.04%
Overall | -0.23% | -0.13% | -0.08% | -0.17% | -0.09% | -0.04%
 | -0.23% | -0.13% | -0.08% | -0.17% | -0.08% | -0.04%
Enc Time[%] | 100.0% |  |  | 99.9% |  | 
Dec Time[%] | 101.1% |  |  | 101.0% |  | 

## Slide 7: Simulation results (inter, HM9.0RExt-based)
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.19% | -0.07% | -0.13% | -0.09% | -0.03% | -0.06%
YCbCr 4:4:4 | -0.10% | -0.13% | -0.09% | -0.07% | -0.11% | -0.05%
YCbCr 4:2:2 | -0.12% | -0.05% | 0.04% | -0.09% | -0.04% | -0.01%
Overall | -0.14% | -0.08% | -0.06% | -0.08% | -0.06% | -0.04%
 | -0.14% | -0.22% | -0.04% | -0.09% | 0.23% | -0.05%
Enc Time[%] | 100.0% |  |  | 100.0% |  | 
Dec Time[%] | 101.4% |  |  | 101.0% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -0.03% | -0.02% | -0.05% | -0.02% | 0.00% | -0.04%
YCbCr 4:4:4 | -0.04% | -0.09% | -0.02% | -0.03% | -0.07% | 0.02%
YCbCr 4:2:2 | -0.07% | -0.09% | 0.18% | -0.05% | -0.04% | -0.02%
Overall | -0.04% | -0.07% | 0.03% | -0.03% | -0.03% | -0.01%
 | -0.05% | 0.12% | 0.04% | -0.03% | -0.07% | -0.02%
Enc Time[%] | 100.1% |  |  | 100.1% |  | 
Dec Time[%] | 100.6% |  |  | 100.7% |  | 

## Slide 8: Simulation results (AI, HM9.0.1-based)
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | -0.16% | -0.24% | -0.22% | -0.18% | -0.29% | -0.27%
Class B | -0.04% | -0.11% | -0.13% | -0.05% | -0.10% | -0.11%
Class C | -0.04% | -0.08% | -0.11% | -0.04% | -0.09% | -0.09%
Class D | -0.04% | -0.04% | -0.10% | -0.05% | -0.12% | -0.04%
Class E | -0.07% | -0.11% | -0.13% | -0.09% | -0.16% | -0.08%
Overall | -0.07% | -0.12% | -0.14% | -0.08% | -0.15% | -0.12%
 | -0.07% | -0.12% | -0.13% | -0.08% | -0.14% | -0.12%
Class F | 0.16% | 0.04% | 0.02% | 0.13% | -0.01% | 0.05%
Enc Time[%] | 100.6% |  |  | 100.6% |  | 
Dec Time[%] | 99.2% |  |  | 99.3% |  | 
[Note] The proposal is applied only for luma.
The proposal is not applied to 4x4.

## Slide 9: Conclusion
Modified intra angular prediction
  Predicted samples adjacent to the reference samples are modified in DC-prediction manner
Simulation results showed
  For intra,
    Overall average (Main-tier): 0.08% ~ 0.23%
    Max (Traffic): 0.7% (R), 0.4% (G), 0.3% (B)
    Complexity: 100.0% (Enc), 101.1% (Dec)
  Works OK with inter, too
  Works OK with HEVC ver.1
  Cross-checked by KDDI (JCTVC-L0375)
Suggestion: Adopt this modification in HEVC ver.1/2

## Slide 10
Thank you, questions?