## Slide 1: Inter-Layer SPS Prediction FOR HEVC EXTENSIONS
JCTVC-L0137
Thomas Rusert (Ericsson)

## Slide 2: Outline
Suggested SPS/VPS design criteria for HEVC extensions
SPS design with inter-layer SPS prediction

## Slide 3: General SPS/VPS Design Criteria For HEVC Ext.
VPS contents should change infrequently
  VPS activation requires IDR in all layers
  Layer-specific parameters that may change are preferably contained in SPS instead
Amount of VPS data associated with higher layers should be small
  Avoid overhead for lower layers (VPS is part of all decodable sub-bitstreams)
Size of parameter sets (VPS in particular) should be small
  Minimize bit overhead for out-of-band transmission, thus minimizing delay for e.g. session setup
  This is particularly true for VPS which is intended to be used for capability exchange

## Slide 4: Specific SPS/VPS Design Criteria For HEVC Ext.
Classes of parameters to include in VPS extension
Classes of parameters to include in SPS in HEVC extensions
Parameters that are useful for bitstream extraction and/or capability exchange | Y
Parameters that are not required for bitstream extraction and/or capability exchange | N
Sequence-level parameters that may change in some layers while not affecting the general layer structure | N
Sequence-level parameters that are not present in VPS (including parameters related to coding tools) | Y
Parameters present in VPS (except for parameters required for base layer decoding) | N

## Slide 5: Proposed SPS Design for HEVC Extensions
Parameters not included in SPS with nuh_layer_id > 0 (compared to base SPS)
  profile_tier_level( )
  sps_max_sub_layers_minus1
  sps_temporal_id_nesting_flag
  sps_sub_layer_ordering_info_present_flag
  sps_max_dec_pic_buffering[ i ]
  sps_max_num_reorder_pics[ i ]
  sps_max_latency_increase[ i ]
Parameters remaining in SPS with nuh_layer_id > 0 [number of bits under CTC]
  Representation format related parameters (picture size, chroma format, bit depth) [52]
  Reference picture sets [140]
  VUI [1]
  All other parameters (tools and restrictions) [29]
When decoding scalable/3D bitstreams, several layer-specific SPSs may be required  may lead to redundancy across SPSs  inter-layer SPS prediction

## Slide 6: Proposed Inter-Layer SPS Prediction
Additional syntax in SPS with nuh_layer_id > 0
  Indication whether SPS prediction is used
  Reference layer for SPS prediction
  Indication which groups of parameters are predicted
Parameter inheritance at SPS activation time
  Syntax elements not present in the SPS are inherited from the active SPS in the reference layer