## Slide 1: JCTVC-L0162 AHG7: Coding 4:2:2 chroma format with 4:2:0 and 4:4:4 format codecs
R&D
© BBC MMXIII
Andrea Gabriellini and Marta Mrak
BBC Research and Development

## Slide 2: Coding 4:2:2 signal using 4:4:4 and 4:2:0 codecs
Application scenarios
  Sources in 4:2:0 and 4:4:4 formats are used in environments with 4:2:2 serial interfaces
  Sources in 4:2:2 format used in environment where 4:2:2 codecs are not available
Challenges
  Selection of resampling filters
  Ensuring usage of correct filter at the decoder side
  Performance issues, especially in cascaded coding scenarios:

## Slide 3: Scenarios
Coding of 4:2:2 format with 4:2:0 codec
  Requires downsampling that introduces losses
  Careful filter design can minimise resampling losses; see e.g. SMPTE solutions
Coding of 4:2:2 format with 4:4:4 codec
  Upsampling/downsampling process does not have to introduce losses
    Use reversible filters
  Evaluated scenario:

## Slide 4: Coding 4:2:2 format with 4:4:4 codec
Any upsampling and downsampling filters can be used
Here focus on providing reversible resampling
  Resampling 4:2:2  4:4:4  4:2:2 does not introduce losses
  S-Filter and F-Filter
S-Filter
  Encoder - 4:2:2 to 4:4:4 using line doubling:
  Decoder - 4:4:4 to 4:2:2 as
  Limited performance, but does not require increasing bit-depth to achieve reversibility

## Slide 5: Coding 4:2:2 format with 4:4:4 codec (cont.)
F-Filter
  Generally can be any FIR filter
  Focus on reversibility
  Short filter used in experiments, here defined with taps a / 2k :
    For reversibility requires bit-depth increase by only 1 bit (ku = 1)
  Longer filters will generally have better anti-aliasing properties, but generally require higher bit-depth increase to keep reversibility properties
Sampling | Filter taps, a | k
Up | 1, 1 | ku = 1
Down | -1, 2, 6, 2, -1 | kd = 3

## Slide 6: Experiments
Anchor: HM 9.0 RExt; 4:2:2 format coding
Tested: HM 9.0 RExt 4:4:4 format coding, 4:2:2 samples
RExt test conditions and related sequences in 4:2:2 format
  10-bit coding only

## Slide 7: Results
 |  | Filter S |  |  |  |  |  |  | Filter F |  |  |  |  | 
 |  | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  |  | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 |  | Y | U | V | Y | U | V |  | Y | U | V | Y | U | V
Traffic_2560x1600_30_10bit_422_crop.yuv |  | 3.3% | -1.6% | -2.1% | 4.9% | -0.7% | -1.4% |  | 1.8% | 2.1% | 1.2% | 2.6% | 3.1% | 1.8%
Kimono1_1920x1080_24_10bit_422.yuv |  | 3.4% | -0.9% | -2.7% | 5.8% | 3.5% | -2.8% |  | 2.1% | 0.6% | -0.7% | 1.7% | 6.0% | -0.6%
EBUHorse_1920x1080_50_10bit_422.yuv |  | 2.9% | -0.9% | -3.6% | 4.9% | 1.6% | -3.4% |  | 1.5% | 2.4% | 0.1% | 1.8% | 6.0% | 0.3%
EBUGraphics_1920x1080_50_10bit_422.yuv |  | 3.6% | -1.5% | -5.0% | 6.3% | 1.2% | -1.2% |  | -0.1% | 1.4% | -1.3% | 1.4% | 5.8% | 2.4%
EBUWaterRocksClose_1920x1080_50_10bit_422.yuv |  | 3.4% | -0.1% | -5.7% | 5.7% | 1.5% | -3.6% |  | 1.5% | 4.0% | -0.8% | 2.1% | 7.5% | 1.6%
EBUKidsSoccer_1920x1080_50_10bit_422.yuv |  | 1.8% | -5.2% | -5.7% | 2.8% | -2.1% | -2.0% |  | 1.1% | -1.1% | -1.9% | 1.3% | 1.4% | 1.0%
Seeking_1920x1080_50_10bit_422.yuv |  | 3.3% | -1.3% | -2.8% | 5.3% | 2.3% | 1.3% |  | 0.7% | 3.1% | 2.1% | 0.3% | 8.7% | 7.1%
Overall |  | 3.1% | -1.6% | -3.9% | 5.1% | 1.0% | -1.9% |  | 1.2% | 1.8% | -0.2% | 1.6% | 5.5% | 2.0%
Enc Time[%] |  | 116% |  |  | 115% |  |  |  | 115% |  |  | 114% |  | 
Dec Time[%] |  | 126% |  |  | 126% |  |  |  | 127% |  |  | 123% |  | 
 |  | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 |  | Y | U | V | Y | U | V |  | Y | U | V | Y | U | V
Traffic_2560x1600_30_10bit_422_crop.yuv |  | 2.5% | -4.3% | -7.6% | 4.8% | -1.1% | -6.2% |  | 0.6% | -1.3% | -5.0% | 1.6% | 1.2% | -4.4%
Kimono1_1920x1080_24_10bit_422.yuv |  | 2.1% | -3.6% | -4.7% | 4.6% | -1.0% | -4.7% |  | 0.9% | -1.6% | -3.2% | 1.3% | -0.3% | -4.5%
EBUHorse_1920x1080_50_10bit_422.yuv |  | 2.3% | -7.8% | -12.2% | 2.9% | -2.2% | -14.7% |  | 0.6% | -2.9% | -8.0% | -0.6% | 3.6% | -9.3%
EBUGraphics_1920x1080_50_10bit_422.yuv |  | 3.8% | -2.2% | -1.3% | 6.6% | -1.3% | -1.2% |  | 0.1% | -1.4% | -2.4% | 1.9% | 1.6% | -0.4%
EBUWaterRocksClose_1920x1080_50_10bit_422.yuv |  | 0.9% | 3.8% | 4.0% | 2.0% | 3.0% | 0.6% |  | -0.2% | 8.2% | 7.8% | 0.0% | 7.5% | 5.2%
EBUKidsSoccer_1920x1080_50_10bit_422.yuv |  | 1.6% | -14.4% | -13.8% | 2.7% | -15.5% | -14.5% |  | 0.9% | -7.7% | -7.6% | 0.9% | -7.5% | -7.1%
Seeking_1920x1080_50_10bit_422.yuv |  | 1.5% | -2.5% | -2.8% | 3.5% | 2.8% | -0.7% |  | -0.5% | 0.9% | 1.5% | -1.4% | 5.2% | 2.8%
Overall |  | 2.1% | -4.4% | -5.5% | 3.9% | -2.2% | -5.9% |  | 0.3% | -0.8% | -2.4% | 0.5% | 1.6% | -2.5%
Enc Time[%] |  | 110% |  |  | 110% |  |  |  | 109% |  |  | 108% |  | 
Dec Time[%] |  | 125% |  |  | 122% |  |  |  | 129% |  |  | 124% |  | 
 |  | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 |  | Y | U | V | Y | U | V |  | Y | U | V | Y | U | V
Traffic_2560x1600_30_10bit_422_crop.yuv |  | -0.7% | 2.1% | -1.7% | 0.8% | 5.5% | 1.5% |  | -2.1% | 3.1% | -1.6% | -1.7% | 5.5% | -0.9%
Kimono1_1920x1080_24_10bit_422.yuv |  | 0.1% | 3.0% | 3.8% | 1.3% | 3.9% | 4.1% |  | -0.6% | 4.6% | 4.6% | -1.1% | 4.4% | 3.0%
EBUHorse_1920x1080_50_10bit_422.yuv |  | 0.1% | 1.1% | -4.4% | 0.3% | 8.9% | -0.4% |  | -1.0% | 5.4% | -2.4% | -2.7% | 16.3% | -1.5%
EBUGraphics_1920x1080_50_10bit_422.yuv |  | 2.1% | 4.7% | 6.8% | 4.5% | 5.5% | 6.0% |  | -1.2% | 3.0% | 1.5% | 0.0% | 7.2% | 3.9%
EBUWaterRocksClose_1920x1080_50_10bit_422.yuv |  | 0.3% | 5.3% | 4.5% | 1.6% | 5.4% | 2.7% |  | -0.7% | 9.6% | 8.4% | -0.6% | 10.0% | 8.1%
EBUKidsSoccer_1920x1080_50_10bit_422.yuv |  | 0.6% | -14.6% | -14.1% | 0.9% | -13.5% | -12.2% |  | 0.2% | -10.7% | -10.1% | -0.3% | -10.2% | -8.3%
Seeking_1920x1080_50_10bit_422.yuv |  | 0.1% | 4.8% | 3.9% | 0.8% | 10.5% | 7.2% |  | -1.2% | 8.2% | 8.4% | -3.2% | 13.2% | 11.1%
Overall |  | 0.4% | 0.9% | -0.2% | 1.4% | 3.8% | 1.3% |  | -1.0% | 3.3% | 1.3% | -1.4% | 6.6% | 2.2%
Enc Time[%] |  | 109% |  |  | 109% |  |  |  | 108% |  |  | 107% |  | 
Dec Time[%] |  | 121% |  |  | 119% |  |  |  | 125% |  |  | 121% |  | 

## Slide 8: Conclusions
When content in 4:2:2 chroma format is coded using 4:4:4 or 4:2:0 it is important to choose suitable filter pairs
  Depending on how the resampling on the encoder is performed, a filter for decoder should be defined
Proposal
  Enable resampling at the decoder side
  Enable signalling of filter coefficients to enable desirable resampling at the decoder side