## Slide 1: An encoder bug fix for the reference index framework in SHVC reference software (JCTVC-L0167)
Jinlei Zhang, Bin Li, Houqiang Li (USTC)
Haitao Yang (Huawei)

## Slide 2: Introduction
Inter-layer texture prediction is a coding tool in SMuC 0.1.1 to enhance the compression efficiency of scalable video coding
Two approaches for the inter-layer texture prediction
  Intra BL
  Ref_idx framework

## Slide 3: Problem statement
The cause of the bug
  In the ref_idx framework, the BLP (BL picture) is appended to the end of both reference picture lists of the EL coding picture
  In motion estimation, the cost of BLP in list1 is set to MAX_UINT, since BLP is already searched in list0
  In case the best reference picture in list0 is BLP, the cost of list1 BLP (MAX_UINT) is stored as the smallest cost after uni-directional search in list1
The effect of the bug
  It makes the uni-directional prediction from list1 unusable
  It affects RA cases where bi-directional prediction is allowed

## Slide 4: Proposed bug fix
In the function predInterSearch(), remove the following condition for setting best motion and cost information for list1 pictures
( iRefList == 1 && (pcCU->getSlice()->getNumRefIdx(REF_PIC_LIST_C) > 0) && (iRefIdxTemp==0 || iRefIdxTemp == iRefIdx[0]) && !pcCU->getSlice()->getNoBackPredFlag() && (iRefIdxTemp == pcCU->getSlice()->getRefIdxOfL0FromRefIdxOfL1(iRefIdxTemp)) )

## Slide 5: Experimental results
Anchor for comparison is SMuC0.1.1 with the DCT bug fix
Without the bug fix
With the bug fix
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 1.5% | 3.8% | 4.1% |  |  |  | 1.6% | 4.7% | 5.5%
Class B | 1.8% | 4.7% | 5.3% | 1.5% | 2.9% | 3.4% | 2.4% | 5.9% | 7.4%
Overall (EL+BL) | 1.7% | 4.5% | 5.0% | 1.5% | 2.9% | 3.4% | 2.1% | 5.6% | 6.8%
Overall (EL) | 3.0% | 8.0% | 8.7% | 3.4% | 7.0% | 7.6% | 4.2% | 10.1% | 12.0%
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.1% | 1.4% | 1.6% |  |  |  | 0.1% | 1.7% | 2.2%
Class B | 0.1% | 2.1% | 2.3% | -0.3% | 0.3% | 0.6% | -0.1% | 1.9% | 2.9%
Overall (EL+BL) | 0.1% | 1.9% | 2.1% | -0.3% | 0.3% | 0.6% | 0.0% | 1.8% | 2.7%
Overall (EL) | 0.1% | 3.2% | 3.5% | -1.3% | 0.6% | 0.4% | -0.1% | 3.1% | 4.3%

## Slide 6: Closing remarks
BD-rate for test case RA 2x, RA 1.5x and RA SNR are reduced by 1.6%, 1.8% and 2.1%, by applying the proposed bug fix.
Suggest adopting the proposed encoder bug fix.