## Slide 1: CE1: Test 1 - Rectangular transform units for 4:2:2 (and AHG7 benchmarks)
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-L0182

## Slide 2: Introduction
CE1 has been designed to explore the effectiveness of different block structures for 4:2:2.
Test 1 explores rectangular TUs:
  Rectangular TUs are currently used in the HEVC RExt model.
  There is no other HEVC software version to compare against.
  For this reason, comparisons have been made against other codecs, for information only.

## Slide 3: Rectangular TUs
Compared to 4:2:0, 4:2:2 processing differs in RExt: as follows:
  A TU is a rectangular sample array instead of square (but covers the same image region)
  The intra-angle-prediction values ‘intraPredAngle’ and ‘invAngle’ are doubled/halved.
    This accounts for the change in sample aspect ratio (and would also be needed for square TUs).
  The intra-planar-prediction applies a different shift to the top row
    This accounts for the aspect ratio of the TU.
  The QP is incremented by 3 prior to quantisation/dequantisation
    This accounts for a √2 factor from the 2D transforms.
  Nx2N scaling lists are formed from horizontally sub-sampled 2Nx2N scaling lists.

## Slide 4: Comparison against AVC

## Slide 5: Comparison against SStP and AVC

## Slide 6: Bit distribution

## Slide 7: Conclusion
HEVC is offering 16%, 18% and 13% gain over AVC at HEHT operating points for 4:2:2, 4:4:4 and GBR sequences (with chroma averaging at 12%, 15% and 10%).
  It is hoped that the Range Extension model can further increase these gains.
HEVC is typically only 5% better than AVC at SStP operating points.
  A spreadsheet has been provided to explore the performance at different operating points.
A spreadsheet indicating the distribution of bits has been provided, to show the importance of chroma .
  Unsurprisingly, chroma is:
    More important for lower QPs than higher QPs
    ~2x more important for 4:4:4 than 4:2:2
    ~2x more important for 4:2:2 than 4:2:0
    For GBR 4:4:4, chroma (B+R) is more than double the bits of luma (G)!