## Slide 1: Non-TE4: Switchable De-ringing Filter for Inter-layer Prediction
Zhan Ma, Felix Fernandes
Samsung Electronics

## Slide 2: Proposal
Switchable de-ringing filter (SDRF) for intraBL
  -0.9%/-0.4% for AI HEVC 2x/1.5x
  -0.9%/-0.3%/-0.6% for RA HEVC 2x/1.5x/SNR
  -1.2%/-0.8%/-1.0% for LDP HEVC 2x/1.5x/SNR
Switchable de-ring filter (SDRF) for both intraBL and intraBLSkip
  intraBLSkip signaling re-uses JCTVC-L0230 (TI)
  -1.2%/-0.7% for AI HEVC 2x/1.5x
  -1.1%/-0.6%/-0.5% for RA HEVC 2x/1.5x/SNR
  -1.5%/-1.3%/-1.2% for LDP HEVC 2x/1.5x/SNR

## Slide 3: Motivation
Ringing artifacts are observed
  Re-sampling error
  Quantization error
Proposed solution is reducing the ringing artifacts so as to improve the up-sampled base layer reconstruction and inter-layer coding efficiency

## Slide 4: Technical Description
3x3 template
 | Luma | Chroma
2x | W_luma_2x = {{w(-4), w(-3), w(-2)}, {{ 3, 4, 3 }, {w(-1), w( 0), w( 1)}, = { 4, 5, 4 }, {w( 2), w( 3), w( 4)}} { 3, 4, 3 }} | W_chroma_2x = {{w(-4), w(-3), w(-2)}, {{1 , 2 , 1 }, {w(-1), w( 0), w( 1)}, = {2 , 4 , 2 }, {w( 2), w( 3), w( 4)}} {1 , 2 , 1 }}
1.5x/SNR | W_luma_15x = {{w(-4), w(-3), w(-2)}, {{ 1, 4, 1 }, {w(-1), w( 0), w( 1)}, = { 4, 12, 4 }, {w( 2), w( 3), w( 4)}} { 1, 4, 1 }} | W_chroma_15x = {{w(-4), w(-3), w(-2)}, {{1 , 2 , 1 }, {w(-1), w( 0), w( 1)}, = {2 , 16 , 2 }, {w( 2), w( 3), w( 4)}} {1 , 2 , 1 }}
g_luma[65] = { 64, 61, 54, 44, 33, 23, 15, 9, 5, 2, 1, 0, 0, … … , 0 };
g_chroma[33] = { 8, 4, 2, 1, 0, 0, … … 0 };

## Slide 5: CU level switchable de-ringing filter (SDRF)
A new flag drfFlag is introduced
  When the block is coded using intraBL or intraBL skip, this drfFlag is encoded to indicate whether this block is using upsampled BL or filtered up-sampled BL.

## Slide 6: Simulation Results – SDRF for intraBL
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Overall (EL+BL) | -0.9% | -1.0% | -1.1% | -0.4% | -0.4% | -0.4% |  |  | 
Overall (EL) | -1.9% | -2.1% | -2.3% | -1.0% | -1.2% | -1.1% |  |  | 
Enc Time[%] | 119.3% |  |  | 117.0% |  |  |  |  | 
Dec Time[%] | 115.1% |  |  | 111.6% |  |  |  |  | 
Enc Mem[%] | 102.9% |  |  | 104.1% |  |  |  |  | 
BL Match | Matched |  |  | Matched |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall (EL+BL) | -0.9% | -0.2% | -0.3% | -0.3% | 0.2% | 0.2% | -0.6% | 0.1% | 0.3%
Overall (EL) | -1.8% | -0.6% | -0.7% | -0.7% | 0.2% | 0.3% | -1.0% | 0.1% | 0.3%
Enc Time[%] | 106.3% |  |  | 104.9% |  |  | 103.9% |  | 
Dec Time[%] | 105.7% |  |  | 104.8% |  |  | 106.5% |  | 
Enc Mem[%] | 103.3% |  |  | 104.5% |  |  | 112.3% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall (EL+BL) | -1.2% | -0.7% | -0.6% | -0.8% | -0.1% | 0.0% | -1.0% | -0.2% | 0.0%
Overall (EL) | -2.3% | -1.4% | -1.2% | -2.2% | -0.5% | -0.2% | -1.9% | -0.7% | -0.2%
Enc Time[%] | 106.1% |  |  | 104.8% |  |  | 104.0% |  | 
Dec Time[%] | 106.4% |  |  | 107.8% |  |  | 104.9% |  | 
Enc Mem[%] | 103.3% |  |  | 104.4% |  |  | 112.5% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 

## Slide 7: Simulation Results – SDRF for intraBL + IntraBLSkip
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Overall (EL+BL) | -1.2% | -0.7% | -0.8% | -0.7% | 0.4% | 0.1% |  |  | 
Overall (EL) | -2.5% | -1.6% | -1.8% | -2.4% | 1.7% | 0.9% |  |  | 
Enc Time[%] | 115.5% |  |  | 112.6% |  |  |  |  | 
Dec Time[%] | 102.3% |  |  | 95.2% |  |  |  |  | 
Enc Mem[%] | 103.2% |  |  | 103.8% |  |  |  |  | 
BL Match | Matched |  |  | Matched |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall (EL+BL) | -1.1% | 0.1% | 0.1% | -0.6% | 0.9% | 0.9% | -0.5% | 0.9% | 1.1%
Overall (EL) | -2.2% | -0.1% | -0.1% | -1.8% | 2.3% | 1.7% | -1.1% | 1.4% | 1.7%
Enc Time[%] | 100.6% |  |  | 96.2% |  |  | 100.5% |  | 
Dec Time[%] | 100.1% |  |  | 96.4% |  |  | 100.8% |  | 
Enc Mem[%] | 103.3% |  |  | 104.3% |  |  | 112.4% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Overall (EL+BL) | -1.5% | -0.3% | -0.2% | -1.3% | 0.9% | 0.8% | -1.2% | 0.4% | 0.7%
Overall (EL) | -2.9% | -0.7% | -0.6% | -4.0% | 2.3% | 1.9% | -2.3% | 0.2% | 0.6%
Enc Time[%] | 101.7% |  |  | 96.5% |  |  | 101.5% |  | 
Dec Time[%] | 101.3% |  |  | 99.9% |  |  | 101.5% |  | 
Enc Mem[%] | 103.4% |  |  | 104.5% |  |  | 112.4% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 

## Slide 8: Conclusion
Suggest to include SDRF into inter-layer filtering CE for further study.
Q & A.