## Slide 1: JCTVC-L0206 TE5: Using base layer MV in Merge and AMVP modes (test 5.2.2)
Vadim Seregin, Jianle Chen, Marta Karczewicz

## Slide 2: Solution 1
Merge
  BL MV is inserted as the first candidate, pruning is done for each spatial candidates with co-located BL MV
  HEVC pruning kept unchanged
AMVP
  BL MV is inserted after TMVP
Merge list (total 5)
Base layer MV
Left
Above
Above right
Left bottom (if candNum<4)
Above left (if candNum<4)
TMVP
Combined candidates
Zero candidates
AMVP list (total 2)
Left
Above
TMVP
Base layer MV
Zero candidates

## Slide 3: Solution 2
Base layer MV is derived from the center
Base layer MV is inserted as a first candidate into the completed candidate list
  Advantage: Merge/AMVP candidates list generation of HEVC is kept unchanged

## Slide 4: Experimental results (Merge)

## Slide 5: Experimental results
Uncompressed base layer
Compressed base layer
Test |  | RA |  |  | LD-P |  |  | Average
 |  | 2x | 1.5x | SNR | 2x | 1.5x | SNR | 
Solution 1 | Merge | -2.28 | -2.36 | -2.49 | -1.32 | -1.28 | -2.03 | -1.96
 | AMVP | -1.49 | -1.48 | -1.54 | -1.01 | -0.83 | -1.05 | -1.23
 | Merge+AMVP | -2.42 | -2.49 | -2.61 | -1.44 | -1.35 | -2.11 | -2.07
Solution 2 | Merge | -1.99 | -2.16 | -2.22 | -1.04 | -1.06 | -1.76 | -1.71
 | AMVP | -1.47 | -1.47 | -1.53 | -1.00 | -0.82 | -1.06 | -1.23
 | Merge+AMVP | -2.11 | -2.28 | -2.32 | -1.16 | -1.14 | -1.81 | -1.80
Test |  | RA |  |  | LD-P |  |  | Average
 |  | 2x | 1.5x | SNR | 2x | 1.5x | SNR | 
Solution 1 | Merge | -1.16 | -1.83 | -2.01 | -0.37 | -0.83 | -1.43 | -1.27
 | AMVP | -0.83 | -1.19 | -1.32 | -0.47 | -0.63 | -0.81 | -0.88
 | Merge+AMVP | -1.17 | -1.93 | -2.11 | -0.39 | -0.87 | -1.46 | -1.32
Solution 2 | Merge | -0.94 | -1.63 | -1.74 | -0.13 | -0.60 | -1.13 | -1.03
 | AMVP | -0.80 | -1.18 | -1.31 | -0.46 | -0.63 | -0.81 | -0.87
 | Merge+AMVP | -0.88 | -1.72 | -1.80 | -0.11 | -0.65 | -1.15 | -1.05