## Slide 1: L0209: On Implicit Signaling of Scalability Dimension Identifiers
Sachin Deshpande
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Introduction
In current video parameter set extension design dimension Id values (dimension_id[i][j]) for each scalability dimension of each layer are explicitly listed and transmitted.
It is asserted that in many typical situations the dimension Id values for each scalability dimension for each layer can be derived based on signaling a parameter about each scalability dimension.
This document proposes such a method for implicit signaling of scalability dimension identifiers in video parameter set extension.
It is asserted that the main advantages of the proposed approach are that:
  It allows a simple signalling mechanism which does not need to explicitly list all the scalability dimension identifiers for each layer_id.
  It requires fewer bits to signal when the dimension IDs are assigned according to a typical manner providing full scalability on various scalability dimensions.
  It supports explicit signalling of scalability dimension identifiers for each layer_id if required by some application.
Two syntax variants are proposed (Variant A, Variant B)
<number>
Notes: <number>

## Slide 3: Proposal Variant A
vps_implicit_dimension_ids_flag with a value of 1 specifies that the explicit listing of dimension_id[i][j] values for various scalability dimensions is not signaled and the dimension id[i][j] values are inferred. vps_implicit_dimension_ids_flag with a value of 0 specifies that the explicit listing of dimension_id[i][j] values for various scalability dimensions is signaled.
max_dimension_id_minus1[i] specifies the maximum value of the dimension_id for the scalability dimension i.
<number>
Notes: <number>

## Slide 4: Proposal Variant A
When dimension_id values are implicitly signaled they are inferred as DimId[i][j] as described by the code below
<number>
int Id[]={0,0,0,…,0};
for(i=0;i<=vps_max_layers_minus1;i++)
{
for(j=0;j<NumScalabilityTypes;j++)
{
DimId[i][j]= Id[j];
}
Id[NumScalabilityTypes-1]= Id[NumScalabilityTypes-1]+1;
for(k= NumScalabilityTypes-1;k>=0;k--)
{
if(Id[k]==(max_dimension_id_minus1[k]+1))
{
Id[k]=0;
Id[k-1]= Id[k-1]+1;
}
}
}
Notes: <number>

## Slide 5: Proposal Variant B
Variant B is similar to variant A except that the syntax elements vps_nuh_layer_id_present_flag and layer_id_in_nuh[ i ] are also not signaled when implicitly signaling scalability dimension identifiers.
Semantics and decoding process for Variant B is same as that for variant A except that additionally the value of NUH layer id is inferred to be equal to the entry index i of the loop for (i=0; i<=vps_max_layers_minus1; i++).
<number>
Notes: <number>

## Slide 6: Conclusion
This document proposes implicit signaling of scalability dimension identifiers in video parameter set extension.
Two syntax variants are proposed.
We propose to adopt one of the proposed approaches to VPS extension design.
<number>