## Slide 1: L0210: On Layer Dependency Signaling
Sachin Deshpande
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Introduction
In current video parameter set extension design layer dependency information is signaled using fixed length syntax elements which specify:
  The number of layers each layer directly depends on - num_direct_ref_layers[ i ] coded as u(6)
  A list of these reference layer id values – a list of size num_direct_ref_layers[ i ] signaling ref_layer_id[ i ][ j ] values coded as u(6).
This document proposes a new syntax for signaling layer dependency information. It is asserted that the proposed syntax is simpler and bit efficient.
It is asserted that the main advantages of the proposed approach are that:
  It allow easy parsing of layer dependency information to detect which layers are independent and which layers are dependent on other layers.
  It requires fewer bits to signal in case a layer is independent.
Four different syntax variants are proposed.
<number>
Notes: <number>

## Slide 3: Proposal – Summary of Variants
Variant 1: Signals a mask of layer dependency information for all layer ids. Then it signals a list of reference layer id values only for layer ids which have reference layers that they depend on.
Variant 2: Signals a 1 bit flag for each layer indicating if the layer is dependent or independent. Then for the dependent layers it signals a list of reference layer id values that they depend on.
Variant 3: A two-dimensional array of 0 or 1 values is sent. Each row in the array corresponds to one layer id value. Each 0 or 1 mask pattern in a row signals which layers the particular layer depends upon.
Variant 4: Is a combination of variant 1 and variant 3. A mask of layer dependency information for all layer ids is signaled. Then only for the dependent layers a mask pattern of 0 or 1 values signaling which layers the dependent layer depends on is signaled.
<number>
Notes: <number>

## Slide 4: Proposal Variant 1
layer_dependency_information_pattern signals a pattern of 0 and 1 bits with the length equal to vps_max_layers_minus1.
A value of 0 for i’th bit of layer_dependency_information_pattern indicates that the layer with layer_id (i+1) is an independent layer. A value of 1 for i’th bit of layer_dependency_information_pattern indicates that the layer with layer_id (i+1) is a dependent layer which depends on one or more of other layers.
The value of NumDepLayers is equal to the sum of number of bits in the layer_dependency_information_pattern having value of 1.
<number>
Variant 1: Signals a mask of layer dependency information for all layer ids. Then it signals a list of reference layer id values only for layer ids which have reference layers that they depend on.
Notes: <number>

## Slide 5: Proposal Variant 2
layer_dependency_flag[i] signals if a layer depends on other layers . A value of 0 for the flag indicates that the layer with layer_id i is an independent layer. A value of 1 for i’th bit indicates that the layer with layer_id i is a dependent layer.
<number>
Variant 2: Signals a 1 bit flag for each layer indicating if the layer is dependent or independent. Then for the dependent layers it signals a list of reference layer id values that they depend on.
Notes: <number>

## Slide 6: Proposal Variant 3
layer_dependency_map[i] signals a pattern of 0 and 1 bits with the length equal to vps_max_layers_minus1. A value of 0 for k’th bit of layer_dependency_map[i] indicates that the layer i does not depend on layer with layer_id (k+1). A value of 1 for k’th bit of layer_dependency_map[i] indicates that the layer i depends on layer with layer_id (k+1).
<number>
Variant 3: A two-dimensional array of 0 or 1 values is sent. Each row in the array corresponds to one layer id value. Each 0 or 1 mask pattern in a row signals which layers the particular layer depends upon.
Notes: <number>

## Slide 7: Proposal Variant 4
layer_dependency_information_pattern
has the same semantics as in variant 1
layer_dependency_map[i] has the same semantics as in variant 3.
The value of NumDepLayers is equal to the sum of number of bits in the layer_dependency_information_pattern having value of 1.
Thus in variant 4 the layer_dependency_map is signaled only for the dependent layers.
<number>
Variant 4: Is a combination of variant 1 and variant 3. A mask of layer dependency information for all layer ids is signaled. Then only for the dependent layers a mask pattern of 0 or 1 values signaling which layers the dependent layer depends on is signaled.
Notes: <number>

## Slide 8: Conclusion
This document proposes layer dependency signaling in video parameter set extension.
Four syntax variants are proposed.
We propose to adopt one of the proposed approaches to VPS extension design. Our preference is to adopt variant 4.
<number>